## Slide 1: Consolidated Views on Rel-19
ETRI, SK Telecom, KT, LG Uplus

## Slide 2: General Views on Rel-19
Rel-19 roles & general considerations
  Rel-19 should be focused on completing specifications of 5G-Advanced (Rel-18).
  Rel-19 should be prepared for and be linked to 6G, to ensure a smooth transition and continuity of network services.
  The number of items should be limited based on the maximum TU budget for WGs.
Commercial deployment issues and consideration for 5GS enhancements
  Enhancement of network slicing (e.g., optimization of RAN-Core slicing, slicing failure recovery, etc.)
  Network/service openness (Open network APIs - CAPIF, CAMARA (GSMA), Open gateway (GSMA), etc.)
  Network management for CAPEX/OPEX efficiency (e.g., network optimization, failure recovery, energy efficiency, etc.)
Expected to be considered in 6G and expanding the network portfolio
  Supporting new services (e.g., sensing/Ambient IoT, Integrated AI and communication., etc.)
  Expanding the network to include TN/NTN, 3GPP/Non-3GPP, etc.
  Supporting network softwarization, cloud-native, and energy-aware environment

## Slide 3: Focus Items and Prioritization
AI/ML
UPEAS - Ph2
Robust Core
Metaverse/XR
Energy Efficiency
5G Satellite - Ph3
VMR - Ph2
Ambient IoT

## Slide 4: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1. | AI/ML related (See slide 6 for more details) | Key Work Tasks - Study the possible architectural and functional extensions for cross-domain AI/ML support (e.g., UE, RAN, Core, applications, etc.) Study the possible architectural and functional extensions to support AI/ML from the perspective of LCM (Life-cycle management) Study how to assist 5GS/5GC to make operational decision (e.g., recommendation) | - | SA2 | Yes | TBD
2. | UPEAS - Ph2 (See slide 7 for more details) | Key Work Tasks - Study on enhancement of UPF event exposure to support more features to NFs Study on modularized UPF services taking advantage of cloud-native, programmability, and flexible deployment | - | SA2 | No | TBD
3. | Robust Core (See slide 8 for more details) | Key Work Tasks - 1. Protecting from signal storm and abnormal network functions (prediction, mitigation, recommendation, etc.) | - | SA2 | No | TBD
4. | Metaverse/XR (See slide 9 for more details) | Key Work Tasks - Study the functional enhancement to support more features including coordinated input/output data from multiple users in a single location Study enhancements on PDU set handling Study enhancements on QoS handling for Metaverse service | Yes, TR 22.856 [FS_Metaverse] | SA2 | Yes | TBD

## Slide 5: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5. | Energy Efficiency (See slide 10 for more details) | Key Work Tasks - 5G to adapt energy-aware procedures, e.g., NF to operate based on energy consumption to meet various end-user’s service requirements. (e.g., UE registration, NF selection, etc) | Yes, TR 22.882-100 [FS_EnergyServ] | SA2 | No | TBD
6. | 5G Satellite - Ph3 (See slide 11 for more details) | Key Work Tasks - NTN-based traffic distribution and/or aggregation across two 3GPP access links UE-Satellite-UE communication without going through the ground network | Yes, TR 22.865 [FS_5GSAT_Ph3] | SA2 | Yes | SA3 for security, SA5 for charging, SA6 for application enablement
7. | VMR enhancements (See slide 12 for more details) | Key Work Tasks - Support of height measurement event for m-IAB/VMR mounted in aerial vehicles Support for NTN backhaul, to provide service on aircrafts, UAMs and other areas without TN coverage EPC connectivity to m-IAB/VMR for EN-DC support (depending on the outcome of R19 m-IAB where standalone is being specified and EN-DC is down prioritized) | Yes, TR 22.261 [FS_VMR] | SA2 | Yes | SA5 for authorization
8. | Ambient IoT (See slide 13 for more details) | Key Work Tasks - Study architecture requirements to support Ambient IoT service within 5GS Study registration and connection management for Ambient IoT devices (e.g., security aspects, QoS and traffic management, etc.) Study how to perform positioning for Ambient IoT device Support of device life cycle management | Yes, TR 22.840 [FS_Ambient IoT] | SA2 | Yes | SA3 for security, SA5 for charging

## Slide 6: Architectural enhancements for 5G AI/ML
New potential study issues
  Study the possible architectural and functional extensions for cross-domain AI/ML support (e.g., UE, RAN, Core, applications, etc.)
  Study the possible architectural and functional extensions to support AI/ML from the perspective of LCM (e.g., data collection, model training, model delivery, model inference, model update, etc.)
  Study how to assist 5GS/5GC to make operational decision (e.g., recommendation)
  Study how to evolve from network data analytics to network operational recommendation
<Cross-Domain (UE-RAN-Core-Applications) AI/ML support >
< Analytics enhancements - from data intelligence to operational intelligence>

## Slide 7: Architectural enhancements for UPF
Discussed in Rel-18
  Supporting data collection directly from UPF to NWDAF [Rel-18]
  Supporting NAT information exposure from UPF to NEF [Rel-18]
  Supporting TSN management information exposure from UPF to TSN AF/TSCTSF [Rel-18]
Items to be discussed in Rel-19
  Enhancement of UPF event exposure to support more features to NFs
    NWDAF, AF/NEF, CHF, TSCTSF, etc.
    Data exposure (e.g. sensing data)
  Modularized UPF services taking advantage of cloud-native, programmability, and flexible deployment
<Architectural enhancements for UPF>

## Slide 8: Robust Core
The study is aiming at identifying and analyzing existing and new methods for 5GC to support protecting against signal storm and related misbehaving network functions.
With the Core network being central to 5G System (5GS), making a robust and resilient Core is more complicated and challenging especially with increasing number NFs. 5GC needs to perform correctly and accurately all the time, including handling of abnormal NFs that could cause unintended malicious traffic. It should be able to prevent against (un)expected scenarios such as signal storm period and related misbehaving NFs.
SA2#157 https://portal.3gpp.org/ngppapp/CreateTDoc.aspx?mode=view&contributionId=1442135

## Slide 9: Architectural enhancements of Metaverse and XR
Items newly discussed in SA1 [FS_Metaverse] Rel-19
  Efficient and scalable support of XRM coordination among a large number of users in a single location
    Management of multiple users information and their performance in a single location
    Exposure of multiple users information in a single location including performance parameters
  Enhancement of FS_XRM
  Enhancements on PDU set handling
  Enhancements on QoS handling for XRM service
<Concept of 5GS Metaverse service to multiple users in locations>

## Slide 10: NF Energy-related operation
Operators are unaware of their own individual NFs’ power consumption or requirements, and how they behave with 5GS procedures for end-to-end service quality.
5G system shall be able to provide a mechanism for one or more network functions to operate based on energy consumption to meet various end-user’s service requirements. (e.g., UE registration, NF selection, etc)
5G system shall be able to provide means to coordinate the operation of individual network functions to target optimization of energy consumption within the 5G network.
Use-case in the TR : https://www.3gpp.org/ftp/tsg_sa/WG1_Serv/TSGS1_102_Berlin/Inbox/post_meeting_draft_TRs/Draft_S1-231341_TR%2022882-110_rm_v2.docx

## Slide 11: Enhancement of Satellite Access and Backhaul
Items newly discussed in SA1 Rel-19 [FS_DualSteer & FS_5GSAT_Ph3]
  NTN-based traffic distribution and/or aggregation across two 3GPP access links
    Multiple connectivity over NTN-based NG-RAN and cellular NG-RAN
    Dual steering over two 3GPP networks(satellite or UAV with gNB on board)
  UE-Satellite-UE communication without going through the ground network
    Communication between UEs under the coverage of the same satellite or satellite constellation
    Service continuity between satellites and between satellite and terrestrial network
<Service continuity for UE-Satellite-UE communication without going through the ground network>
<Multiple connectivity involving transparent NTN-based NG-RAN and cellular NG-RAN(same PLMN)>

## Slide 12: VMR (Vehicle-Mounted Relay) enhancements
SA R19: SA2 VMR_Ph2
In R18, scope on VMR was limited to 5G standalone m-IAB. R19 should include to support other architecture options
WT#1.1: Support of height measurement event for m-IAB/VMR mounted in aerial vehicles
WT#1.2: Support for NTN backhaul, to provide service on aircrafts, UAMs and other areas without TN coverage
WT#1.3: EPC connectivity to m-IAB/VMR for EN-DC support (depending on the outcome of R19 m-IAB where standalone is being specified and EN-DC is down prioritized)
NTN
gNB/eNB

## Slide 13: Ambient IoT
Items newly discussed in SA1 [FS_Ambient IoT] Rel-19 and RAN Plenary [FS_Ambient_IoT_RAN] Rel-18
  Ambient IoT device is powered by energy harvesting, being either battery-less or with limited energy storage capability
  Supporting ultra-low power consumption and ultra-low complexity IoT devices under extreme environmental conditions
  Supporting the Ambient IoT services, considering both active tag and passive tag
Items to be discussed in Rel-19
  Architecture requirements to support Ambient IoT service within 5GS
  Registration and Connection Management for Ambient IoT devices
<Use-case of Ambient IoT - Smart Logistics at shipping port>

## Slide 14: Focus Items - Summary
Architectural enhancements for 5G AI/ML
AI/ML integration
Enhancement of satellite access and backhaul
VMR (Vehicle-Mounted Relay) enhancements
Ambient IoT
Verticals & new services
Preparatory works for 6G should be also considered (not limited to Rel-19)
  Integration of sensing and communication
  Integration of computing, routing, and storage capabilities
  RAN-Core convergence: Evolution of SBA
  Highly reliable mobile networks based on Digital Twin Network
  Network of sub-networks
Architectural enhancements for UPF (UPEAS phase-2)
Robust Core
Metaverse / XR
Energy efficiency
UPF & architecture enhancement