## Slide 1: KPN’s view on SA Rel-19
Jos Adema
SA delegate, KPN

## Slide 2: KPN priorities and focus areas
Continuation of existing business in a sustainable way
  Environmental sustainability: KPN's goal is zero carbon emission in 2040
Future ready network
  Legacy solutions to be phased out
  Inefficient solutions to be improved
  Establish basic solutions that enable new business opportunities
Supporting new business opportunities
  New business opportunities facilitate vertical markets (e.g. inventory tracking, smart farming)
  New business opportunities indoor e.g. in the office
  These use cases impose requirements that cannot be fulfilled with current generation cellular networks
Regulatory
  Operators are obliged to comply to the regulatory requirements

## Slide 3: Overall View on Rel-19 SA2 Content (1)
S.NO. | Title | Brief Description and Key Objectives | KPN focus area | Related Stage-1 Study/Work Item | RAN dependencies
1. | Energy Efficiency (FS_EnergyServ) | Leverage Energy Saving as a Service, following the requirements from SA1 EnergyServ. KPN as one of the Mobile operators with target of Net Zero for 2040 supports all Energy Efficiency related items. | Continuation of existing business in a sustainable way | Yes, TR11.881 | Yes
2. | Femto (HgNB) (see slide 6) | High bandwidth and throughput with 5G are required indoors to enable new immersive applications such as AR/VR/MR, etc. While a lot of capacity is required indoor, outdoor to indoor coverage with 5G mid and high-bands is limited. 5G Femto offers a cost-effective way to improve 5G indoor coverage, and offload macro gNB network traffic. 5G Femto can use higher frequency bands, allowing premises owners to deploy HgNB on their own, and leading to efficient and effective usage of higher frequency spectrum. | Future ready network | Yes, TS 22.261 clause 6.38 | Yes
3. | Robust and Resilient Core (FS_RRC) | Preventing, detecting and protection against signaling storms is an issue in the 2G/3G/4G environment especially for IoT and for 5GC this might be even worse due to the increasing number of network functions. Mechanisms and measures for improving resilience are important for KPN because we already encountered escalations to the highest management | Future ready network | No | Don’t know
4. | UE Policy (FS_eUEPO_Ph2) | UE policies provided by the network provides a way of operator control of UE functionality. Optimizations are needed for how UE policies can be requested and provisioned. Study how to optimize the UE Policy provisioning procedures to ensure that the UE policy provisioned to the UE are enforceable. Study whether new triggers are needed for UE Policy provisioning procedure and whether procedures other than initial Registration can be used to provision the UE Policy. | Future ready network | No | No
5. | Harmonizing 5G IMS with SBA (FS_H5GIMS_SBA) | Harmonizing 5G IMS with SBA will lead mobile networks to smooth 5GC - IMS integration with less interoperability issues. Same discovery and Selection approach can be used for both 5GC and IMS. It can also help with a harmonized subscription database to follow the SBA subscription formats. For the operators that uses SCP in their 5GC networks, this WID can help to use same approach for packet forwarding in 5G IMS network as well. | Future ready network | No | No

## Slide 4: Overall View on Rel-19 SA2 Content (2)
S.NO. | Title | Brief Description and Key Objectives | KPN focus area | Related Stage-1 Study/Work Item | RAN dependencies
6. | Ambient IoT (FS_Ambient IoT_SA2; see slide 5) | Ambient IoT is a very promising technology for logistics and for large scale sensing (e.g. in agriculture). Two sectors that are very prominent in The Netherlands and hence important to KPN. Example use cases: Logistics tracking and tracing from factory to warehouse to destination Sensing of e.g. nutrients and water level in a greenhouse or health of cows. Ambient IoT not only needs “low complexity” devices. Also the network needs to be optimized to take into account the characteristics of Ambient IoT. | Supporting new business opportunities | Yes, TR 22.840 | Yes, major
7. | MVPN (FS_ MVPN) | Mobile VPN helps with connecting non-5G user equipment to 5G network. There are few legacy solutions for private networks and the LAN networks behind them but each of them has their own complexity and concern. With a unique way of implementation (MVPN) for UE identity and accessing to private LAN networks, KPN or other operators can solve different issues in enterprise sections. | Supporting new business opportunities | No | Yes
8. | PINE/eUUI5 (FS_eUUI5) | Defining a unique end user identity format and connect it to subscription will help operators in Enterprise, MVPN and Personal IoT implementations. With this feature, operators can have end user / application / device based policies like parental control or charging. | Supporting new business opportunities | No | Don’t know
9. | Enhancing Emergency Services when Zero CS network coverage (FS_enhEM0CS) | Investigate and identify Circuit Switched (CS) related activities those that can be removed from relevant processes or signaling procedures when a network no longer supports a CS network for voice or Emergency voice services. KPN is supportive to all improvements in emergency voice services. | Regulatory/future ready network | No | Don’t know
10. | Roaming Value Added Services | Roaming services like welcome SMS and SOR are a necessity for operators and should be well specified for 5G to be flexible e.g. choice of outsourcing or do it yourself | Regulatory/future ready network | Yes, TS22.261 | No

## Slide 5: Ambient IoT
      Ambient IoT is a very promising technology for logistics and for large scale sensing (e.g. in agriculture). Two sectors that are very prominent in The Netherlands and hence important to KPN. Example use cases:
        Logistics tracking and tracing from factory to warehouse to destination
        Sensing of e.g. nutrients and water level in a greenhouse or health of cows
      What is important to KPN:
        A worldwide technology that can be used across different regions, countries, operators and SNPNs
        Common communication technology for RF powered devices and devices with other power sources (e.g. vibration, light, …). Third party network exposure for communication, to trigger groups of devices in a specific location, and to control where power needs to be provided
        Efficient support for different life-cycles – from a burglary sensor on a window (powered by breaking glass) with a life-time of ~50 years to a smart label on a package that is discarded when the cardboard box is discarded 2 weeks later. Study the impact on e.g. identifier usage and subscription data. It must be possible to permanently disable devices by the network
        Optimised procedures. E.g. performing a complete initial registration for a device that only sends 200 bits of data before registering on a different network is not efficient.
        Not only focus on device costs e.g. a 2 Euro device but with a 10 Euro/month subscription does not work

## Slide 6: Femto
      Most data is generated indoors!
        Mobile data usage patterns show that a lot of mobile data is generated not when people are on the road, but when people are indoors.
        Ever higher video resolution and new high data rate services like AR/VR will further increase indoor usage. These services are mostly used indoor and significantly contribute to overall capacity requirement.
        Outdoor to indoor coverage is increasingly difficult e.g. because of coated window panes.
        Femto-cells provide an easy solution to provide indoor coverage, e.g. in small offices, shops, etc. The premises owners can install their own networks using higher frequency bands; offloading macro gNBs, and increasing use of lesser used frequency bands
        Use of licensed spectrum allows for more operator control of the service quality
        End to end security and QoS from UE to network implies also security and QoS control of connection to femtocell
Doctors waiting room