## Slide 1: OQ Technology's views on NTN service and architecture evolution in Rel-19
OQ Technology

## Slide 2: OQTEC’s Prioritized Rel-19 Topics
Store and Forward
GNSS Independent operation
5GC supporting IoT NTN
UE-Sat-UE Communication
Quality of Service management for NTN systems
Regenerative Payload

## Slide 3: 1. Regenerative payload
Regenerative payload generic architecture study:
  Mminimum necessary set of 3GPP core network functions to be embedded in the satellite.
  Core network impacts on interfaces, protocols of having lightweight embedded 3GPP functions.
  UEs Authentication.
  Goal is to support:
    Delay sensitive and/or delay tolerant service;
    Reduced user and/or control plane latency;
    Unicast, multicast and broadcast;
    Edge computing on board;
  NOTE: ISL assumed but not mandatory
  FOCUS: Option1(DU onboard, CU on Earth); Option2: (Fully regenerative with/without ISL);

## Slide 4: 2. S&F operation
Store and Forward study impacts on interfaces & protocols:
  UEs Authentication when the feeder link is unavailable;
  Store user data on satellite when feeder link is unavailable and forward when the feeder link is available;
  Mobility and paging optimization;
  New architectural extensions for S&F operation
    Distributed satellite-ground EPC/5GC functions.
    EPC/5GC onboard;

## Slide 5: 3. UE-Sat-UE communication
Study impacts on interfaces & protocols of the UE-Sat-UE communication:
  Support UE-Sat-UE communication without going to the ground-station;
  Core network impacts on interfaces, protocols of having user-plan onboard i.e. UPF;
  UEs onboard Authentication;
  Session management;

## Slide 6: 4. GNSS independent operation
GNSS independent operation, 5GS:
  Enable UE location determination without GNSS system;
    For mobile terminals: using LTE/5G UE positioning methods;
    For stationary terminals: to be preconfigured;
  Study impacts on 5GC/EPC of UE location determination;

## Slide 7: 5. 5GC Support for IoT NTN
5GC supporting IoT NTN:
  Study specific impacts, if any, on interfaces and protocols of 5GC supporting IoT NTN
  Support integrated NTN-NR and NTN-IoT services
  NOTE: In Rel-17/Rel-18, NB-IoT is supported by EPC only;

## Slide 8: 6. QoS Management for NTN systems
Support flexible QoS management for NTN:
  Study impacts of QoS requirements for NTN systems;
    This includes HAPS, LEO, MEO and GEO platforms
    Offered services to be supported with flexible QoS requirements (i.e. propagation delay variant between different platforms impact the supported services (texting, low resolution video streaming, etc.))

## Slide 9: Summary
Topics | SA Impacts
Regenerative payload | SA2, SA3
Store and Forward operation | SA2, SA3, SA5, SA6
UE-Sat-UE communication | SA2, SA3, SA5, SA6
GNSS Independent operation | SA2, SA6
5GC support for IoT NTN | SA2
QoS Management for NTN systems | SA2, SA5