## Slide 1: Stage 2 Release 19 Priorities for Multimedia Priority Service (MPS)
Robert Streijl/Peter Monnes
Peraton Labs
Supporting Companies: CISA ECD

## Slide 2: Outline
Release 19 MPS topics
  MPS for Messaging,
  Untrusted WLAN Authorization, and
  5GC LBO Authorization

## Slide 3: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1. | MPS for Messaging | MPS priority for IMS messaging and SMS including, SMS over NAS and SMS over IP | Yes, TS 22.153 | SA2* | No | 
 |  | MPS priority for MSGin5G | Yes, TS 22.153 | SA6* | No | 
2. | Untrusted WLAN Authorization | Priority authorization for untrusted WLAN access. | Yes, TS 22.153 | SA3** | No | SA2
3. | 5GC LBO Authorization | Home network support for service authorization by the visited network during LBO roaming. | Yes, TS 22.153 | SA2** | No | 
* A study is not required
** May require a study

## Slide 4: MPS for Messaging
Description
  In addition to voice/video calls and data specified in TS 22.153, authorized MPS Service Users also need priority for messaging services in periods of network congestion during which normal commercial messaging services are degraded.
Stage 1
  TS 22.153 § 9.4 “MPS for Messaging Services”
Scope
  Support of MPS priority for SMS, IMS messaging and MSGin5G
  Initiated only by UEs with a subscription for MPS, recipient need not have an MPS subscription.
  EPC and 5GC

## Slide 5: Untrusted WLAN Authorization
Description
  Trusted access is supported per Rel-18, but there is no full solution for untrusted access.
  The 3GPP system should convey information to allow an untrusted WLAN to verify authorization for priority usage.
Stage 1
  In TS 22.153 § 10.1.1.3 “WLAN Interworking”: “For a UE with WLAN access to the EPC/5GC, the 3GPP system shall support delivery of the following to the WLAN”
    “indication of MPS for MMTEL voice/video authorization”,…
    “indication of MPS for DTS authorization”.
Scope
  Convey information to allow an untrusted WLAN to verify authorization for priority for a UE connected via an untrusted WLAN to an EPC or 5GC.

## Slide 6: 5GC LBO Authorization
Description
  Home network support for service authorization by the visited network during LBO roaming.
Stage 1
  TS 22.261: The 5G system shall support a UE with a 5G subscription roaming into a 5G Visited Mobile Network which has a roaming agreement with the UE's 5G Home Mobile Network
  TS 22.153: “The system shall support means for a Service User using a UE with an MPS subscription to initiate an MPS session (e.g., MPS for DTS) when roaming within the home country and outside the home country.”
Scope
  Specify a common solution to support 5GC LBO authorization, including support for MPS

## Slide 7: Summary
Meeting time is proposed for the following Release 19 MPS topics:
  MPS for Messaging,
  Untrusted WLAN Authorization, and
  5GC LBO Authorization