## Slide 1: vivo’s views on SA2 Rel19

## Slide 2: Criteria for prioritizing topics in Rel19
Bring outstanding improvement to 5G communication
Promising candidate feature(s) for future network and early preparation for 6G
Greatly beneficial for UE: Power Saving, QoE, etc.

## Slide 3: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | AIML for 5GS Service to enable 5GC and Air interface Intelligence (See slides 7-11 for more details, Annex slides 26-44) | This study item aims to leverage AIML technologies to enable 5GC and Air interface Intelligence (AI for Network) and/or further enhance 5GC to improve the user experience of Application layer AI/ML operation (Network for AI). Key Work Tasks includes defining: Part A (AI for Network): Architecture enhancement to support 5G Core intelligence e.g. vertical federal learning, detection/prevention of signaling storm (high) Part B (AI for Network): AI/ML alignment and convergence for Air interface and 5GC e.g. UE data collection, Model ID alignment, Lifecycle management, Model deliver to UE and AI based positioning (high & urgent, supporting R19 RAN AIML WID) Part C (Network for AI) : further 5GC enhancement to improve Application AIML e.g. UE consuming data analytics, model distribution via sidelink (may not urgent) | No | SA2 | Yes, only part B has RAN dependencies | -
2. | Integrated Sensing & Communications (See slides 13-15 for more details, Annex slides 46-52) | 5G system support for NR-based sensing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g., shape, size, orientation, speed, location, distances or relative motion between objects, etc.) using NR RF signals. Key Work Tasks includes defining: Overall architecture and function enhancement to support new sensing service. Basic functionality and E2E procedure for Sensing service exposure, Discovery and selection of the sensing entities, Authorization, Sensing control parameter generation and provisioning, related QoS/Policy enhancement. Security/privacy for sensing e.g. data privacy, user consent (coordinated with SA3) Charging for sensing (coordinated with SA5) | Yes, TR 22.837 TS 22.xxx (To be determined in SA#100) | SA2 | Yes | SA3 for security, SA5 for charging

## Slide 4: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | Ambient IOT (See slides 17-18 for more details, Annex slides 55-62) | This study item aims to leverage 5GS system to support communicating with Ambient device, which is either battery-less or with limited energy storage capability, can be maintenance free and have long life span (e.g., more than 10 years), has low complexity, small size and lower capabilities and lower power consumption than NB-IoT/eMTC devices. Key Work Tasks includes defining: 1. Architecture enhancement for Ambient IoT within 5GS 2. Manage and control a UE or a RAN node for communication with Ambient IoT device(s) directly. 3. Common and simplified protocol stack between Ambient IoT device(s). 4. Control and manage Ambient IoT device(s) based on 3rd party request and provide collected information from Ambient IoT device(s) to the 3rd party. 5. Charging information collection for Ambient IoT services. | Yes, TR 22.840 | SA2 | Yes | SA3 for security, SA5 for charging
4 | XRM phase2 (See slides 20-22 for more details) | In R18, 5GS XRM feature is defined. But due to limited time, the feature is not comprehensively defined and more XRM service and scenarios needs to be considered. SA1 Metaverse also has some related requirement. There is a necessity to continue the study of XRM in Rel-19. Key Work Tasks includes defining: PDU Set handling and PDU Set Marking enhancement, e.g. for encrypted traffic Multi-flow handling Mobility further QoS enhancement; power consumption; QoS Monitoring/QNC and exposure | Yes, TR 22.856 | SA2 | Yes | --

## Slide 5: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5 | Metaverse & MEC (See Annex slides 64-66 for more details) | 5G system support for Mobile Metaverse Service, especially for IMS 3D Avatar communication which has been concluded in SA1 TR 22.856, which require capability of producing 3D avatar media, rendering the avatar based on the body movement information (e.g. body motion or facial expression) of a human user and support a set of transcoders from and to avatar representations e.g. between text, speech and avatar encoding. Key Work Tasks includes defining: 1.IMS/NG-RTC Architecture enhancement to support diversity media service 2.Coordination/negotiation between the UE and IMS when performing avatar communication service processing, by considering the following aspects: Service type, UE capability, performance requirements, etc. 3.UE/mobile metaverse server Capability management, e.g., registration, selection, query, updating, exposure, de-registration 4.Coordination with SA4 (e.g. protocol, support of split rendering) 5.MEC enhancement e.g. computing based EAS discovery | Yes, TR 22.856 | SA2 | No | SA4, SA6
6 | 5GSAT_Ph3 | Satellite's inclusion to provide global coverage has gained more and more attention. 5G system already supports satellite access with transparent mode as NR access technology (R17), including the consideration of mobility management and power-saving enhancement regarding discontinuous coverage ( R18). R19 SA1 continues the investigation of service requirements to support new use cases. Key Work Tasks includes defining: Low latency voice call via satellite Mobility mechanism enhancement with regenerative mode satellite UE to Network relay support via satellite access Service provision for UE without GNSS | Yes, TR 22.865 | SA2 | Yes | SA4

## Slide 6
R19
FS_ALML_5GS: AIML for 5GS Service to
enable 5GC and Air Interface Intelligence
SA2/RAN

## Slide 7: Background and Motivation
The convergence of communication and AI technology made progress and are composed of two aspects:
  AI for Network: both RAN (in R18) and SA2 (in R16, R17 and R18) has studied and/or specified the AI-enabled network architecture and leverage AI/ML to enable 5GC and Air interface.
  Network for AI: SA2 in R18 also studied and/or specified how to enhance 5G core network to improve the user experience of Application layer AI/ML operation(s) e.g. by exposing 5G Core information to assist Application AIML
Based on the above, it is proposed in R19 to leverage AIML technologies to enable 5GC and Air interface Intelligence (AI for Network) and further enhance 5GC to improve the user experience of Application AI/ML operation(Network for AI):
    Part A (AI for Network) : Architecture enhancement to support 5G Core Intelligence
    Part B (AI for Network) : AI/ML alignment and convergence for Air Interface and 5GC(high & urgent, supporting R19 RAN AIML WID)
    Part C (Network for AI) : further 5GC enhancement to improve Application AIML
Notes: S2-S2-2306503

## Slide 8
Objectives for New Study on AIML for 5GS (focusing on Part B)
Part A (AI for Network): Architecture enhancement to support 5GC intelligence e.g. vertical federal learning
Part B(AI for Network): AI/ML alignment and convergence for Air interface and Core network
  Terminology alignment btw RAN and SA2 (e.g. AI/ML Mode in RAN vs ML Mode defined in SA2)
  UE data collection framework enhancement to support AI/ML use cases (coordinated with RAN, UP solution related to DCAF/EVEX UE data collection defined in R17 eNA_ph2 in SA2)
  ML Model delivery to UE(Model delivery within core network supported in R17/18 eNA without involving UE)
  Lifecycle management of AI/ML model btw RAN and SA2 (data collection, model training, model inference, model monitoring )
  SA2 and RAN Convergence for Model ID/Analytics ID defined in SA2 since R16 eNA and Model ID/feature ID studied/concluded in RAN R18
  Architecture enhancement to support AI based Positioning.
Part C (Network for AI) : further 5GC enhancement to improve Application AIML e.g. UE consuming data analytics
Note1: At the moment, in order to have a full picture, all the potential objectives are listed below as starting point and whether having a common AI SID or having two separate SIDs (e.g. AI for Network and Network for AI) is TBD and dependent on discussion outcome
Please see updated draft SID(on the top of S2-2306462 from China Mobile/vivo) including Part A/B/C
Please see updated discussion paper in details (on the top of S2-2306460 from vivo/China Mobile)

## Slide 9
xxx
AI/ML framework and terminology
  SA2 Impacts: alignment btw SA2 as AI/ML framework and terminology has been defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Lifecycle management of AI/ML model: e.g., data collection, model training, model deployment, model transfer, model inference, model monitoring, model updating, Model selection/activation/deactivation/switching/fallback, UE capability
  SA2 Impacts: alignment btw SA2 as Lifecycle management esp. data collection, model training, model inference, model monitoring defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Use case study
  CSI feedback enhancement: CSI compression, CSI prediction
  Beam management: spatial domain beam prediction, temporal domain beam prediction
  Positioning accuracy enhancements: direct AI/ML positioning, AI/ML assisted positioning
    SA2 Impacts: LCS architecture enhancement needed and related with ML Model delivery and UE data collection (positioning specific)
Network-UE collaboration levels (SA2 impacts: ML model transfer and mode ID/analytics ID concept)
  Level x: No collaboration
  Level y: Signaling-based collaboration without model transfer
  Level z: Signaling-based collaboration with model transfer
Performance evaluation methodology and KPIs
  SA2 impacts: alignment btw SA2 regarding ML Model performance monitoring in R18 eNA_ph3 KI#1 and potential R19 enhancement
RAN Progress in R18 (1/3)

## Slide 10
xxx
Model performance monitoring
  Model monitoring methods
    Monitoring based on inference accuracy, including metrics related to intermediate KPIs for AI/ML model (comparison between model output and label, e.g., NMSE, SGCS)
    Monitoring based on system performance, including metrics related to system performance KPIs (e.g., BLER, throughput)
    Monitoring based on data distribution, including Input-based and output-based
  Model monitoring KPIs, including accuracy and relevance, overhead, complexity, latency
  SA2 impacts: alignment/convergence btw SA2 regarding ML Model performance monitoring in R18 eNA-Ph3 KI#1 and potential R19 enhancement
Model transfer/delivery
  Model transfer format
    Proprietary-format
    Open-format, including parameter-only updating, both parameter and structure updating
    SA2 impacts: alignment/convergence btw SA2 regarding in R18 eNA_ph3 KI#5 Enhance trained ML Model sharing and previous work in R17 eNA_ph2 for trained ML Model sharing
  Model transfer/delivery signaling, including CP-based and UP-based
    SA2 impacts: alignment btw SA2 or enhancement in SA2 regarding UP solution DCAF/EVEX UE data collection defined in R17 eNA_ph2 in SA2
RAN Progress in R18 (2/3)

## Slide 11
xxx
Model/Functionality Identification
  Model ID concept, including logical model ID and physical model ID
  Relationship between UE feature, functionality, model, applicable conditions
  Model description information
  SA2 impacts: alignment btw SA2 or enhancement in SA2 regarding ML Model ID definition/analytics ID since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Model training types for two-sided models
  Type 1: Joint training of the two-sided model at a single side/entity, e.g., UE-sided or Network-sided
  Type 2: Joint training of the two-sided model at network side and UE side, respectively.
  Type 3: Separate training at network side and UE side, where the UE-side CSI generation part and the network-side CSI reconstruction part are trained by UE side and network side, respectively.
  SA2 impacts: alignment btw SA2 or enhancement in SA2 to support ML Model deliver to UE regarding ML Model delivery within core network ,which is already supported in R17/18 eNA but not involve UE.
vivo’s view: AI/ML alignment and convergence for Air interface and 5GC has strong dependency with R16 eNA/R17 eNA_ph2/R18 eNA_ph3 e.g. UE data collection, Model ID alignment, Lifecycle management, Model deliver.
RAN Progress in R18 (3/3)

## Slide 12
R19
Integrated Sensing & Communications
SA2/SA3/SA5/RAN

## Slide 13: ISAC – architecture enhancement
1) gNB-to-gNB, monostatic
2) gNB1-to-gNB2, bistatic
3) gNB-to-UE, Bistatic
4) UE-to-gNB, Bistatic
5) UE-to-UE, Monostatic
6) UE1-to-UE2, Bistatic
vivo’s preference: Option 1 can flexibly support different sensing modes e.g. BS and UE bistatic, BS monostatic.
Option 1a
Option 1b
Option 2
Option 3
SA1 has common consensus on that sensing mode (monostatic/bistatic) will not be specified/mentioned in the requirements. Solution-oriented description will restrict downstream workgroups, i.e., SA2 will decide the architecture for sensing
vivo’s preference: Architecture should flexibly support the different sensing modes i.e. BS and UE bistatic, BS monostatic, UE monostatic and at least support sensing mode 4), 1), 3) in R19 if time is limited
BS - oriented
BS + UE
UE oriented

## Slide 14: ISAC – Sensing Function characteristics
Option 1: SF exposes sensing data
Option 2: SF exposes “intermediate” sensing result(s)
Option 3: SF exposes sensing objective
vivo’s preference: Option 2 simplifies core network SF functionalities and secures the information to be exposed to a 3rd party.
Advantages:
Only expose the “intermediate” sensing result to avoid or alleviate data privacy
Disadvantages:
Not clear how to define “intermediate” sensing result in 3GPP
Advantages:
No data privacy issue
5GS is self-contained and can cater to different sensing services.
Disadvantages:
Complexify SF functionalities, which is service-oriented.
Advantages:
Simplified SF functionalities in 5GS, as well as leaves flexibilities to 3rd party to enrich sensing services.
Disadvantages:
Direct raw data exposure and data privacy issues
NOTE: sensing objective is service-oriented, e.g.
For intruder detection applicaitons, sensing objective can be a Boolean value (0 or 1), whether there is an intruder or not.
For health monitoring applications, sensing objective can be the respiration rate of a human, e.g. 30 times/min.
For a UAV tracking application, sensing objective can be the location+velocity of a UAV.
…
Sensing result is intermediate results that used to derive the final sensing objective.

## Slide 15: ISAC – RAN dependency analysis
Option 1: Standardized service-oriented sensing measurement
Option 2: Non-standardized sensing measurement
Option 3: Standardized + Non-standardized (Combo)
Compared to positioning service, sensing service involves diversified sensing targets (human, car, rainfall, etc.) and offers richer service types (intruder detection, health monitoring, autonomous driving etc.) than positioning service.
Different sensing service requires different sensing measurements.
Investigation of standardized sensing measurement parameters (L1/L2) e.g. in RAN1 and sensing data transfer from Sensing Rx to SF is necessary.
vivo’s preference: Option 3 offers better balance between standardization work and market
Advantage:
Standardized interface between RAN and SF, high interoperability among different manufacturers
Service-oriented authentication and authorization
Disadvantage:
Lower compatibility with new sensing services
Standard work for each sensing service
Advantage:
Less dependency on RAN 1 work
Disadvantage:
Lower interoperability regarding different RAN and core network manufactures
Advantage:
Safeguarding 5G sensing services
More flexible to new services
Disadvantage:
Lower interoperability among different manufacturers regarding new services

## Slide 16
R19
Ambient IOT
SA2/SA3/SA5RAN
  Note：Using “Reader” is for briefly presenting a UE/Base Station communicating with AIOT Devices. It doesn’t means to introduce a new terminology.

## Slide 17: Ambient IOT: Architecture
    “UE as reader”: left is reader, right connecting to 5GC in UE’s way
    “Base Station as reader”: left is reader, right connecting to 5GC in Base Station’s way
    Possible CN impact for Ambient IOT
      Enhance existing NF (preferred) or new NF
      A compatible and sufficiently extensible Arch. for different kinds of readers and AIOT devices types
      Support:
        Device Type A/B/C
        Manage and control UE reader/Base Station reader
        Use cases: Inventory/Sensor data/Control
        Group handling for massive Tag number
        licensed spectrum, Indoors & Outdoors
vivo’s view: both UE as reader(preferred) and base station as reader should be studied in R19 with support of Device Type A/B/C.
Device A | No energy storage | no independent signal generation, i.e. backscattering transmission
Device B | Has energy storage | no independent signal generation, i.e. backscattering transmission. Use of stored energy can include amplification for reflected signals
Device C | Has energy storage | has independent signal generation, i.e. active RF component for transmission

## Slide 18: Ambient IOT: Simplified and Common interface/protocol stack
    vivo’s view: Simplified protocol stack of the interface between Reader and AIOT devices for low power consumption, low complexity and low cost, e.g. simplified procedures and features for AIOT devices
    vivo’s view: Common and consolidated interface between AIOT device and reader for all topologies and device types and it is beneficial for the business. CN involvement should be compatible to both UE reader and Base Station reader
Low complexity
Low power consumption
Low cost
Ambient device:
either battery-less or with limited energy storage capability
can be maintenance free and have long life span (e.g., more than 10 years)
has lower complexity, smaller size and lower capabilities and lower power consumption than NB-IoT/eMTC devices.

## Slide 19
R19
XRM Phase2
SA2/RAN

## Slide 20: XRM phase2: Multiple Flows Handling
Scenario1
    vivo’s view: propose to study the handling of multiples flows for the listed scenarios.
Different packets within a single RTP steam may have different QoS requirement
e.g. I frame and B frame may have different reliability requirement
Scenario2
XR traffic can be carried by QUIC.
For a given service data, it may include multiple QUIC connections, and each QUIC connection may have different QoS requirement.
Scenario3
    A XR gaming may serve multiple users in different locations and it requires approximate arrival of background data to all the game Terminals and an acceptable user experience no matter where the other users are.
Scenario4
Multi-flows coordination ( SA1 Metaverse)
coordinate multiple flows delivered to/from one or more UE(s) based on latency and synchronization constraints
coordination of diverse medias transmitted to a UE

## Slide 21: XRM phase2：PDU Set handling and PDU Set marking
PDU Set identification & marking
Secured media flow
  Study the support for encrypted media traffic or traffic using proprietary protocols, including: HTTP/DASH, QUIC
  DFI is a kind of technique supporting application recognition based on traffic behavior Traffic characteristics is not impacted by encryption.
Support RTP header extension at SA4
Reduce outer header overhead between RAN and UPF
PDU Set handling (R18 leftover)
    PDU Set QoS further enhancement: PSER, PSDB, and the other PDU Set handling further enhancement, e.g. PDU Set Importance, PDU Set dependency
    UL PDU Set handling
      It is not comprehensively discussed in rel18

## Slide 22: XRM phase2: others
Mobility
Mobility is not comprehensive considered for the whole XRM feature in rel18
Further Power Saving enhancement
    Consider whether more traffic characteristics is beneficial for power saving
    Consider both UL and DL traffic
QoS Monitoring/QNC and exposure
More QoS parameter can be considered to be measured to reflect the XR traffic’s experience and support application layer adaption (e.g. coding and throughput )

## Slide 23: Summary
2nd Sensing (SA2/SA3/SA5/RAN)
Architecture enhancement
E2E signaling procedures
Data privacy
Charging
3rd Ambient IOT (SA2/SA3/SA5/RAN)
Manage the communication between Reader and AIOT devices, e.g. read, write, inventory, etc.
Architecture enhancement.
Simplified protocol stack for AIOT devices
5th Metaverse & MEC (SA2/SA4/SA6)
IMS based computing offload
MEC enhancement e.g. computing based EAS discovery
4th XR enhanced (SA2/RAN)
Mobility, multi-flows handling
PDU Set handling and Marking, e.g. Secured media flow
further QoS enhancement; power consumption; QoS Monitoring/QNC and exposure
6th Satellite (SA2/SA4)
Low latency voice call supported
Mobility mechanism enhancement with regenerative mode satellite
UE to Network relay support
1st FS_AI/ML_5GS (SA2/RAN)
Part A(AI for Network) : 5GC Intelligence (high)
Part B(AI for Network) : Alignment for Air Interface and 5GC (high & urgent)
Part C(Network for AI): 5G enhancement to improve Application AIML (may not urgent)

## Slide 24
Thank You!

## Slide 25
Annex: detail Slides for the following Topics
  FS_AI/ML_5GS
  Integrated Sensing and Communication
  Ambient IOT
  Metaverse & MEC

## Slide 26
R19
Annex: FS ALML_5GS: AIML for 5GS Service to
enable 5GC and Air Interface Intelligence
SA2/RAN

## Slide 27: Background and Motivation
The convergence of communication network and AI technology already made progress in 3GPP, which are composed of two aspects:
  AI for Network: both RAN (in R18) and SA2 (in R16, R17 and R18) has studied and/or specified the AI-enabled network architecture and leverage AI/ML to enable 5GC and Air interface.
  Network for AI: SA2 in R18 also studied and/or specified how to enhance 5G core network to improve the user experience of Application layer AI/ML operation(s) e.g. by exposing 5G Core information to assist AIML operation in Application server and UE.
Notes: S2-S2-2306503

## Slide 28: Background and Motivation
Based on the above, it is proposed in Rel-19 to leverage AIML technologies to enable 5GC and/or Air interface Intelligence (AI for Network) and further enhance 5GC to improve the user experience of Application layer AI/ML operation:
    Part A (AI for Network) : Architecture enhancement to support 5G Core Intelligence
    Part B (AI for Network) : AI/ML alignment and convergence for Air Interface and 5GC network
    Part C (Network for AI) : further 5GC enhancement to improve Application AIML
    At the moment, in order to have a full picture, all the potential objectives are listed below as a start point and whether having a common AI SID or having two separate SIDs (e.g. AI for Network and Network for AI) is TBD and dependent on discussion outcome.
    Note:
  The following slides focus on Part B: AIML convergence for Air Interface and 5GC network
  Regarding Part A, see joint discussion paper S2-2306503 from China Mobile/vivo
  Regarding Part C, also see S2-2306475(P5) from Samsung and S2-2306424 (P10~P14 ) from OPPO
Notes: S2-S2-2306503

## Slide 29
xxx
RAN Progress Summary and potential SA2 impacts
(High level)

## Slide 30
xxx
RP-221348.zip New SID on Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface is approved in RAN#96 with following objectives (high level):
  Use case study: CSI feedback enhancement, Beam management, Positioning accuracy enhancements
  AI/ML framework and terminology
  Network-UE collaboration levels
  Performance evaluation methodology and KPIs
High level progress summary and future plan
  Complete AI/ML model, terminology and description to identify common and specific characteristics for framework investigations, since main aspects of lifecycle management have been deeply discussed
  Evaluate performance benefits of AI/ML based algorithms for the agreed use cases in the final representative set, since various performance results have been provided for not fully aligned scenarios and use cases
  Assess potential specification impact, specifically for the agreed use cases in the final representative set and for a common framework
Introduction of Study on AI/ML for NR Air Interface in RA1

## Slide 31
xxx
AI/ML framework and terminology
  SA2 Impacts: alignment btw SA2 as AI/ML framework and terminology has been defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Lifecycle management of AI/ML model: e.g., data collection, model training, model deployment, model transfer, model inference, model monitoring, model updating, Model selection/activation/deactivation/switching/fallback, UE capability
  SA2 Impacts: alignment btw SA2 as Lifecycle management esp. data collection, model training, model inference, model monitoring defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Use case study
  CSI feedback enhancement: CSI compression, CSI prediction
  Beam management: spatial domain beam prediction, temporal domain beam prediction
  Positioning accuracy enhancements: direct AI/ML positioning, AI/ML assisted positioning
    SA2 Impacts: LCS architecture enhancement needed and related with ML Model delivery and UE data collection (positioning specific)
Network-UE collaboration levels (SA2 impacts: ML model transfer and mode ID/analytics ID concept)
  Level x: No collaboration
  Level y: Signaling-based collaboration without model transfer
  Level z: Signaling-based collaboration with model transfer
Performance evaluation methodology and KPIs
  SA2 impacts: alignment btw SA2 regarding ML Model performance monitoring in R18 eNA_ph3 KI#1 and potential R19 enhancement
RAN Progress (1/3)

## Slide 32
xxx
Model performance monitoring
  Model monitoring methods
    Monitoring based on inference accuracy, including metrics related to intermediate KPIs for AI/ML model (comparison between model output and label, e.g., NMSE, SGCS)
    Monitoring based on system performance, including metrics related to system performance KPIs (e.g., BLER, throughput)
    Monitoring based on data distribution, including Input-based and output-based
  Model monitoring KPIs, including accuracy and relevance, overhead, complexity, latency
  SA2 impacts: alignment/convergence btw SA2 regarding ML Model performance monitoring in R18 eNA-Ph3 KI#1 and potential R19 enhancement
Model transfer/delivery
  Model transfer format
    Proprietary-format
    Open-format, including parameter-only updating, both parameter and structure updating
    SA2 impacts: alignment/convergence btw SA2 regarding in R18 eNA_ph3 KI#5 Enhance trained ML Model sharing and previous work in R17 eNA_ph2 for trained ML Model sharing
  Model transfer/delivery signaling, including CP-based and UP-based
    SA2 impacts: alignment btw SA2 or enhancement in SA2 regarding UP solution DCAF/EVEX UE data collection defined in R17 eNA_ph2 in SA2
RAN Progress (2/3)

## Slide 33
xxx
Model/Functionality Identification
  Model ID concept, including logical model ID and physical model ID
  Relationship between UE feature, functionality, model, applicable conditions
  Model description information
  SA2 impacts: alignment btw SA2 or enhancement in SA2 regarding ML Model ID definition/analytics ID since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Model training types for two-sided models
  Type 1: Joint training of the two-sided model at a single side/entity, e.g., UE-sided or Network-sided
  Type 2: Joint training of the two-sided model at network side and UE side, respectively.
  Type 3: Separate training at network side and UE side, where the UE-side CSI generation part and the network-side CSI reconstruction part are trained by UE side and network side, respectively.
  SA2 impacts: alignment btw SA2 or enhancement in SA2 to support ML Model deliver to UE regarding ML Model delivery within core network ,which is already supported in R17/18 eNA but not involve UE.
RAN progress (3/3)

## Slide 34
xxx
RAN Progress Summary and potential SA2 impacts
(Detailed Analysis)

## Slide 35
Summary of AI/ML framework and terminology in SA2 and RAN
vivo view: Alignment/convergence btw SA2 and RAN as AI/ML framework and terminology has been defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
SA2 R18 eNA_ph3
RAN1 FS_NR_AIML_Air
Since R16, Data Collection feature permits NWDAF to retrieve data from various sources and Network Data Analytics Exposure is defined in TS 23.288.
Terminology such as ML Model ID/Analytics ID and Analytics logical function and Model Training logical function
Data collection has large impact on other modules of AI/ML framework. Collections of training data, inference data and monitoring data would have different requirements and procedures..
Terminology such as AI/ML Model, data collection, AI/ML model training, model identification, functionality identification

## Slide 36
Summary of Lifecycle management of AI/ML model in SA2 and RAN
vivo view: Alignment/convergence btw SA2 and RAN as AI/ML framework and terminology has been defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
SA2 R18 eNA_ph3 KI#1
RAN1 FS_NR_AIML_Air
Since R16, Data storage architecture via Message Framework defined in TS 23.288
Data collection is one of the key aspects in lifecycle management of AI/ML in RAN study

## Slide 37
Summary of Model performance monitoring in SA2 and RAN
vivo view: Alignment/convergence between SA2 regarding ML performance monitoring in R18 eNA-Ph3 KI#1 and potential R19 enhancement
SA2 R18 eNA_ph3 KI#1
RAN1 FS_NR_AIML_Air
In R18, define Model/Analytics Accuracy for classification in TS23.288, which is the number of correct predictions out of all predictions.
In R19, may further discuss how to measure Model performance for regression
Model monitoring is used to against generalization problem, and then is the key point in R18 RAN1
Model monitoring methods and monitoring KPIs have been deeply discussed

## Slide 38
Summary of Model/Functionality/Analytics ID in SA2 and RAN
vivo view: Alignment/convergence between SA2 and RAN or enhancement in SA2 regarding ML Model ID definition/analytics ID since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
SA2 R18 eNA_ph3 KI#1
RAN1 FS_NR_AIML_Air
Since R16, NWDAF service consumer subscribes to a (set of) ML Model associated with a Analytics ID(s)
The NWDAF containing MTLF notifies the NWDAF service consumer with a set of pair(s) of ML Model ID
NOTE: the structure and format of the ML Model ID and its uniqueness are up to stage 3 in R18.
Model ID is important in model identification to distinguish different models with same functionality

## Slide 39
RAN2 progress：
  CP solution：Logged/Immediate MDT, L3 measurements, L1 measurement (CSI reporting), UAI, Early measurements, LPP (for positioning only, related to AI based positioning discussion in SA2)
  UP solution: EVEX framework(highly related to SA2 DCAF/NWDAF)
Note: Please see joint discussion paper S2-2306506 from QUALCOMM/vivo for the details.
    vivo view: UP solution is complementary to CP solution and SA2 should be tasked to study whether and how to enhance UE data collection framework to meet RAN requirement (coordinated with RAN).
Summary of UE data collection

## Slide 40
R17 SA2 eNA_ph2 progress
R18 SA2 eNA_ph3 progress
Summary of Model transfer/delivery in SA2
In R17, only Model delivery within 5GC between same vendor is supported
Model delivery to UE is not supported
In R18, introduce ML model Interoperability information to somehow support Model delivery within 5GC NWDAFs among multi-vendors;
ML Model Interoperability Information, this is vendor-specific information that conveys, e.g., requested model file format, model execution environment, etc.
Still Model delivery to UE is not supported

## Slide 41
Training
NW side
Neutral site
UE side
Compiling
Storage
Inference (inside UE)
Model delivery
Case y
Training
NW side
Neutral site
UE side
Compiling
Storage
(inside NW)
Inference (inside UE)
Model transfer in proprietary format
Case z1
Training
NW side
Neutral site
UE side
Compiling
Storage
(inside NW)
Inference (inside UE)
Model transfer in proprietary format
Case z2
Training
NW side
Neutral site
UE side
Compiling
(inside UE)
Storage
(inside NW)
Inference (inside UE)
Model transfer in open format
Case z3
Training
NW side
Neutral site
UE side
Compiling
(inside UE)
Storage
(inside NW)
Inference (inside UE)
Model transfer in open format of a known or unknown model structure at UE
Case z4 and z5
Summary of Model transfer/delivery discussion in RAN1

## Slide 42
How to support Model delivery to UE - RAN2 progress
Based on RAN1 draft conclusion of model transfer/delivery，RAN2 listed all potential solutions 。
  Option 1: Model transfer/delivery between UE and gNB via CP and UP solutions
    Applicable use cases: CSI feedback enhancement, Beam management
  Option 2: Model transfer/delivery between UE and CN (except LMF) via CP and UP solutions
    Applicable use cases: CSI feedback enhancement, Beam management
  Option 3: Model transfer/delivery between UE and LMF via CP and UP solutions
    Applicable use cases: Positioning accuracy enhancement
  Option 4: Model transfer/delivery between UE and server
    Applicable use cases: CSI feedback enhancement, Beam management, Positioning accuracy enhancement
    vivo view: SA2 should be involved and tasked to study whether and how to support Model delivery to UE (coordinated with RAN).
Summary of Model transfer/delivery discussion in RAN2

## Slide 43
For characterization and performance evaluations of AI/ML based positioning accuracy enhancement, the following two AI/ML based positioning methods are selected.
  Direct AI/ML positioning
  AI/ML assisted positioning
AI based Positioning - RAN1 progress
Summary of AI based Positioning discussion in RAN

## Slide 44
Uses cases listed by RAN
Uses cases listed by RAN

## Slide 45
Coordination between LMF and NWDAF
  How CN help train AI LCS Model(s), including A-AIML/D-AIML
  Model delivery enhancement
    Regarding UE based A-AIML/D-AIML, how CN delivery Model(s) to UE
    Regarding RAN based A-AIML, if CN involved, whether and how CN delivery Model(s) to RAN
    etc.
Data collection enhancement for AI based Positioning
AI model performance monitoring for positioning related to how to measure ML Model performance for regression
5GC architecture enhancement to support AI based Position
5GC architecture enhancement to support AI based Positioning
Notes: 基于AI的定位增强—SA2网络架构增强Objective(s)

## Slide 46
R19
Annex：Integrated Sensing & Communications
SA2/SA3/SA5/RAN

## Slide 47: Background
Wireless sensing technologies aim at acquiring information about a remote object and its characteristics without physically contacting it. The perception data of the object and its surrounding can be utilized for analysis, so that meaningful information about the object and its characteristics can be obtained.
Integrated Sensing and Communication refers to the technologies that combine sensing and communication systems to utilize wireless resources more efficiently. ISAC provided by 3GPP 5G system means the sensing capabilities are provided by the same 5G NR wireless communication system and infrastructure as used for communication, and the sensing information could be derived from RF-based and/or non-RF based sensors.

## Slide 48: Use Cases in SA1
Intruder detection is a typical use cases that was proposed by several companies with different scenarios. This use case can be achieved via different sensing modes: BS monostatic, BS and UE bistatic, UE monostatic.
Similar use cases are parking lot detection, UAV collision avoidance, AGV collision avoidance.
vivo’s preference: xxxxx.
 | Base station monostatic | railway | BS and UE bistatic | UE Monostatic
Intruder detection | Use case 5.2, higyway human/animal detection | Use case 5.7, railway human/animal detection | Use case 5.6, yard intrusion detection | Use case 5.1, home intrusion detection
Parking lot detection | Use case 5.20 |  | Use case 5.20 | Use case 5.20
Collision avoidance | Use case 5.12, avoid UAV (UE, or not) collision to building/tree |  | Use case 5.13, avoid human (holding UE) collision to AGV | 

## Slide 49: Architecture considerations
SA1’s ongoing FS_Sensing will start the consolidation work since SA1#102 in May 2023.
There are 6 sensing modes: (were discussed in SA1 once, but more appropriate to be discussed in SA2 )
SA1 has common consensus that sensing mode (monostatic/bistatic) will not be specified/mentioned in the requirements. Solution-oriented description will restrict downstream workgroups, i.e., SA2 will decide the architecture for sensing.
vivo’s preference: Architecture should flexibly support the different sensing modes i.e. BS monostatic, BS and UE bistatic, UE monostatic and at least support sensing mode 1), 3), 4) in R19 if time is limited
Base station oriented | Base station and UE | UE oriented
1) gNB-to-gNB, monostatic
2) gNB1-to-gNB2, bistatic
3) gNB-to-UE, Bistatic
4) UE-to-gNB, Bistatic
5) UE-to-UE, Monostatic
6) UE1-to-UE2, Bistatic

## Slide 50: Architecture options
vivo’s preference: prefer Option 1 as it can flexibly support the different sensing modes i.e. BS monostatic, BS and UE bistatic, UE monostatic.
Option1a.
Option1b.
Option2.
Option3.
Nx  interface between AMF and SF
Ny  interface between RAN and SF
Nz  interface between UPF and SF

## Slide 51: Sensing result exposure – SA1 discussion
SA1 has defined
  3GPP sensing data: Data derived from 3GPP radio signals impacted (e.g. reflected, refracted, diffracted) by an object or environment of interest for sensing purposes, and optionally processed within the 5G system
  Sensing result: processed 3GPP sensing data requested by a service consumer
Sensing objective is a kind of sensing result that can be directly consumed by an application, i.e. by utilizing sensing data and sensing assistance information exposed by a trusted 3rd party to derive, e.g. is there any intruder or not,
Sensing processing functionalities describe the capability that an entity in 5G system can process the sensing data to obtain sensing result and/or achieve sensing objective (S1-230297, S1-230286).
3GPP sensing data
sensing result
sensing objective
Processing entity#1
Processing entity#2

## Slide 52: Sensing result exposure – SA2 potential architecture
vivo’s initial preference: Option 1 simplifies core network SF functionalities and secure the information to be exposed to a 3rd party.
Option 1 | Option 2 | Option 3
SF exposes “intermediate” sensing result to a 3rd party | SF exposes sensing objective to a 3rd party. | SF exposes sensing data to a 3rd party.
SF performs functionalities of Processing entity #1 as shown in page#53 Advantages: Only expose the sensing result to avoid or alleviate data privacy Disadvantages: Not clear how to define “intermediate” sensing result in 3GPP | SF preforms functionalities of Processing entity #1 and Processing entity #2 as shown in page#53 Advantages: No data privacy issue 5GS is self contained and can cater to different sensing services. Disadvantages: Complexify SF functionalities, which is service-oriented. | SF mainly performs the functionality of exposure without processing Advantages: Simplified SF functionalities in 5GS, as well as leaves flexibilities to 3rd party to enrich sensing services. Disadvantages: Direct raw data exposure and data privacy
tunnel
Notes: 黄色高亮部分去掉

## Slide 53: Coordination between RAN and SA
Compared to positioning service, sensing service involves diversified sensing targets (human, car, rainfall, etc.) and offers richer service types (intruder detection, health monitoring, autonomous driving etc.) than positioning service.
Different service requires different sensing measurement, which is foreseen to produce a larger volume and more private data.
Investigation on standardized sensing measurement parameters (L1/L2) and sensing data transfer from Sensing Rx to SF is necessary.
Option#1: Standardized service-oriented sensing measurement transfer | Option#2: Non-standardized sensing measurement | Option #3: Standardized + Non-standardized
RAN1 standardizes service-oriented sensing measurement parameters to transfer SA2 standardizes corresponding sensing result for exposure Advantage: Standardized interface between RAN and SF, high interoperability among different manufacturers Service-oriented authentication and authorization Disadvantage: Lower compatibility to new sensing services Much standardize work for each sensing service | Using a container for sensing data transfer from RAN to SF SA2 standardizes service-oriented sensing result for exposure Advantage: Less dependency on RAN 1 work Disadvantage: Lower interoperability regarding different RAN and core network manufactures | RAN1 standardizes some service-oriented (e.g. 5GS provided sensing service) sensing measurement parameters to transfer, meanwhile, uses container for some private or new sensing services SA2 standardizes service-oriented sensing result for exposure Advantage: Safeguarding 5G sensing services More flexible to new services Disadvantage: Lower interoperability among different manufacturers regarding new services
vivo’s preference: Option#3 offers better balance between standardization work and market

## Slide 54
R19
Annex：Ambient IOT
SA2/SA3/SA5RAN

## Slide 55
Ambient IOT: Motivation
R19
    Ambient IoT technology
    Large communication range
    Highly increased communication efficiency
    Automatically communication, without labor participation
    Easily tracking within the wide coverage of 5GS
    Existing RFID technology
    Hand-hold machine scanning (labor-consuming)
    Large number of Tags (time-consuming)
    Close communication range, cannot work when Tag is covered, suffer from interferences between multiple readers（easily failure）
    3GPP already defined several IoT technologies.
    There are other kinds of the IoT devices which have very specific requirements in terms of size, weight, and power consumption. These IoT devices may be deployed under extreme environmental conditions (e.g., high pressure, extremely high/low temperature, humid environment).
    The power consumption of these IoT devices may be very low and therefore it would be benefit to support maintenance-free for them.

## Slide 56
Ambient IOT: Use Cases at SA1
R19
Enterprise/Factory/Farm use cases
Personal/Consumer use cases
Base Station
IoT APP Platform
tag
Select function and clothes
Washing machine
Ambient IoT device information
Parameter values
Parameter values
Personal use cases; Indoor communication with UE/CPE; Outdoor communication with RAN, UE assistance/relay may be needed.
Smart laundry
Personal belongings Finding
Indoor Positioning
Automated Warehousing
Smart Agriculture/Farm
Environmental Monitoring
Enterprise use cases; Indoor / outdoor communication with RAN, UE assistance/relay may be needed.

## Slide 57
Ambient IOT: Existing studies at RAN and SA1
R19
SA1 TR describes 33 use cases (3 traffic scenarios included)
Reader: UE reader+Base Station Reader
Communication mode:
  Passive AIoT device;
  Active AIoT device
Use case categories
  Inventory, Sensor, Positioning, Control;
  Indoor, Outdoor
Operations to an AIoT device include:
  Activate, Deactivate, Inventory, Read, Write, Positioning, Control.
Access network include:
  PLMN
  NPN
Architectures:
  Direct communication
  Indirect communication (for the case UE as reader)
vivo’s Proposal
    It is difficult to consider all the use case in one study phase1 and propose to differentiate the use cases in different phases
    Rel19 focus on phase1 use cases
      Inventory/read /write
      PLMN
      licensed spectrum,
      Indoors & Outdoors
    Phase2
      others
SA#1 Study
RAN Study
Use case categories at RAN study
  Inventory, Sensor, Positioning(P2), Control;
  Indoor, Outdoor
Four Topologies
Three Ambient IOT Devices
  Note：Using “Reader” in the DP is for briefly presenting a UE/Base Station communicating with AIOT Devices. It doesn’t means to introduce a new terminology.

## Slide 58
Topology 3: BS ↔ assisting node ↔ Ambient IoT device ↔ BS
Ambient IOT: Topologies+ AIOT Devices Types
R19
Topology 4: UE ↔ Ambient IoT device
Topology 1: BS ↔ Ambient IoT device
Topology 2: BS ↔ intermediate node ↔ Ambient IoT device
Device Type |  | 
Device A | No energy storage | no independent signal generation, i.e. backscattering transmission
Device B | Has energy storage | no independent signal generation, i.e. backscattering transmission. Use of stored energy can include amplification for reflected signals
Device C | Has energy storage | has independent signal generation, i.e. active RF component for transmission
vivo’s Proposal
    Phase1
      All AIOT device types
      Basic Topology1+4
      Can further consider Topology2 if time allowed
    Phase2
      Topology 3

## Slide 59
Ambient IOT: Motivation for CN involvement
R19
Manage and control the reader
communication between reader and Tag is control by the Reader and/or APP,
Relay the data
On top of level1 Control the communication between reader and Tag
Identify the Tag
Security mechanism: authentication, encryption & data integrity
Basic procedure for: read/write/inventory(collect the ID)
On top of level2
Positioning, Mobility
Further control procedure for Tag
On top of level3: TBD
Treat Tag is a kind of UE?
  Manage the tag context/status within the 5GS?
…
level1
Level2
level3
level4
    CN involvement could be optional to connect reader and 3rd party App
      However, at least in the 3rd party request scenario, CN behavior needs to be discussed
    Different involvement levels can be considered
    Phase1 study focus on level1 or level2

## Slide 60
Ambient IOT: Architecture
R19
    “UE as reader”: left is reader, right connecting to 5GC in UE’s way
    “Base Station as reader”: left is reader, right connecting to 5GC in Base Station’s way
    CN impact for Ambient IOT
      Option1: enhance existing NF (preferred)
      Option2: consider new NF
      Support:
        Device Type A/B/C
        Topology1+4: UE Reader + Base Station reader
        Use cases: Inventory/Sensor data/Control
        Group handling for massive Tag number
        licensed spectrum, Indoors & Outdoors
      Consider:
        Positioning/Mobility
        Energy Harvest
    A compatible and sufficiently extensible Arch. for different kinds of readers and AIOT devices types

## Slide 61
Low complexity
R19
    Simplified protocol stack of the interface between Reader and AIOT devices for low power consumption, low complexity and low cost.
    Simplified procedures and features for AIOT devices
Ambient IOT: Simplified and Common interface/protocol stack
Low power consumption
Low cost
    Common and consolidated interface between AIOT device and reader for all topologies and device types and it is beneficial for the business
      Common signal channel design and procedures for all topologies, as much as possible.
      CN involvement should be compatible to both UE reader and Base Station reader

## Slide 62
Ambient IOT Phase1 study
R19
    SA2 Responsibility
      Architecture enhancement for ambient IOT within 5GS
        Considering two new roles and possible CN impact for AIOT: AIOT device, Reader Device
        Two communication between AIOT device and Network: direct access or indirect access, i.e. Base Station reader and UE reader
      Reader control and management, support both 3rd party reader, operator reader, and personal reader,
      Based on 3rd party request, control and manage the communication between Reader and AIOT devices, including read, write, inventory, etc.
      how 5G system to provide collected information from Ambient IoT device(s) to the 3rd party.
      Simplified protocol stack of the interface between Reader and AIOT devices for low power consumption, low complexity and low cost.
SA3/5
RAN1/2
SA2
    SA3 Responsibility
      Authentication + Security detail
        On demand authentication, e.g. authenticate Ambient IOT devices by 5GS, authenticate reader by Ambient IOT devices
    SA5 Responsibility
      Charging
    RAN1/2 Responsibility
      AS Layer communication between Reader and AIoT devices
      Signal channel design and procedure description between Reader and AIOT devices;
      Simplified protocol between AIOT device and Reader
      Indoor/outdoor
      Licensed Spectrum
      Charging for Ambient IOT device related service
      NOTE2: The ambient IOT device might not be a UE, might without UICC.
      NOTE3: The study should focus on PLMN scenario and licensed spectrum indoor/outdoor.
SA2+SA3+RAN cooperation

## Slide 63
R19
Annex：Metaverse & MEC
SA2/SA4/SA6

## Slide 64: Progress in SA1 FS_Metaverse (1)
IMS-based 3D avatar communication
  The IMS shall allow multimedia conversational communications between two or more users providing real time conversational transfer of animated user digital representation and speech data.
  The 5G system shall support a means for UEs to produce 3D avatar media to be sent uplink, and to receive this media downlink.
  The 5G system shall support a means for the production of 3D avatar media to be accomplished on a UE to support confidentiality of the data used to produce the 3D avatar (e.g. from the UE cameras, etc.)
  The 5G system shall support a means to enable locally generated media (e.g. text or video) of a party to be transcoded before it is rendered for the receiving party.

## Slide 65: Progress in SA1 FS_Metaverse (2)
IMS-based 3D Avatar Call Support for Accessibility Use Cases
  The 5G system shall support the encoding of sensor data capturing the facial expression and movement and gestures of a person, in a standard form, such that as part of the avatar encoding.
  The 5G system shall support a set of transcoders from and to avatar representations e.g. between text, speech and avatar encoding.
  The 5G system shall support the avatar transcoding functionality to control the appearance of the avatar based on the preferences of its associated user.
  The 5G system shall support a set of transcoders to facilitate accessibility of avatar representation from and to GTT to control the appearance of the encoded avatar.

## Slide 66: Considering on IMS/NG-RTC enhancement to support mobile metaverse service
IMS/NG-RTC extends to support diversity media service (Avatar generation, language transcoder, etc)
  Open to enhance either IMS architecture or NG-RTC architecture
Coordination/negotiation between the UE and IMS when performing avatar communication service processing, by considering the following aspects (including but not limited)
  Service type, UE capability (e.g. computing/processing capability), performance requirements, etc.
UE/mobile metaverse server Capability management in IMS (including but not limited)
  Refined new capability management (e.g. registration, selection, query, updating, exposure, de-registration)
Coordination with SA4 (e.g. protocol, support of split rendering)