## Slide 1: Release-19 Priorities
Charter Communications, Comcast, CableLabs

## Slide 2: Outline
This document is a consolidated view of Release-19 topics of interest to the companies co-sourced this contribution
Release-19 topics of interest (not in the order of specific priority)
  Enhancements to Shared Access Network Architecture
  N3GPP enhancements to identify UEs behind WLAN AP
  ATSSS enhancements
  Extension of support for L4S for non-3GPP access connected to 5GC
  Security enhancements
  5WWC enhancements on visibility of devices

## Slide 3: Overall View on Rel-19 Content (1/3)
The list is not in specific priority order.
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
#1 | Enhancements to Shared Access Network Architecture (See slides 6-7 for details) | Description: NetShare specifies service requirements for inter-connecting participating operators’ core networks and Shared NG-RAN of the hosting operator via an element of the Hosting Operator. Key Work Tasks include - Study architecture options including definition of new network functions and/or enhancements of existing network functions to enable indirect network sharing Note: New network function specified to be part of the hosting operator network Study interfaces enhancements, if any, between the hosting and participating operators network function | Yes, TR 22.851 (NetShare) | SA2 | Yes | SA3 for security, SA5 for charging
#2 | N3GPP Enhancements to identify UEs behind WLAN AP (See slide 8-9 for details) | Description: Enhancements to UE configuration, UE policy and registration functionality to facilitate identification of UE connected behind a WLAN AP using PSK Key Work Tasks include - Study methods/procedures to identify the UE when it connects to WLAN using PSK; study encompasses: Enhancements to existing N3GPP registration procedure or specifying a new procedure Enhancements to UE policy to trigger the procedure when the UE connects to WLAN AP using PSK This could include updates to USIM configuration Study methods/enhancements to enable reporting of its continued association with a WLAN AP or a new association with a new WLAN AP Study methods/enhancements to enable reporting of the N3GPP access related information by the UE (e.g., BSSID, ESSID, UE local IP address, etc.) Enhance the API framework to enable subscription/notification for N3GPP association information related to a UE by an operator managed AF | - | SA2 Enhancement to Rel-15/17 N3GPP work within SA2 | No | SA3 for security

## Slide 4: Overall View on Rel-19 Content (2/3)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
#3 | ATSSS enhancements (See slide 10 for details) | Study an ATSSS-like solution between one 3GPP access and one WLAN. Since the first release of 5GS, untrusted/trusted WLAN (i.e., N3IWF and TNGF) have not been fully adapted that also prevents adaption of 5GS capabilities like ATSSS. A ‘lightweight’ ATSSS-like capabilities between one 3GPP and one WLAN can be beneficial for the ecosystem until (un)trusted access nodes become widely available. Note: Rel-19 proposals like the ones in S2-2306991/92 to SA2#157 have similar concept. Study ATSSS between two 3GPP and one non-3GPP access legs for a UE with single or multiple subscriptions Separate ATSSS functions out of UPF | No Yes, TR 22.841 (DualSteer) No | SA2 SA2 SA2 | No No No | SA3 for security, SA5 for charging?
#4 | Extension of support for L4S for non-3GPP access connected to 5GC (See slide 11 for details) | As part of Rel-18 XRM WI, 5GS has introduced network information exposure based on congestion experienced by NG-RAN (i.e., congestion reporting and ECN marking for L4S). This capability enables better QoE for high data rate low latency type applications like XR. In order to ensure similar QoE over any access network the UE is accessing, the network information exposure capabilities need to be extended to support non-3GPP accesses (i.e., untrusted, trusted, wireline) connected to 5GC. Similar requirements have also been identified as part of SA1 Metaverse SID conclusions in Rel-19. Key Work Tasks include - Enhancements to support L4S over non-3GPP access connected to 5GS for high data rate low latency type applications. Enhancements to have integrated handling of high data rate low latency type applications over 3GPP and non-3GPP accesses. Note: Following Rel-19 proposals to SA2#157 have coverage of this feature: S2-2306753, S2-2307383, S2-2307245, S2-2307179) | Yes, TR 22.856 (Metaverse) | SA2 | No | No
The list is not in specific priority order.

## Slide 5: Overall View on Rel-19 Content (3/3)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
#5 | Security enhancements for UEs connecting over non-3GPP access (See slide 12 for details) | Study optimization of UE authentication over non-3GPP access: Optimization across UE mobility in trusted non-3GPP access across different TNAPs (under same and different TNGFs) Optimization of re-authentication during UE mobility in non-3GPP access by using, for example: 802.11r Fast Basic Service Set (BSS) Transition (FT) for UE mobility and reassociation with a new AP in Wi-Fi access EAP Re-authentication Protocol (ERP) | No | SA3 | No | No
#6 | 5WWC enhancements on visibility of devices behind RG (See slide 13 for details) | Since the 5WWC work started in Rel-16, though there was interest (S2-1904943) from BBF and CableLabs on bridged mode RG deployments and relevant requirements for devices connecting behind RG, no solution has been agreed to address such requirements in Rel-16/18. Specifically, requirements like visibility of each device in 5GC, allocation of IP addresses to each device by SMF/5GC, policy control by 5GC based on MAC and/or IP addresses of each device, etc. Lacking such a solution for devices behind RG not only prevents operators to make use of the full potential of converged 5GC architecture but also prevents offering services already offered by non-converged core deployments. Note: As part of Rel-18 5WWC_Ph2 study, solution #8 in TR 23.700-17 addresses the requirements. If SA2 can agree on such a solution, this can be addressed as TEI19 WID. | No | SA2 | No | SA5 for charging?
The list is not in specific priority order.

## Slide 6: #1. Enhancements for Supporting 5G Indirect Network Sharing (1/2)
Background
  Network sharing enables operators to maximize rollout and improve overall network quality. 3GPP system supports several types of network sharing since Rel-5, most of which are inherited by 5G
  One of the challenges for the operators is the maintenance of the interconnections (e.g., number of network interfaces) between the shared NG-RAN and participating operators’ core network
  In TR 22.851, SA1 studied the feasibility of sharing when there is no direct interconnection between the shared NG-RAN and participating operators’ core networks
Proposal
  Study the architecture options including definition of new network functions and/or enhancements of existing network functions to enable Indirect Network Sharing
    Note: The new network functions specified are to be part of the hosting operator network
  Study the interfaces enhancements, if any, that are necessary between the hosting and participating operators network functions

## Slide 7: #1. Network Sharing Architecture Options (2/2)
5GC Operator A
5GC Operator B
5GC Operator C
5GC Operator X
NG-RAN Operator X
5G MOCN
Many N2/N3
connections
Many N2/N3
connections
Many N2/N3
connections
5GC Operator A
5GC Operator B
5GC Operator C
NG-RAN Operator X
Few N2’/N3’
connections
Many N2/N3
connections
Operator X
GW NE
5GC Operator X
Few N2’/N3’
connections
Few N2’/N3’
connections
5GC Operator A
5GC Operator B
5GC Operator C
NG-RAN Operator X
Few N14’/N16’
connections
Many N2/N3
connections
5GC Operator X
Few N14’/N16’
connections
Few N14’/N16’
connections
5G Indirect Network Sharing
Gateway-type Solution
5G Indirect Network Sharing
NF-to-NF Solution
To be studied
To be studied
Exists today
UE 1 of OP X
UE 2 of OP A
UE 3 of OP B
UE 4 of OP C
UE 1 of OP X
UE 2 of OP A
UE 3 of OP B
UE 4 of OP C
UE 1 of OP X
UE 2 of OP A
UE 3 of OP B
UE 4 of OP C
SIB {PLMNs of host &
participating OPs}
SIB {PLMNs of host &
participating OPs}
SIB {PLMNs of host &
participating OPs}
….
….
Host Operator
Participating Operators
Host Operator
Participating Operators
Host Operator
Participating Operators

## Slide 8: #2. N3GPP enhancements to identify UEs behind WLAN AP (1/2)
Introduction
  MAC randomization is being increasingly adopted as a privacy/security measure by device OEMs, greatly impeding the ability of operators to use MAC address as a unique device identifier within their WLAN infrastructure and offer differentiated user experience over it
  Pre-Shared Key (PSK) is predominantly used by end-users, especially in residential deployments (even 3GPP meetings use pre-shared key ) where NSWO authentication (which relies on EAP) cannot be leveraged to identify the UE
Key Issues
  How to identify a UE within the 5GC that connects to the residential WLAN AP using PSK
  How to identify whether the UE is connected to the residential AP managed by the operator or a residential AP that is not managed by the operator
Observations from 3GPP specifications review
  Untrusted N3GPP registration could be leveraged to identify UEs connecting to WLAN using PSK or an alternative procedure could be developed
  Mechanism by which the UE triggers registration procedure over untrusted N3GPP is unclear
  No mechanism for the UE to share N3GPP access related information via an N1 procedure that could allow the operator to determine whether the UE is connecting via a specific managed residential AP or a non-managed AP

## Slide 9: #2. N3GPP enhancements to identify UEs behind WLAN AP (2/2)
Proposals
  Study methods/procedures to identify the UE when it connects to WLAN using PSK; study encompasses:
    Enhancements to existing N3GPP registration procedure or specifying a new procedure
    Enhancements to UE policy to trigger the procedure when the UE connects to WLAN AP using PSK
      This could include updates to USIM configuration
  Study methods/enhancements to enable reporting of its continued association with a WLAN AP or a new association with a new WLAN AP
  Study methods/enhancements to enable reporting of the N3GPP access related information by the UE (e.g., BSSID, ESSID, UE local IP address, etc.)
  Enhance the API framework to enable subscription/notification for N3GPP association information related to a UE by an operator managed AF

## Slide 10: #3. ATSSS enhancements
Study ATSSS-like solution between one 3GPP access and one WLAN.
  Current ATSSS architecture with untrusted/trusted WLAN requires N3IWF and TNGF, which have not been fully adapted in the ecosystem. A ‘lightweight’ ATSSS-like capabilities between one 3GPP and one WLAN can be beneficial for the ecosystem until (un)trusted access nodes become widely available.
  Rel-19 proposals like the ones in S2-2306991/92 to SA2#157 has the similar concept.
Study ATSSS between two 3GPP access and one non-3GPP access legs based on SA1 Rel-19 DualSteer WI allowing mainly
  Autonomous simultaneous data transmission over two types of access networks.
  Seamless user data switching, steering and splitting of the 3GPP legs from PLMN(s), SNPN&PLMN or SNPN(s) operated by one or two operators for UE with single and preferably multiple PLMN(s)/SNPN(s) subscriptions.
  Improved low latency and high reliability across multiple types of access networks to meet user QoE.
Architectural enhancements to separate ATSSS functions out of UPF
  Having ATSSS functions out of the UPF (e.g., a new NF or an external node) will allow flexibility for operator deployments.
  Architectural impact for CP/policy signaling and UP data transfer needs to be studied.
DualSteer
inter-PLMN scenario with two 3GPP + one non-3GPP accesses
New node with ATSSS functions in 3GPP architecture.
ATSSS
?
?
?
?
ATSSS

## Slide 11: #4. Extension of support for L4S for non-3GPP access connected to 5GC
Proposals
  Ensure overall QoE for delivering low latency media via converged 5GC can be applied for non-3GPP access deployments.
    Enhance 5GC to support non-3GPP access network reporting of congestion information, L4S marking, and support API based exposure information to AF
    Enhance ATSSS to make use of L4S services
  Standardize in Rel-19, non-3GPP access network support for L4S over 5GC such as:
    Perform L4S marking as instructed by SMF/PCF
    Report congestion information to PSA UPF via GTP-U header
    Support API based exposure of network information towards AF

## Slide 12: #5. Security enhancements for UEs connecting over non-3GPP access
Study optimization of UE authentication during UE mobility in trusted non-3GPP access across different TNAPs under
  Same TNGF
  Different TNGFs
Study optimization of re-authentication during UE mobility in non-3GPP access by using, for example
  802.11r Fast Basic Service Set (BSS) Transition (FT) for UE mobility and reassociation to a new AP in Wi-Fi access
  EAP Re-authentication Protocol (ERP)
Optimization across UE mobility in trusted non-3GPP access
TNGF
5GC
TNGF
TNGF
TNAPs

## Slide 13: #6. 5WWC enhancements on visibility of devices behind RG
Rel-18 5WWC_Ph2 WI has introduced a solution for group of devices (behind AP/RG) connecting to 5GC and providing differentiated services only for those group of devices. However, the solution is not sufficient for operators as it does not allow capabilities and service offerings like the ones below that already exist in their network.
  Visibility and identification of each device (e.g., MAC address).
  Allocation of IP address(es) to each device.
  Subscriber/end-user and operator control of services and differentiated QoS policy (by customer and operator) to each device. Capabilities such as
    Usage and service visibility: Subscriber to view, monitor usage across applications and devices real time.
    User-controlled prioritization and Parental control: Subscriber to prioritize, control QoS or block individual device(s) or device(s) of an individual user or applications. Subscriber to control access based on time of day and/or content type.
Having awareness of each device in 5GC will also allow operators to additional services, for example,
  NaaS to third parties for sponsored connectivity (e.g., an 8K movie to a specific device from a streaming provider even though the subscriber’s regular subscription does not allow it.)
Standardizing capabilities/requirements like the ones above will allow operators fully benefit from converged 5GC architecture.
  In Rel-18 TR 23-700-17 had Solution #8 (“combo Ethernet + IP” PDU type) that would facilitate the use cases above for RG (FN-RG, 5G-RG), but it could not make the TR conclusions. If such a solution is agreeable by SA2, this can be addressed as a TEI-19 WID.
Solution concluded in Rel-18
TR 23.700-17, Solution #8, Protocol stack for combo PDU session.

## Slide 14: Summary
This document highlights some Rel-19 SA topics of interest to Charter Communications, Comcast and CableLabs.