## Slide 1: SA Rel-19 scoping, Ericsson initial view
Krister Sällberg
Ericsson

## Slide 2: Outline: SA2 Rel-19 package – A few Considerations
Feature development for Mobile Broadband services
  Adapting to meet new traffic patterns and application trends
Balanced support of features driven from deployments of different verticals
Some of the features on the table depend very much on RAN driven specifications
Expectation that enhancements of features of earlier releases will be included in Rel-19
  However, we should be very selective as pointed out by major operators about the need of market deployment & feedback
Important to get market feed-back on important gaps of missing functionality (e.g. from 5G deployments).
  We need to have a budget to take care of such Study Items / Work Items
SA1 Rel-19 stage 1 requirements are broad and challenging for a single release.
  There is a need for proper down selection – preferably SA1 doing the first step of within Work Item down scoping.
  Some larger feature may be specified over two releases.
Ericsson favors a new scheme of selection of rapporteurs avoiding race for rapporteurship
  Such process needs to be agreed soon.

## Slide 3: Content:Initial scoping input – Themes grouping
Industrial Verticals
  User Plane Redundancy for IP
  Ethernet alignment
Resilience by Dual 3GPP Networks
ATSSS Dual Steer
Network Automation
AI/ML
MBB adapt to new traffic patterns and trends
  MASQUE Enhanced Traffic Management
  XR / Metaverse
  ATSSS Lite
IMS and NG RTC
  IMS Data Channel leveraged for XR/Metaverse
  IMS event exposure framework
RAN Driven work
Mission Critical, VMR enhancements, ProSe, NTN Evolution, Femto
Exploring new business
Ambient IoT
Integrated Sensing and Communication

## Slide 4: Content:Initial scoping input
Ericsson Proposed SA2 Study Items into SA2#157 (additional slides provided for details)
  5GS Study on user plane redundancy for IP (used to be DetNet_Ph2, S2-2306440)
  MASQUE Enhanced Traffic Management (S2-2306574)
  Delegation of (re)selection of target NF across PLMNs (S2-2306582)
  Roaming Value Added Services (S2-2306445)
  IMS event exposure framework (S2-2306443)
  Third party call ID in IMS sessions (Potential TEI19 WID)
  (S2-2306444)
  TEI19 WID: Minimize the number of Policy Associations
  (S2-2306435)
Possible TEI19 items
Need to set a side a healthy budget, addressing operators’ immediate needs on improvement of existing deployments/features
For SA2 to be discussed
Prefer not to do another phase in Rel-19
  NPN, Slicing, Edge Computing, UPEAS, 5WWC, SFC

## Slide 5: Overall View on Rel-19 Content - 1
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | 5GS Study on user plane redundancy for IP | redundant paths in 5GS using multiple UEs (23.501 Annex F) or dual connectivity (23.501 clause 5.33.2.1); PREOF (packet replication, elimination and ordering function) at the UPF within the data network on N6; PREOF at the terminal device or at a host behind the terminal device; DetNet controller outside of the 5GS, or a DetNet controller within the 5GS operated by the 3GPP operator. (See slide later) | Continuation of Time Sensitive Communications and Redundant user plane improvement | SA2 | No | No
2 | New SID on MASQUE for Enhanced Traffic Management | Can benefit the 5GS Traffic management by explicit information exchange on fully encrypted traffic. The study identifies the relevant information that would be exposed Can benefit other 5GC functions like reporting of user plane data as input to analytics or to monitor the correct URSP enforcement in the UE. Need to be advertised towards the UE, and which information the UE needs to be provisioned with if any. Can integrate in the PCC Framework, and which enhancements are required the PCC framework, if any. The solutions should consider user plane transmission efficiency. The solutions should not be limited to work with QUIC traffic. They should work on all type of MASQUE deployments i.e. one or two-proxies, where the second proxy is run by a third party that is deployed on the DN. | A use case that may benefit of having MASQUE technology in Release’19 is Traffic Detection with user privacy e.g. on top of an operator provided relay service, for UPF functions in TS 23.501 clause 5.8 | SA2 | No | SA3

## Slide 6: Overall View on Rel-19 Content - 2
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | Study on delegation of (re)selection of target NF across PLMNs | The study aims to validate the benefits of delegating selection and/or reselection of the target destination logic from the NF (client) to a different target PLMN, while its objectives are the following: Identify the implications of having different combinations of communication models between client PLMN and destination PLMN. Identify the element(s) in the destination PLMN that is responsible to perform the delegated logic and describe the required capabilities. Propose required procedure and interfaces update. | 3GPP has defined indirect communication via the SCP, allowing for different levels of delegation from the NF (acting as client) to the SCP, of the selection and reselection of the target destination logic. In current specifications, indirect communication is defined only intra-PLMN, that implies that delegation of (re)selection logic is not possible when the target destination is in a different PLMN than the client NF. | SA2 | No | No
4 | Study on Roaming Value Added Services | The objectives of this study are the stage 2 aspects for the following RVAS in 5GS enabled by the PLMN as requirement have been specified in TS 22.261: Welcome SMS Steering of Roaming (SoR) during the registration procedure Subscription-based routing to a particular core network (e.g. in a different country) | TS 22.261 | SA2 | No | No

## Slide 7: Overall View on Rel-19 Content - 3
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5 | Study on IMS event exposure framework | •event subscription mechanisms via subscribe / notify procedures to external API invokers, •identification of IMS events that can be subscribed to, •locator functionality whereby the IMS NF / IMS NFs serving the specific subscriber(s) for which the specific event was requested is found, •subscribe / notify procedures from the IMS NF / IMS NFs serving the specific subscriber(s) for the requested event. •synergies with the Network Exposure Framework defined in 5GS (e.g., exposure of events to external API invokers via the network exposure function (NEF) from the IMS NF / IMS NFs). | There are currently no standard defined mechanisms in IMS for an external (to the PLMN trust domain) API invoker to subscribe to specific events related to a specific IMS subscriber / group of IMS subscribers. The serving IMS NFs (providing / producing said events / data) cannot be dynamically located by the API invoker. An example of a specific event that can be subscribed to is “IMS user call-state” (e.g., idle, busy, registered etc.). This specific event may be used by an external AF (e.g., a backend bank fraud system) to obtain the call-state of an IMS user. This information can be input to fraud algorithms (e.g., suspicious activity on User-X’s bank account plus user X call state = busy indicates a heightened risk of fraud). | SA2 | No | SA3
6 | Study on 3rd party call id in IMS Sessions | The objective is to get a solution to KI#1 “How the Originating IMS network signs the 3rd party IDs and terminating IMS network verifies the 3rd party IDs” as outlined in TR 33.890, from the NG-RTC study into normative specifications. The study will ensure that SA3 is involved in the security aspects required for any selected solution This is also a possible candidate for TEI-19 if solution can be agreed via discussions/draft CRs. | Evolution of IMS multimedia telephony service (NG_RTC) | SA2 | No | SA3

## Slide 8: Overall View on Rel-19 Content - 4
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
7 | Minimize the number of Policy Associations | The objective is to minimize the establishment of AM, UE and SM Policy Associations as follows: -The Access and Mobility Subscription Data Type is extended to indicate if the UE subscription is enabled for the reception of UE Policies or the reception of AM Policies. -The AMF triggers the AM Policy Association Establishment based on the indication of whether AM Policies are enabled for the registered SUPI, as provided in the Access and Mobility subscription data. -The AMF triggers the UE Policy Association Establishment based on the indication of whether UE Policies are enabled for the registered SUPI, as provided in the Access and Mobility subscription data. -The Session Management Subscription data Data Type is extended to indicate if the UE subscription is enabled for the reception of SM Policies. -The SMF triggers the SM Policy Association Establishment based on the indication of whether SM Policies are enabled for the SUPI, DNN,S-NSSAI as provided in the Session Management Subscription data -For exposure, when the provided service parameters require the delivery of UE policies to the UE, the UDM authorizes the AF request based on the indication of whether the UE is enabled for the reception of UE policies. -For exposure, the provided AM influence parameters provided by the AF are authorized by the UDM authorizes based on the indication of whether the UE is enabled for the provisioning of AM Policies. | Improved network efficiency as well as UE signalling, TEI19 WI proposal | SA2 | No | No
… |  |  |  |  |  | 

## Slide 9: Summary
Balanced content
Properly scoped content respecting timeline
Aligned content with RAN where dependency identified
Small(er) enhancements/improvements addressing operators’ deployment and market needs

## Slide 10
Additional Material in support of the proposed SI/WI

## Slide 11: Study on User Plane Redundancy for IP

## Slide 12: Rel-18 DetNet solution
UE
(R)AN
UPF
SMF
AMF
PCF
TSCTSF
CPF: DetNet controller
DetNet network
5GS logical DetNet Router
DetNet system
NW-TT
UDM
For industrial/critical communications
Realized DetNet forwarding sub-layer: 5GS acting as a transit router.
TSCTSF maps requirements (max. latency and max. loss) and traffic specification to 3GPP parameters
DetNet service sub-layer not specified in rel-18 due to lack of IETF support for IP user plane

## Slide 13: DetNet service sub-layer for IP
Redundant paths with packet replication and elimination
  Failure of one path does not affect e2e traffic
Redundancy e2e or for a segment
3GPP support for redundant paths:
  Mutiple UEs (23.501 Annex F)
  Dual connectivity (23.501 clause 5.33.2.1)
  Redundancy handling for replication and elimination not part of 3GPP spec.
IETF solution for DetNet IP user plane service sub-layer now mature
  draft-ietf-detnet-mpls-over-ip-preof expected to become RFC in rel-19 timeframe
  Uses MPLS headers for encapsulation without requiring MPLS support.
DetNet controller
PREOF
PREOF
Host1
Host2
PREOF: Packet Replication, Elimination and Ordering Function (DetNet)

## Slide 14: 5GS IP service layer support for DetNet - Example 1
UE2
UE1
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS
Redundant 5GS path using 2 UEs
DetNet controller provided in operator domain
Operator self-contained solution for redundancy as a service

## Slide 15: 5GS IP service layer support for DetNet - Example 2
Redundant 5GS path using dual connectivity (single UE)
DetNet controller provided in operator domain
Operator self-contained solution for redundancy as a service
UE
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS

## Slide 16: 5GS IP service layer support for DetNet - Example 3
Redundant 5GS path using 2 UEs
External DetNet controller
Redundancy can be extended e2e, PREOF possible outside of 5GS
UE2
UE1
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS

## Slide 17: User plane redundancy for IP: Summary
Rel-18 DetNet limited to forwarding sub-layer
Rel-19 DetNet possible to extend to IP service sub-layer to provide redundancy
Flexible framework proposed to integrate with industrial/critical applications:
  DetNet controller may be outside of 5GS, or integrated into 5GS for operator self-contained solution
  PREOF functionality may reside within 5GS, or outside
  3GPP redundant paths possible with multiple UEs or using dual connectivity
Adds operator value to integrate 5GS to industrial deployments and provide 5GS redundancy as a service.

## Slide 18: MASQUE for Enhanced Traffic Management

## Slide 19: MASQUE Specifications
IETF MASQUE (Multiplexed Application Substrate over QUIC Encryption) WG was established in June 2020.​
It was Chartered to specify secure proxy protocols and mechanisms based on QUIC.
Main deliverables include so far:​
RFC 9297 - HTTP Datagrams and the Capsule Protocol (ietf.org)​
Defines the concept of datagrams for HTTP. Primarily to be used for HTTP3 over QUIC with support for the datagrams. ​
RFC 9298 - Proxying UDP in HTTP (ietf.org) ​
Extends HTTP with support for UDP proxying. It uses HTTP datagrams​
Work ongoing and soon to become RFCs as well​
draft-ietf-masque-connect-ip-01 - IP Proxying Support for HTTP ​
Extends HTTP with support for IP proxying​
The MASQUE WG has been rechartered to focus on extensions to the base specifications. This allows the WG to work on extensions such as adding sequence numbers to HTTP datagrams (which will be used by ATSSS).

## Slide 20: MASQUE Technology Principles
An HTTP-based tunnel is established between a client and a relay (aka MASQUE server) which receives traffic from the client through the tunnel and forwards it to a target server or another relay. While earlier versions of HTTP are supported it is mostly intended to be used with HTTP3 over QUIC.​
The MASQUE server provides a proxy service that forwards multiple flows inside an HTTP3 connection:​
  HTTP3 settings indicate support for HTTP datagrams. Extended HTTP CONNECT method with new upgrade tokens indicate UDP or IP proxying. ​
  The HTTP-based CAPSULE protocol allows for tunnel configuration messages and stream-based encoding of encapsulated datagrams.​
  Multiple encapsulated connections: End-to-end security is unaltered by proxy​
​
​
​
​Client establishes HTTP3 tunnel connection to MASQUE proxy (yellow)
Client establishes HTTP3 tunnel connection to MASQUE proxy (yellow)​
This technology allows endpoints and in-network relays to exchange information explicitly​
Client
MASQUE
Server
Target
Server
(or second relay)
HTTP3 / QUIC tunnel
End-to-end
connection

## Slide 21: MASQUE Deployment Examples
3GPP Release 18 ATSSS
Support for MP-QUIC and MASQUE introduced to enable packet splitting of UDP flows across 3GPP and non-3GPP access
Could also support general IP flows but this was not part of rel-18 (could be future extension)
Relay Service for Privacy (on the field)
It consists of two QUIC/MASQUE proxies (relays):
  Ingress proxy: assigns the user an anonymous IP address (maps to their region but not their actual location).
  Egress proxy: decrypts the web address they want to visit and forwards them to their destination.
This separation of information protects the user’s privacy. No single entity can identify both who a user is and which sites they visit.
Application
Server
Application
Application
MASQUE
Ingress proxy
Application
MASQUE Egress proxy
Client
Non-3GPP
AN
RAN
UPF
SMF
N3IWF
Multi-access PDU Session
MASQUE / MP-QUIC client
MASQUE / MP-QUIC proxy
W-AGF

## Slide 22: MASQUE enabled 5GS Benefits this proposal brings
5GS may generalize the usage of MASQUE that has been introduced for ATSSS in Release’18.
MNO may be able to satisfy user E2E concern for privacy and the network needs integrating the MASQUE relay in the UPF (i.e. the Mobile network takes part in the relay service ).
  MASQUE can be used for exchange of explicit information between end-points and in-network relays. Integrated in the UPF Policy Control Enforcement Point, it may facilitate Traffic Detection on guaranteed information for:
    Traffic Management (e.g. QoS, charging…)
    Traffic Data Collection (e.g. for Analytics)
  (Compared to using information from passive listeners, suffering from increasing encryption trend and conditioned to traffic changes)
The information exchanged is controlled, correct and useful. It is not subject to changes in communication patterns and in how traffic flows are observed by the network.
It may be an opportunity for new use cases and for MNOs to establish new and well-defined business relationships

## Slide 23: SID Summary
Main objective of this study is to study the potential of MASQUE technology to enhance 5GC Traffic management capabilities.
The Study evaluates whether ATSSS MASQUE proxy in UPF should be generalized in Release’19.
This study determines whether and how MASQUE capabilities in the 5GC user plane:
  Can benefit the 5GS Traffic management by explicit information exchange on fully encrypted traffic. The study identifies the relevant information that would be exposed.
  Can benefit other 5GC functions like reporting of user plane data as input to analytics or to monitor the correct URSP enforcement in the UE.
  Need to be advertised towards the UE, and which information the UE needs to be provisioned with if any.
  Can integrate in the PCC Framework, and which enhancements are required the PCC framework, if any.
Any solutions consider user plane transmission efficiency and are not be limited to work with QUIC traffic only or specific MASQUE deployments (i.e. one or two-proxies).
Proposal is to leave HR roaming scenarios out of scope in this release.

## Slide 24: Study on delegation of (re)selection of target NF across PLMNs

## Slide 25: Outline
NF1
NF2
NFc3
SCPx
vSEPP
SCPy
NFp1
NFp2
NFp3
hSEPP
vPLMN
hPLMN
{ [sbi-target-apiroot] AND/OR
[sbi-discovery-nf-set]} OR
(sbi-discovery-*)
sbi-target-apiroot
3GPP has defined indirect communication via the SCP, allowing for different levels of delegation from the NF (acting as client) to the SCP, of the selection and reselection of the target destination logic.
However, indirect communication via the SCP is not defined across PLMNs, since the NF target is selected in the vPLMN

## Slide 26: Content
Delegation of (re)selection logic from NF to SCP provides some advantages as follows:
  It allows selection is performed closer to the target destination, what provides in some cases a more up to date information about target health and status.
  It allows reselection is performed closer to the target destination, what minimizes signaling path for the retry.
These advantages now are restricted for intra-PLMN interactions, not possible across PLMNs

## Slide 27: Summary
This SID proposes the following objectives
  Identify the implications of having different combinations of communication models between client PLMN and destination PLMN.
  Identify the element(s) in the destination PLMN that is responsible to perform the delegated logic and describe the required capabilities.
  Propose required procedure and interfaces update.

## Slide 28: Study on IMS event exposure framework

## Slide 29: Outline
There are currently no standard defined mechanisms in IMS for an external (to the PLMN trust domain) API invoker to subscribe to specific events related to a specific IMS subscriber / group of IMS subscribers.
The serving IMS NFs (providing / producing said events / data) cannot be dynamically located by the API invoker.
An example of a specific event that can be subscribed to is “IMS user call-state” (e.g., idle, busy, registered etc.).
The objective of the study is to update the IMS reference architecture (i.e., TS. 23.228) to provide a framework whereby external (to the PLMN trust domain) API invokers can dynamically subscribe to IMS events related to a specific IMS subscriber or group of IMS subscribers via subscribe / notify mechanism.

## Slide 30: Content
It is proposed to study the following items in 3GPP R19:
IMS event subscription mechanisms via subscribe / notify procedures to external API invokers,
identify IMS events that can be subscribed to,
locator functionality whereby the IMS NF / IMS NFs serving the specific subscriber(s) for which the specific event was requested is found,
subscribe / notify procedures from the IMS NF / IMS NFs serving the specific subscriber(s) for the requested event,
synergies with the Network Exposure Framework defined in 5GS (e.g., exposure of events to external API invokers via the network exposure function (NEF) from the IMS NF / IMS NFs).
IMS exposure framework
S
AF
S
AF
S
AF
S
IMS NF
S
IMS NF
S
IMS NF
Trust domain
S
Overview

## Slide 31: Summary
Study standard defined mechanisms in IMS enabling an external (to the PLMN trust domain) API invoker to subscribe to specific events related to a specific IMS subscriber / group of IMS subscribers:
  define event subscription mechanism,
  define specific events,
  define locator functionality,
  define synergies with the Network Exposure Framework defined in 5GS (e.g., NEF).

## Slide 32: Study on 3rd party ID

## Slide 33: Outline
There is currently no standard defined mechanisms in IMS to support an operator to enrich calls with 3rd party caller information (like a name card with attached iconography) in the caller network or a mechanism to verify that caller information before it’s presented to the callee.
Use case: An enterprise whishes to present its logo to the callee for calls that is made from its communication system via an operator network.

## Slide 34: Content
It is proposed to study the following items in 3GPP R19:
The objective is to get a solution to KI#1 “How the Originating IMS network signs the 3rd party IDs and terminating IMS network verifies the 3rd party IDs” as outlined in TR 33.890 into normative specifications.
The study should define the architecture of the outlined solution as described in TR 33.890 Solution 1.

## Slide 35: Minimize the number of Policy Associations

## Slide 36: Outline
PCC authorization:
  The SMF determines based on local configuration whether PCC authorization is required for the PDU Session, then requests to establish a SM Policy Association to the PCF.
AM Policies:
  The AMF also determines based on local configuration where AM Policies are needed, this local configuration,
The problem is that some AM and SM Policy Association may be established and maintained until the UE deregisters or the PDU Session terminates, although there are no policies for this SUPI (DNN and S-NSSAI). This impacts performance and increases signalling.
UE Policies:
  The AMF triggers the UE Policy Association using the UE policy container, if not present, then the AMF triggers, based on local configuration, the UE Policy Association Establishment procedure to the PCF to request UE Policies, if any.
The problem is that the AMF triggers the request for UE Policies without knowing if the UE needs UE Policies or not, for example some IoT devices may not need any UE Policies. For those UEs that do not need any UE Policies, the UE Policy Association remains established, that impacts the performance and causes extra signalling between the AMF and the PCF.

## Slide 37: Solution described in the TEI19 WID
Extend Access and Mobility Subscription Data Types used in the Nudm_SubscriberDataManagement Service and defined in TS 23.502 18.1.1 Table 5.2.3.3.1-1.
  New Field: Indication of Access and Mobility Policies enabled.
  Description of the new Field: Indicates if the user has Access and Mobility Policies enabled or not.
  New Field: Indication of UE Policies enabled.
  Description of the new Field: Indicates if the user has UE Policies enabled or not.
Extend Session Management Subscription Data Types used in the Nudm_SubscriberDataManagement Service and defined in TS 23.502 18.1.1 Table 5.2.3.3.1-1.
  New Field: PCC authorization is enabled.
  Description of the new Field: Indicates if the user has PCC authorization enabled for the PDU Session.
DM to include a new explicit indication of whether the UE/SUPI is required/authorized/allowed to receive UE policies, the AMF may be able to infer whether the UE/SUPI is required to receive UE policies based on existing subscription data.

## Slide 38: Solution described in the TEI19 WID
Extend AM Policy Establishment procedure defined in TS 23.502 18.1.1 clause 4.16.1.2
  Step 1, AMF decision is based on local policies and the indication of whether the SUPI has AM Policies enabled.
Extend UE Policy Establishment procedure defined in TS 23.502 18.1.1 clause 4.16.11
  Step 1, AMF decision is based on local policies and the indication of whether the SUPI has UE Policies enabled.
Extend SM Policy Establishment procedure defined in TS 23.502 18.1.1 clause 4.16.4
  Step 1, SMF decision is based on local policies and the indication of whether the PDU Session of this SUPI has PCC authorization enabled.
DM to include a new explicit indication of whether the UE/SUPI is required/authorized/allowed to receive UE policies, the AMF may be able to infer whether the UE/SUPI is required to receive UE policies based on existing subscription data.