## Slide 1: Interconnect of SNPN for Release 19
Novamint, EDF, b<>com, Cisco, Quixoticity

## Slide 2: Outline
Where we are for supporting SNPN:
  From Release 15, several activities have been conducted around NPN and SNPN
  SNPN deployments are expected to rise tremendously in the coming years, especially in locations where there is no suitable public network, to support digitalization of verticals areas of work.
  In several sectors (ports, airports, mainports, utilities, railway…), this will imply multiple deployments of SNPNs with very distinct owners sharing and using the same services (for example, a container port with several container terminals and one generic container exchange route all owned and managed by different players or SNPNs deployed on ships).
  The challenges associated to “interconnect” of SNPNs have not been addressed yet in particular the associated aspects such as security, scalability, continuity of service… and resilience.
  SA1 has initiated a study on “interconnect of SNPN” in Release 19
What is expected:
  Study impacts and define solutions to support Interconnect between several SNPNs
  Study impacts and define enhancements especially in term of security and scalability to support Interconnect of SNPN with identity providers (Credential Holders)

## Slide 3: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Interconnect between SNPNs | Study impacts and define solutions to support Interconnect between several SNPNs Key Work objectives includes the following aspects: Identify key issues and solutions to support interconnect between several SNPNs to ensure service continuity, security resilience… Identify the impacts and the necessary changes for supporting Interconnect between SNPNs for some key enablers | Yes, TR 22.848 | SA2 or SA6 | No | SA3 for security, SA5 for management
2 | Interconnect of SNPN with identity providers | Scalable interconnect between Identity Providers and a large number of Standalone Non-Public Networks (SNPNs) using dynamic connections Key Work Tasks includes: Defining overall architecture and function enhancement to the N32 reference point to allow for scalable and secure on-the-fly establishment of signalling connection between a Standalone Non-Public Network and an Identity Provider, including in presence of Firewall functionality (related to FS_ISN; TR 22.848) | Yes, TR 22.848 | SA3 | No | SA2 for Alignment

## Slide 4: Interconnect between SNPNs
Use cases and requirements addressed under SA1 Release 19 (TR 22.848)
Motivation
  In many sectors, verticals have started to deploy Standalone Non-Public Networks (SNPN) in ports, airports, mainports, utilities, railway, etc.
  This is leading to the emergence of many new use cases where the verticals are confronted with aspects related to the interconnect of SNPNs with different owners, in locations where there is no public network, and where there is a need to deal with security, authorisation, continuity of service, coordination and resilience.
  There is as well the emergence of new use cases of « moving » or deployable SNPNs with the associated challenges to interconnect and coordinate with other SNPNs (examples of coordination between several SNPNs in a naval context or container ship with SNPN on board debarking in different port terminals with SNPNs across the globe)
  There is a need to facilitate the interconnect between the SNPNs for the benefits of the end users and support of vertical services and applications
Areas for study:
  Study impacts and define solutions to support Interconnect between several SNPNs

## Slide 5: Interconnect of SNPN with identity providers
Motivation
  In contrast to PLMNs, there is no administrative entity like the GSMA for helping manage the interconnect between SNPNs and Identity Providers, e.g., by providing a registry of PLMN signalling endpoints.
  SNPN may reside behind a NAT Gateway/Firewall device which prevents inbound subscription requests from Identity Providers who have authenticated their users onto the SNPN
  The Identity Provider may leverage the services of a cloud provider which uses dynamic IP address assignment for the providers signalling endpoints.
  The number of interconnected SNPNs and Identity Providers is expected to be considerably greater than the number of PLMNs today.
  However, because of the limited area covered by an SNPN and the low number of subscribers from an individual identity provider, the number of signalling events between organizations is expected to be considerably less than between PLMNs. Hence, it may not be feasible to maintain permanently established signalling connections between them.
Areas for study:
  Study impacts and define solutions to address scalability and security aspects inherent to interconnect of SNPNs with entities that authenticate and authorize UE access to the SNPNs.
Areas for study:
  Enhancements in term of security and scalability to support Interconnect of SNPN with identity providers (Credential Holders)
Use cases and requirements
addressed under SA1 Release 19
(TR 22.848)

## Slide 6: Summary Interconnect of SNPN
Topics | SA1 requirements | SA impacts | Stage 3 Impacts | Market Relevance
Interconnect between SNPNs | ***** | SA2 / SA6 , SA3, SA5 | CT1, CT4 | HIGH (1)
Interconnect of SNPN with identity providers | ***** | SA3, SA2 | CT4 | HIGH (1) (2)
key capability needed to support commercial deployments planned in the (very) short term
already supported by non 3GPP solutions