## Slide 1: China Mobile’s View on R19 SA2

## Slide 2: Outline
Overview of the SA2 R19
CMCC Interested Topics for R19
Deep Dive of 5 Rel-19 Topics
Suggested Handling of R19 SA2 SI/WI

## Slide 3: Overview for SA2 R19
Based on timeline decision in March SA plenary, the R19 will be a short release in 5G-A era. For SA2, there will be only 15 months for study and normative work.
Less than 15 study items are expected in SA2.
R19 is an important release which may introduce the topic of pre-6G.
These items should be selected based on the learn from deployment of 5G.
  Big impact for industry e.g. TSN，V2X
  Limited because of terminal capability e.g. SSC mode2/3，MBS
  Big impact for operator network evolution e.g. SNPN
  Industry requirement is not clear：Prose

## Slide 4: CMCC Interested Topics for R19
XRM-Enhancement
Integrated Sensing and Communication
NG-RTC
AI for Network and Network for AI
Energy Saving as a Service
SBA enhancement for User Plane (i.e., Exposure……)
Ambient IoT
System enhancement: user plan exposure, Resilience Core, TSC, URLLC, Edge Computing
UAV enhancement
Satellite enhancement
Upper layer Traffic splitting: over multiple 3GPP access
Roaming Value-add service

## Slide 5: Deep Dive of 5 Rel-19 Topics
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | XRM Ph2 | 5G system supports XRM Ph2 requirement and Metaverse service Key Work Tasks includes: Enhancement for PDU Set handling(e.g. QoS parameters, informations, protocols) QoS control enhancement e.g. under the utilization of QUIC, Tethered UE scenario, N6 delay. 5GS Support the optimization in distributed task processing for split rendering. Support Non-3GPP access e.g. L4S, PDU set handling. Support high mobility and large capacity of XR and media service. Support spatial information and digital asset information management. | Yes TS 22.261( WID RMobility), TR 22.856 | SA2 | Yes | SA3 for security, SA4 for media/Meta/XR service
2 | Integrated Sensing and Communications | supports the capabilities to perceive and utilize the information of the surrounding environment and/or the objects within (e.g. shape, size, orientation, speed, location, distances or relative motion between objects, etc.) via NR RF signals. Key Work Tasks: Overall architecture and function enhancement to support new sensing service. Basic functionality for Sensing service exposure, Discovery and selection of the sensing entities, Sensing control parameter generation and provisioning, related QoS/Policy enhancement, Handling of sensing data. E2E signaling interactions to support sensing service including the sensing service initiation, sensing authorization, sensing control, and sensing data report, sensing service continuity. Aspects involving secuity and privacy mechanism, charging and non-3GPP sensing. | Yes TR 22.837 TS 22.261 | SA2 | Yes | SA3 for security, SA5 for charging

## Slide 6: Deep Dive of 5 Rel-19 Topics
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 SI/WI | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | System architecture for next generation real time communication services phase 2 | study the enhancement to the IMS network architecture, interfaces and procedures for the next generation real time communication services requirements on phase 2. Key Work Tasks Overall architecture and function enhancement to support new sensing service. IMS related services enhancements, including supporting standalone data channel, third party ID etc. Interworking, LBO roaming and Data off for data channel applications Exposure of IMS real-time communication capabilities SBA enhancements on CSCF service registration and discovery, service based media plane | Yes TS 22.261 | SA2 | No | SA3 for security, SA5 for charging SA4 for media
4 | Artificial Intelligence (AI)/Machine Learning (ML) for 5GS Service to enable 5GC and Air interface Intelligence | Up to now, 3GPP in RAN and SA2 WGs has studied and/or specified AI-enabled network architecture and leverage Artificial Intelligence (AI)/Machine Learning (ML) to enable 5GC and Air interface Intelligence in terms of data collection, ML model training, analytics inference, and closed-loop procedures by consuming data analytics, etc. Key Work Tasks: AI/ML enabled Use Case(s) of 5GS Service: Detection/prevention/mitigation of signalling storm, NWDAF assisted energy saving and NWDAF assisted policy recommendation. Leveraging AI/ML technologies of 5GS AIML Service: Study whether and how to enhance architecture to support vertical federal learning, online learning and enforcement learning in the 5GC. Support for AI/ML for air interface | No | SA2 | Yes | SA3 for security
5 | Architecture enhancement of supporting Energy Efficiency as service criteria | Architecture enhancement of energy efficiency from systematic perspective, follow SA1 EnergyServ requirements Key Work Tasks- Enhancement on network exposure on energy related information (e.g. energy consumption on NF level, network slice level, network sharing condition, UE level, PDU session level, etc.). New NF for energy saving (e.g. energy consumption evaluation, energy usage adjustment for NF from CN aspect, energy saving related decision making). Enhancement on QoS or SLA parameters to involve EE related requirement. Energy saving triggered network adjustment (e.g. User migration and traffic diversion, timely capacity expansion and reduction, Inter-slice de-routing, slice gating, etc.) | Yes TS 22.261 TR 22.882 consolidation | SA2 | Yes | SA3 for security, SA5 for EE measurement and charging

## Slide 7: XRM Ph2
Scenarios and Motivation
  Further enhancement based on R18 PDU set handling mechanism
  Tethered UE, non-3GPP access scenarios exist in real network, the enhanced QoS control/PDU set QoS control/L4S should be considered.
  Continue to improve network capacity and user experience to support the XRM service, e.g. high mobility scenario, supporting multiple UEs access in the same location.
  Deep cooperation between application and network, to support the precise QoS/PDU Set QoS guarantee e.g. supporting QUIC tranmission
  New service introduction with extending network capability of supporting digital asset management/transmission g e.g. spatial information, avatar data.
Proposed Objectives in R19
  Enhancement for PDU Set handling(e.g. QoS parameters, informations, protocols)
  Support QoS control enhancement e.g. under the utilization of QUIC, within the Tethered UE scenario, N6 delay, fast and efficient QoS control .
  5GS Support the optimization in distributed task processing for split rendering.
  Support Non-3GPP access e.g. L4S, PDU set handling.
  Support high mobility and large capacity of XR and media service.
  5GS enhancement to support spatial information and digital asset information management.

## Slide 8: Integrated Sensing and Communication
Motivation
  The operator can make use of the existing infrastructure for communication to accommodate the requirement for sensing service with cost-effective manner.
  With the advantages of 3GPP network, Integrated Sensing and Communication can meet potential sensing requirements from different industies, including Wide coverage, Native network-wide sensing, Large quantity of sensing devices including NG-RANs/UEs.
  With the integration of sensing, 5GS is able to setup the connection between the physical and digital world, and enable various new services for public and industry customers.
Usage scenario
  32 scenarios have been introduced in SA1, involving 6 aspects: Smart transportation, UAV, Smart living, Smart city, Smart factory, data privacy/security.
  Sensing modes are mainly about gNB-based( single or multiple gNBs) or UE-based( single or multiple UEs) or gNB+UE.
Proposed Objectives in R19
  Study and define the possible architecture and function enhancement to support new sensing service.
  Sensing service exposure to UE, 5GC NF or AF.
  Discovery and selection of the sensing entities, e.g. AMF, NG-RAN, UE.
  Sensing control parameter generation and provisioning for sensing service.
  Handling of sensing data.
  Define E2E signaling interactions to support sensing service including sensing service initiation, sensing authorization, sensing control, etc.
Scenarios
Sensing modes

## Slide 9: Next Generation Real Time Communications
Migration from legacy voice/video communication to next generation Real Time communications is the new chance and revenue stream for both personal and vertical telecommunication market , leveraging operators’ high-quality networks to provide advanced immersive multimedia services, e.g. XR, Metaverse and various web based applications
By Rel-18 NG_RTC WI 3GPP has established overall architecture and procedures for IMS supporting data channel and AR communications, which is a good basis for further enhancements to provide a complete solution to fulfill more requirements from SA1 and the market.
In R19 it is suggested to enhance NG_RTC solution on the following major aspects:
  Enhance IMS media plane architecture, interfaces and procedures to support mobile Metaverse services and IMS based XR services
  IMS related services enhancements, including supporting standalone data channel, third party ID etc.
  Interworking, LBO roaming and Data off for data channel applications
  Expose IMS real-time communication capabilities (audio, video, data channel) to the enterprises/verticals
  Enhancements on service based architecture of IMS, including CSCF registration and discovery, service based media plane architecture

## Slide 10: Artificial Intelligence (AI)/Machine Learning (ML) for 5GS Service to enable 5GC and Air interface Intelligence
Motivation:
  The work of AI/ML for 5GS in Rel-19 is proposed to expand the scope of network AI services to leverage AI/ML technologies to enable 5GC and Air interface Intelligence by providing network automation and improving the efficiency of 5G network architecture.
Usage scenario：
  Up to now, 3GPP in RAN and SA2 WGs has studied and/or specified AI-enabled network architecture and leverage AI/ML to enable 5GC and Air interface Intelligence in terms of data collection, ML model training, analytics inference, and closed-loop procedures by consuming data analytics, etc. Further study is needed or aligned each other in the future, focusing on 3 objectives.
Objective#1: AI/ML enabled Use Case(s) of 5GS Service
Detection/prevention/ mitigation of signaling storm:
NWDAF assisted energy saving
Scenario#3: NWDAF assisted policy recommendation
Objective#2: Leveraging AI/ML technologies of 5GS AIML Service
Vertical federal learning, including UE, RAN, 5GC and AF.
Enhance architecture to support online learning in the 5GC
Enhance architecture to support reinforcement learning in the 5GC
Objective#3: Support for AI/ML for air interface
Terminology alignment btw RAN and SA2
UE data collection framework enhancement to support AI/ML use cases..
ML Model delivery to UE.
Lifecycle management of AI/ML model btw RAN and SA2.
SA2 and RAN Convergence for Model ID/Analytics ID defined in SA2 since R16 eNA and Model ID/feature ID studied/concluded in RAN R18.
Architecture enhancement to support AI based Positioning.
Proposed Objectives in R19

## Slide 11: Energy Efficiency as a Service
Definition | Study the architecture enhancement of energy efficiency from systematic perspective, follow the requirements from SA1 EnergyServ.
Justification | Apart from enhancing network capability on satisfying user experience while achieving energy efficiency from network aspect, it is worth considering how to deliver services with energy efficiency as service criteria, associated with applications’ preferences, and how to support the policy of handling energy as part of a subscription.
Usage scenario | Enhancement on network exposure on energy related information (e.g. energy consumption on NF level, network slice level, network sharing condition, UE level, PDU session level, etc.). New NF for energy saving (e.g. energy consumption evaluation, energy usage adjustment for NF from CN aspect, energy saving related decision making). Enhancement on QoS or SLA parameters to involve EE related requirement. Energy saving triggered network adjustment (e.g. User migration and traffic diversion, timely capacity expansion and reduction, Inter-slice de-routing, slice gating, etc.). All adjustments in QoS or other actions influencing user experience are considered under the scope of pre-configured SLA.

## Slide 12: Suggested Handling of R19 SA2 SI/WI
Start TEI 19 Early, e.g., from Q1 of 2024
Estimate TUs and Set checking points for SI objectives
Get commitment from operators (i.e., at least four) or vertical customers support/involvement for all SIs/WIs, from diversified regions are preferred
Task SA2 provides input of approved 6* R19 SIs/WIs in Q3 as the first package
  (*The number is provided as guidance of SA workshop output)