## Slide 1: Siemens’ view on Rel-19 for Industrial 5G
Michael Bahr
Delegate, Siemens

## Slide 2: Outline
Main Focus in Industrial 5G – using 5G in industrial communications for cyberphysical control applications such as in industrial manufacturing
Corresponding relevant topics – Non-Public Networks, Industrial IoT with Time-Sensitive Communication and URLLC, 5G Virtual Networks, other general topics supporting industrial requirements and deployments
Industrial stage 1 requirements collected in TS 22.104 and TS 22.261
Difficulty for Rel-19: Feedback loop for Rel-16/17 industrial 5G features cannot be closed yet
  Waiting for Rel-16/17 Industrial 5G features becoming supported in hardware
  Please expect more specific feedback relevant for SA2 Rel-19 when available
 Rel-19 Enhancements to several areas (Industrial IoT, Network Exposure/QoS Monitoring, Sidelink, Positioning)

## Slide 3: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | IIoT: Enhance-ments for 5GS as logical bridge (See slide 6 for more details) | Potential enhancements for configuration of logical 5GS bridge and forwarding in the 5G system (modelled as logical (TSN) bridge). Key Work Tasks includes defining - Support of netconf/YANG. Loop prevention/support of spanning tree protocols Potential enhancements for, e.g. dynamic addition of new VN members, large num-bers of VLANs/UEs, multiple VLANS/TSN streams per UE, multiple devices behind UE | TS 22.261, TS 22.104 | SA2 | No | No
2 | IIoT: Improved TSC Time Sync (slide 7) | Smaller 5G time sync budget 700-800 ns with two (2) wireless links on the path of time synchronization messages. |  |  | Yes, major | No
3 | Enhancements for Network Exposure (See slide 9 for more details) | Access to Network Exposure Function (NEF) to be provided at the UE Key Work Tasks includes defining - Access to Network Exposure Function (NEF) to be provided at the UE (provide NEF access via UE’s R reference point to an application, provide AAA framework that bars unauthorised requests to NEF (fine-grained). | EXPOSE, TS 22.261 | SA2 | No | SA3
4 | Sidelink for Industrial Communication (See slide 10 for more details) | Support of direct device communication/NR sidelink communication with Industrial IoT (IIoT) KPIs for IIoT/factory applications in Standalone NPNs Key Work Tasks includes defining - Support of direct device communication/NR sidelink for IIoT/factory applications in standalone NPNs. Support of Industrial IoT (IIoT) KPIs over sidelink (99.999% communication service availability, 1-5 ms max latency, <1 µs time sync accuracy). 5G-VN support, unicast/multicast communication UE-to-UE Relay in case of limited transmission range | eCAV, TS 22.104 | SA2 | Yes | No

## Slide 4: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5 | Enhancements for QoS Monitoring (See slide 9 for more details) | Provision of 5G communication services end-to-end within 5GS, further QoS monitoring enhancements, that enlarge the functionalities of QoS monitoring (includes features, additional monitored parameters) Key Work Tasks includes defining - Provision of 5G communication services end-to-end within 5GS Further QoS monitoring enhancements (functionalities, additional parameters) | EXPOSE, TS 22.261 | SA2 | Minor (RAN-related monitoring) | No
6 | Manipulation-protected Positioning (See slide 11 for more details) | A secure, uncompromised localisation information is important for different vertical applications, so that a reliable position information of a UE can be determined and provided by the 3GPP system. The provided position information needs to be reliable even under attack scenarios where an attacker tries to intentionally manipulate the position information |  | SA2 | Potentially | SA3
7 | Localization Service: Accuracy of UE position (See slide 11 for more details) | Enhancement of localization service output with accuracy of the UE position, to be provided to application at UE. |  | SA2 | Yes | No
8 | IIoT: Distributed TSN Stream Establishment (See slide 8 for more details) | Interworking of 5GS with distributed protocols of IEEE 802.1 networks (e.g. LRP, RAP) in order to support deployments using distributed TSN stream establishment. | eCAV, TS 22.104 | SA2 | No | No (SA3 unknown)

## Slide 5: Enhancements related to Industrial IoT
Integration of Industrial 5G Standalone Non-Public Networks into industrial network architectures
  re-use of functionalities of existing industrial communication networks and processes already deployed and specific to the manufacturing and process industries.
  5G system (both, RAN and CN elements) must fit into industrial network environments.

## Slide 6: Enhancements related to Industrial IoT
Enhancements with respect to 5G system as logical bridge
  Due to delayed availability of hardware with industrial features, practical feedback has not been available yet on this topic
Potential enhancements for
  Configuration of logical 5GS bridge, e.g. support of netconf/YANG, reuse of IDs (VLAN tags, TSN domain identifiers), dynamic addition of new VN members
  Forwarding in the 5G system (modelled as logical (TSN) bridge), e.g. with many VLANs, multiple UEs in VLAN, multiple VLANs/TSN streams per UE, multiple devices behind UE, support of spanning tree protocols/loop prevention

## Slide 7: Enhancements related to Industrial IoT
Improved time synchronization (smaller 5G time sync budget)
  The current required 5G time sync budget of 900 ns leaves only a very small number for further TSN devices outside the 5G system within the overall time sync budget of 1 µs in integrated TSN-5G networks.
  Two manufacturing robots, both connected to the 5G network with a wireless 5G link (two wireless links on the path of the time synchronization messages), require up to 16+4 TSN hops external to the 5G system, resulting in a smaller 5G time sync budget of approx. 700-800 ns.
 stable time synchronization accuracy of the 5G system of 700-800 ns with two (2) wireless links on the path of the time synchronization messages.

## Slide 8: Enhancements related to Industrial IoT
Distributed TSN stream establishment
  Novel manufacturing systems that offer high production flexibility, dynamics, and versatility benefit from distributed establishment of TSN streams.
  large number of increasingly mobile production assets (e.g. AGVs, mobile robots) which are assigned dynamically to received production tasks.
  Respective applications on the involved machinery set up/change necessary communication services via an application-agnostic user-network interface in a distributed, flexible, dynamic way.
Interworking of 5GS with distributed protocols of IEEE 802.1 networks (e.g. LRP, RAP) in order to support deployments using distributed TSN stream establishment.

## Slide 9: Enhancements related to Network Exposure/QoS Monitoring
Access to Network Exposure Function (NEF) to be provided at the UE
  provide NEF access via UE’s R reference point to an application;
  provide AAA framework that bars unauthorised requests (fine-grained).
Further QoS monitoring enhancements
  Enlarge the functionalities of QoS monitoring (includes features, additional monitored parameters)
Provision of 5G communication services end-to-end within 5GS
  Request, modification, and release of communication services must not be contingent on knowledge of internal 5G system parameters/architecture/setup.

## Slide 10: Sidelink enhancements for industrial communication
Support of direct device communication/NR sidelink for IIoT/factory applications in standalone NPNs
Support of Industrial IoT (IIoT) KPIs over sidelink
  99.999% communication service availability;
  1-5 ms max. latency;
  <1 µs clock synchronicity;
  unicast/multicast communication.
  5G-VN support
  UE-to-UE Relay might be supported in case of limited transmission range.

## Slide 11: Enhancements related to Positioning
Enhancement of localization service output with accuracy of the UE position
  to be provided to application at UE.
Manipulation-protected positioning
  A secure, uncompromised localisation information is important for different vertical applications, so that a reliable position information of a UE can be determined and provided by the 3GPP system.
  The provided position information needs to be reliable even under attack scenarios where an attacker tries to intentionally manipulate the position information (considering also attacks on physical layer).

## Slide 12: Summary
Difficulty for Rel-19: Feedback loop for Rel-16/17 industrial 5G feactures cannot be closed yet
  Waiting for Rel-16/17 Industrial 5G features becoming available in hardware
  Expect more specific feedback relevant for SA2 Rel-19 when available
Only individual enhancements on relevant industrial topics provided for Rel-19
  Industrial IoT, 5GS as logical bridge, Network Exposure/QoS Monitoring, Sidelink for IIoT, Positioning
  Might become work tasks in corresponding, suitable SA2 study/work items
Rel-19 expected to further improve industrial 5G, but valuable feedback from Rel-16/17 industrial deployments needed