## Slide 1: Apple’s views on Rel-19 topics in SA2
Apple

## Slide 2: Outline
Considerations for 5G Advanced Ph-2
Overall view on Rel-19 content – Top 10 items
Motivations for Apple proposed SIDs
Further topics of interest

## Slide 3: Considerations
Rel-19 is the second release of 5G-Advanced
  Support advanced new technologies and services
  System and Service Enhancements to 5GS to enable:
    Improved performance
    Signaling / power efficiency
Stage-2 input should consider:
  Stage-1 requirements
  Rel-18 postponed items
  External / vertical requirements, e.g. GSMA, 5GAA, etc.
  Alignments with other SDOs
  Experiences from operator deployments

## Slide 4: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1. | Streamlined ATSSS (See slide 8 for more details) | Simplify and optimize deployment scenarios for ATSSS and to study additional ATSSS enhancements. Key Work Tasks include: Study how the MPQUIC steering functionality can be extended to be able to steer, switch, and split non-UDP traffic (TCP, IP, Ethernet traffic). Study how to relax the mandatory use of IPSec tunnel encapsulation on the untrusted non-3GPP access for the MPQUIC steering functionality, investigate new architectural options for ATSSS, if necessary. Study how to support an MA PDU Session using a Branching Point (IPv6 multi-homing) or an UL Classifier. The UE shall not be required to know whether the MA PDU Session is using an UL Classifier. Study how to support the establishment of an MA PDU Session to a LADN. | No | SA2 | No | SA3 for security, SA5 for charging and OAM impacts
2. | Enhancements to QoS framework (See slide 9 for more details) | Provide enhancements to the 5G QoS framework. Key Work Tasks include: Study how to enhance the 5GS QoS framework including the Packet Filter Set definition and Packet Flow Description to be able to identify QUIC streams and provide differentiated QoS for different QUIC streams within the same PDU session. Proposed solutions shall be based on IETF protocols or extension of such protocols, if available in IETF. Study how to enhance Reflective QoS to create packet filters for QUIC streams based on the enhanced 5GS QoS framework. Study how to relax the per-packet processing requirements for Reflective QoS so that the UE can sustain higher throughput for the SDF. Study how to extend the UE capability signalling for Reflective QoS to indicate ability to handle different transport protocols. | No | SA2 | Maybe | SA3 for security, SA4 for media aspects

## Slide 5: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3. | Enhancement of 5G UE Policy; Phase-2 (See slide 10 for more details) | Optimize the UE Policy requesting and provisioning procedures. Key Work Tasks include: Study how to optimize the UE Policy provisioning procedures to ensure that the UE policy provisioned to the UE are enforceable by the UE. Study whether new triggers are needed for UE Policy provisioning procedure and whether procedures other than initial Registration and Mobility Registration Update (when UE moves from EPS to 5GS) can be used to provision the UE Policy. | No | SA2 | No | No
4. | MASQUE for Enhanced Traffic Management | Use of MASQUE technology to enhance 5GC Traffic management capabilities. Evaluate whether ATSSS MASQUE proxy in UPF should be generalized in Rel-19. Key Work Tasks include: Study whether and how MASQUE capabilities in the 5GC user plane can benefit the 5GS Traffic management by explicit information exchange on fully encrypted traffic. The study identifies the relevant information that would be exposed. Study whether and how MASQUE capabilities in the 5GC user plane can benefit other 5GC functions like reporting of user plane data as input to analytics or to monitor the correct URSP enforcement in the UE. Study how to advertise MASQUE capabilities towards the UE, and which information the UE needs to be provisioned with if any. Study how to integrate in the PCC Framework, and which enhancements are required the PCC framework, if any. | No | SA2 | No | SA3 for security

## Slide 6: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5. | Further enhancements for XR services and Metaverse | Further enhancements to Rel-18 defined PDU Set handling and UE power savings. Address new Rel-19 requirements from SA1 on Mobile Metaverse Services. Key Work Tasks include: Study enhancements for PDU Set handling, PDU Set identification on N6 for RTP streams with encrypted RTP headers, Support more protocols besides RTP/SRTP, e.g. HTTP/DASH, QUIC. Study enhancements to support non-3GPP access, L4S in non-3GPP access, PDU set related QoS control mechanism extended into non-3GPP access. Study improvements to Uplink QoS and power saving for XRM. Study Multi-Access support, MA-PDU session for XRM, impact of multi-path protocols over end-to-end congestion control (L4S). Support of enhanced XR-based services for Mobile Metaverse Services. | Partially in TR 22.856 (SID: SP-220353) (WID: SP-230509) | SA2 | Maybe | SA3 for security, SA5 for charging, SA4 for media aspects
6. | Upper layer traffic steering, switching and splitting over dual 3GPP access | Enhance the 5G system architecture to address how an MA PDU Session can simultaneously support two 3GPP access paths. Key Work Tasks include: Study how to select the second PLMN or SNPN in case of different 3GPP networks after an initial PLMN was selected for the UE. Study how to enhance registration and session management procedures. The UE can be registered to a single PLMN, to a single SNPN, to two different PLMNs or SNPNs, or to one PLMN and one SNPN. Study how to support mobility between a PDU Session with single 3GPP access and a MA PDU Session with dual 3GPP access as well as between MA PDU Sessions with dual 3GPP accesses. Study the necessary enhancements to support mobile originating and terminating services (e.g., mobile data, voice, SMS, LCS) when the UE is registered to the 5GC network simultaneously via multiple NR accesses and potentially one non-3GPP access. Study how to extend policies, steering functionalities and steering modes. | Yes, TR 22.841 (SID: SP-220445) | SA2 | Maybe | SA3 for security, SA5 for charging and OAM impacts

## Slide 7: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
7. | System Architecture enablers for AI/ML Radio | Study how the 5G System can be enhanced to enable AI/ML Radio. Key Work Tasks include: Study how to support a common 5GS AI/ML framework to enable AI/ML Radio. Study how to enhance existing UE data collection framework to meet requirements for AI/ML model training (for RAN). Study how to support model transfer/delivery to the UE. Study how to support for security and privacy aspects on data collection and model transfer/delivery to UE. | No | SA2 | Yes, major | SA3 for security, SA4 for data collection aspects, RAN WGs for data collection and model transfer/delivery aspects
8. | Emergency SMS over IMS | Study the architectural evolutions of the 3GPP System to support Emergency SMS over IMS for EPS and 5GS. Key Work Tasks includes include: Study how an SMS is routed to an emergency centre serving the UE location, including in roaming case. Study whether IMS emergency registration is used. Study how the emergency service is identified in the IMS signalling. Study how to support SMS to emergency response centre without a USIM/ISIM. Study how the response SM is handled. | Yes, TS 22.101 (WID: SP-220438) | SA2 | No | CT1

## Slide 8: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
9. | Integration of satellite in 5GS Phase-3 | Further 3GPP enhancements to 5GS to support satellite access based on the new use cases introduced in TR 22.865. Key Work Tasks include: Regenerative payload generic architecture study. Study the core network impacts on interfaces, protocols (mobility management, paging) of having “flying” embedded 3GPP functions. Support discontinuous feeder link connection. Study specific impacts on interfaces and protocols of the Store and Forward communication scheme, for both 4G and 5G. Study enhancements to mobility management for discontinuous satellite coverage, paging, handover optimization for regenerative mode UE-satellite-UE communication for 5GS. Study activation of UE-satellite-UE communication, impacts on session management, charging, possibly regulatory services. | Yes, TR 22.865 SID: SP-220679 WID: SP-230516 | SA2 | Yes | SA3 for security, SA5 for charging and OAM impacts, RAN WGs for RAN aspects
10. | Integrated Sensing & Communications | 5G system support for NR-based sensing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g., shape, size, orientation, speed, location, distances or relative motion between objects, etc.) using NR RF signals. Key Work Tasks includes include: Study overall architectural enhancements, required functionalities and procedures to support sensing service. Study QoS model and Policy enhancements to support diverse sensing services Study sensing service authorization and exposure mechanisms of sensing results to trusted third parties Study architectural enhancements and procedures required to support non-3GPP sensing data and related functionality | Yes, TR 22.837 SID: SP-220717 WID: SP-230507 | SA2 | Yes, Major | SA3 for security, SA5 for charging and OAM impacts

## Slide 9: Streamlined ATSSS
Motivations
  Ease ATSSS deployment burden, enable the MPQUIC steering functionality to steer, switch, and split any type of traffic (TCP, IP, Ethernet traffic)
    MPTCP steering functionality can be made optional
  Relax the mandatory requirement of IPSec tunnel encapsulation on the non-3GPP access for the MPQUIC steering functionality
    Study new architectural options for ATSSS
  Complete deferred ATSSS features
    MA PDU Session using a Branching Point or UL Classifier
    Enable ATSSS support when the UE accesses services in LADNs

## Slide 10: Enhancements to QoS framework
Motivations
  QUIC has been adopted for many low latency applications, efficient support of QoS for QUIC streams is becoming increasingly important
    5GS is not equipped to provide QoS for QUIC streams efficiently due to encryption in the header that prevents 5GS to provide differentiated QoS for different QUIC streams
  Reflective QoS is currently controlled on a per-packet basis by using the Reflective QoS Indication (RQI)
    High processing and memory requirements for a UE implementation. UE needs to extract and parse the IP/TCP/UDP/ESP headers to check whether this is a new or existing SDF
  Reflective QoS support for IPSec and other transport protocols (e.g., QUIC) depends on UE’s capability
    UE may have different capabilities for handling various transport protocols in an IP PDU Session. The network is not aware of UE capability for RQoS in this level of details

## Slide 11: Enhancement of 5G UE Policy; Phase-2
Motivations
  Based on Rel-15 5GS UE Policy provisioning design, the PCF provisions the UE Policy even if the UE cannot enforce such policy.
    If the UE does not recognize a URSP rule (e.g. due to not recognizing the Traffic descriptor of the URSP rule), the UE simply ignores the URSP rule without any notification to the network
    5GC needs to ensure that the URSP rules provisioned to the UE are enforceable. With enforceable URSP rules, the mechanisms that allow 5GC to determine when the UE enforces the URSP rules can also be followed efficiently
  The UE triggered UE Policy provisioning procedure is today defined for initial Registration in 5GS or Mobility Registration Update when UE moves from EPS to 5GS.
    When the URSP is missing or invalid, the UE can only use the initial Registration procedure to retrieve the URSP, which will interrupt ongoing sessions not relying on URSP
    Procedures other than initial Registration and Mobility Registration Update (when UE moves from EPS to 5GS) should be also allowed to provision the UE Policy

## Slide 12: Further topics of interest (1/2)
5G support for Femto (HgNB)
  Study overall architecture and required functional and procedural impacts for supporting 5G Femto deployments
  Study how to support the 5G Femto access control mechanism based on the existing CAG concept
  Study how to enable provisioning of subscribers allowed to access 5G Femto cells
  Study how to manage 5G Femto access control by the CAG owner or an authorized administrator
Enhancements in handling of Radio Capabilities
  Identify how to prevent a UE to access a specific RAT/system in which it does not have subscription and therefore will be rejected
  Study how to transfer the radio capability container or UE Radio Capability ID between AMF and MME (and vice versa) in order to avoid retrieval of radio capabilities from the UE from the target system

## Slide 13: Further topics of interest (2/2)
5G enhancements for IP routing
  Study enhancements for enabling connectivity to the same IP subnet/prefix reachable via multiple UEs
  Study enhancements of 5GS to act as an IP router including support of IP routing protocols
  Study enhancements for explicit IP route selection and steering influenced by an AF
ProSe direct/indirect communication for IIOT and private networks
  Identify whether and how enhancements are needed (incl. configuration of UEs, PC5 QoS enhancements) for conveying deterministic communication streams via a ProSe Direct/Indirect Communication, supporting clock synchronization between a group of UEs

## Slide 14: Summary
New features
System Architecture enablers for AI/ML Radio Integrated Sensing and Communication
System and Service Enhancements
Streamlined ATSSS Enhancements to QoS framework Enhancement of 5G UE Policy; Phase-2 MASQUE for Enhanced Traffic Management Further enhancements for XR services Upper layer traffic steering, switching and splitting over dual 3GPP access Integration of satellite in 5GS Phase-3 Emergency SMS over IMS