## Slide 1
TSG CT WG4 Chairman
Nigel Berry (Alcatel-Lucent)
CT WG4 Status Report to TSG CT #67
3GPP TSG CT Plenary Meeting #67 CP-150142
Shanghai, PR China; 9 – 10 March 2015 Revision of CP-150010

## Slide 2: TSG CT WG4 Organisation
Meetings
  CT4 has had one meeting since the last CT plenary:
    CT4#68 (Sorrento), co-located with CT1, CT3 and CT6. The Meeting Report is in CP-150011.
  CT4 will have two meetings during next plenary cycle:
    CT4#68bis (Bratislava);
    CT4#69 (Sanya).
TSG CT WG4 officials are:
  Chairman:
    Nigel Berry (Alcatel-Lucent / ETSI)
  Vice chairs:
    Lionel Morand (Orange / ETSI)
    Yvette Koza (Note)
    (DT / ETSI)
  MCC support:
    Kimmo Kymäläinen
Legend Blue – (re)elected since previous plenary Red – for (re)election in coming plenary period
Notes: 2

## Slide 3
TSG CT WG4 Statistics
TSG CT WG4 statistics:
  106 Change Requests agreed
  Rel-13 Work Items / Study Items approved
    2 new Work Item(s)
    1 revised Work Item(s)
    1 endorsed Work Item(s)
  0 Rel-13 TRs for approval
  0 Rel-13 TSs for approval
  CT4#68:
    104 Registered Participants
    ~69 Participants Attending

## Slide 4
Rel-13 WIs Status – CT4 Led
voE_UTRAN_PPD-CT4 0% => 100%
RTCP_MUX-C4 100%
SHARED_SubData_UPD 0% => 50%
PCSCF_RES_WLAN-CT4 5% => 30%
FS_DLoCME 5% => 10%
FS_EPC_SIG_RACE 0% => 20%
Legend Blue – new since previous plenary
Green – progressed since previous plenary

## Slide 5
Rel-13 WIs Status – CT4 Supported
UPCON-DOTCON-CT4 20% => 50%
E2EMTSI-CT4 0%
QOSE2EMTSI-CT4 0%
ePCSCF_WLAN-CT4 0% => 100%
WSR_EP-CT4 0%
ISAT 90%
Legend Blue – new since previous plenary
Green – progressed since previous plenary

## Slide 6
Rel-12 WIs Status – CT4 Led
IMS_TELEP-CT4 0% => 100%
FS_SHARED_SubData_UPD 85% => 100%
Legend Blue – new since previous plenary
Green – progressed since previous plenary

## Slide 7
Rel-12 WIs Status – CT4 Supported
IMS_WebRTC-CT4 80% => 100% (CT1 Led)
Legend Blue – new since previous plenary
Green – progressed since previous plenary

## Slide 8: Agreed New WIs
CP-15 | New WIDs | Rapporteur
0012 | WID Rel-13 New WID on CT aspects of EVS in 3G Circuit-Switched Networks | Qualcomm Incorporated
0014 | WID Rel-13 New WID on CT4 Aspect of WebRTC Data Channel on IMS Access Gateway | China Mobile, Huawei

## Slide 9: Agreed Revised WIs
CP-15 | Agreed Revised WIDs | Rapporteur
0013 | WID Rel-13 Revised WID on Shared Data Update | Huawei

## Slide 10: Endorsed WIs
CP-15 | Endorsed WIDs | Rapporteur | Notes
0091 | Rel-13 Revised WID on IMS Signalling Activated Trace (ISAT) | Vodafone | CT1 led

## Slide 11: Technical Reports for Approval
CP-15 | Technical Reports agreed to be sent to Plenary for Approval

## Slide 12: Technical Specifications for Information and Approval
CP-15 | Technical Specifications agreed to be sent to Plenary for Information and Approval

## Slide 13: CT4 Issues for CT Plenary
CT4 completed the specification of the Rel-12 work items which were not completed at CT#66, for IMS Telepresence and CLUE data channels in particular.
CT4 is now actively involved in Rel-13 work. CT4 made progress in the design of the new NqAP interface for UPCON, completed the specification of the GTPv2 extensions for Voice over E-UTRAN Paging Policy Differentiation and started 3 studies on P-CSCF restoration for WLAN, EPC signalling improvements for race conditions, and Diameter Load Control.
The number of pre-Rel-12 corrections is now decreasing very noticeably.
CT4 has been using the new 3GPP Ultimate Portal to allocate TDocs and CR numbers. Feedback is largely positive in general (no problems encountered before the meeting, some delay during the meeting for the CT4 officials to assign revisions due to some missing functionalities).

## Slide 14: Incoming liaisons to CT plenary
None

## Slide 15: CRs for Conditional Approval (CT4)
TSG_tdoc | C4 Tdoc | Work_item | Title | Spec | CR | R | Cat | Rel | Agenda | Other specs affected
15 | C4-150344 | TEI9 | Renaming of Location-Type AVP | 29.230 | 0444 | 1 | F | Rel-9 | 9.19.1 | 29.172-0028
15 | C4-150357 | TEI9 | Renaming of Location-Type AVP | 29.230 | 0445 |  | A | Rel-10 | 9.19.1 | 29.172-0029
15 | C4-150358 | TEI9 | Renaming of Location-Type AVP | 29.230 | 0446 |  | A | Rel-11 | 9.19.1 | 29.172-0030
15 | C4-150359 | TEI9 | Renaming of Location-Type AVP | 29.230 | 0447 |  | A | Rel-12 | 9.19.1 | 29.172-0031
18 | C4-150334 | TEI11 | Location reporting in emergency 1xSRVCC | 29.230 | 0436 | 1 | F | Rel-11 | 8.29.1 | 29.172-0026
18 | C4-150335 | TEI11 | Location reporting in emergency 1xSRVCC | 29.230 | 0437 | 1 | A | Rel-12 | 8.29.1 | 29.172-0027
25 | C4-150302 | TEI12 | ULI change reporting upon inter-RAT mobility | 29.274 | 1567 | 1 | F | Rel-12 | 7.3.1 | 23.401-2820, 23.060-1947
25 | C4-150304 | TEI12 | ULI change reporting upon inter-RAT mobility | 29.274 | 1568 | 1 | A | Rel-13 | 7.3.1 | 23.401-2821, 23.060-1948

## Slide 16: CRs for Conditional Approval (CT4)
TSG_tdoc | C4 Tdoc | Work_item | Title | Spec | CR | R | Cat | Rel | Agenda | Other specs affected
27 | C4-150139 | IMS_WebRTC-CT | IMS WebRTC reference updates | 23.334 | 0076 | 1 | F | Rel-12 | 7.2.5 | 24.229-5198
27 | C4-150143 | IMS_WebRTC-CT | IMS WebRTC reference updates | 23.334 | 0077 | 1 | F | Rel-12 | 7.2.5 | 24.229-5199
27 | C4-150140 | IMS_WebRTC-CT | IMS WebRTC reference update | 29.334 | 0084 | 1 | F | Rel-12 | 7.2.5 | 24.229-5198
27 | C4-150141 | IMS_WebRTC-CT | IMS WebRTC reference update | 29.334 | 0085 | 1 | A | Rel-13 | 7.2.5 | 24.229-5199
28 | C4-150381 | ProSe-CT | Location update trigger | 29.230 | 0440 | 2 | F | Rel-12 | 7.2.4 | 29.345-0020
28 | C4-150367 | ProSe-CT | Title AVP codes allocation for Validity related AVPs for TS 29.345 | 29.230 | 0441 | 1 | F | Rel-12 | 7.2.4 | 29.345-0012
28 | C4-150369 | ProSe-CT | Code allocation for the Integrity Check aspect AVPs | 29.230 | 0443 | 1 | F | Rel-12 | 7.2.4 | 29.345-0014
28 | C4-150365 | ProSe-CT | Introduction of Authorized Discovery Range Indication for announcing UE | 29.345 | 0015 | 2 | B | Rel-12 | 7.2.4 | 29.344-0012 (Revised to CP-150149)
37 | C4-150276 | TEI13 | MBMS Alternative IP Multicast Distribution Address | 23.008 | 0437 | 1 | B | Rel-13 | 6.3.1 | 23.246-0391, 29.274-1547
37 | C4-150275 | TEI13 | MBMS Alternative IP Multicast Distribution Address | 29.274 | 1547 | 3 | B | Rel-13 | 6.3.1 | 23.246-0391

## Slide 17: CRs to Plenary
CRs agreed at: CT4#68
  Rel-8 = 1
  Rel-9 = 2
  Rel-10 = -
  Rel-11 = 4
  Rel-12 = 54
  Rel-13 = 18
  No mirror CRs are included in these figures
  Rel-8 to Rel-11 CRs are under FASMO acceptance, i.e. CRs that solve Frequent and Serious Mis-operation Only are accepted. Rel-12 is still slushy expected FASMO CRs only June 2015.

## Slide 18: Rel-13 Overview
6.1.2 CT aspects of voice over E-UTRAN Paging Policy Differentiation [voE-UTRAN_PPD-CT]
  GTPv2 has been extended to include a new Paging Policy Indication in the Downlink Data Notification message, which contains a copy of the DSCP in the TOS (IPv4) or TC (IPv6) information received in the IP payload of the GTP-U packet from the PGW. See C4-150218.

## Slide 19: Rel-13 Overview
6.1.3 P-CSCF Restoration Enhancements with WLAN [PCSCF_RES_WLAN]
  P-CRs propose, for UEs with an IMS PDN connection established in WLAN and affected by a P-CSCF failure/restart:
  a basic P-CSCF restoration procedure, whereby the PGW initiates a PDN disconnection towards the UE upon being notified by the HSS/3GPP AAA Server about the need to restore the user's IMS PDN connection;
  an enhanced P-CSCF restoration procedure for UEs accessing a Trusted WLAN in the Multi-Connection Mode and for UEs accessing an untrusted WLAN, whereby the PGW maintains the user's IMS PDN connection and signals to the UE, via this PDN connection, a list of P-CSCF addresses, leading the UE to re-register to IMS using this PDN connection.
  No enhanced P-CSCF restoration procedures will be defined for UEs accessing a Trusted WLAN in Single Connection Mode or Transparent Single Connection Mode.
It has not been decided yet how to pass the new parameters (UE support flag, P-CSCF addresses) over IKE v2.
The latest version of the TR is available in C4-150327.

## Slide 20: Rel-13 Overview
6.1.4 Diameter Load Control Mechanisms [DLoCME]
The P-CRs on scope, IETF requirements and 3GPP network implications for the HSS case were agreed.
Regarding the HSS case, two points are to be further considered. Given the number of Diameter applications / interfaces with HSS, it is FFS whether to consider the load information is per application within a node or the load information is per node. The other point that is being considered is the HSS selection and the associated load balancing.

## Slide 21: Rel-13 Overview
6.1.5 Study on EPC Signalling Improvement for Race Scenarios [FS_EPC_SIG_RACE]
CT4 has started to analyse the following scenarios:
  whether/how to clean hanging PDN connection contexts in PGW when SGW receives a new Create Session Request from MME/SGSN which collides with an existing PDN connection context served by a different PGW;
  handling of a new IP-CAN session establishment request at the PCRF which collides with an existing IP-CAN session context for the same UE and APN served by a different PGW;
  overlapping transactions in the network, when the MME/SGSN (or TWAN/ePDG) repeats a Create Session Request via an alternative PGW due to transport or processing delay in the network.
The latest version of the TR 29.811is available in C4-150342.

## Slide 22: Rel-13 Overview
6.2.1 User Plane Congestion [UPCON-DOTCON-CT]
CT4 is pursuing the definition of the new NqAP protocol/interface between the RCAF and MME. Several open points require further study:
  whether the MME/SGSN should return at least one response to the RCAF for each request (or if no response is returned if no subscriber / APN needs to be reported)
  whether the MME should return an explicit status in the response message for eNB/ECGI w/o active subscribers, if the MME reports subscribers for other eNB/ECGI.
  whether the SGSN should return an explicit status in the response message for IMSI without active APN, if the SGSN reports APNs for other IMSIs.
  whether a Push mechanism is additionally needed (i.e. RACF subscribing to periodic reports from MME/SGSN for certain eNB/ECGIs or IMSIs).

## Slide 23: Rel-12 Overview
7.1.4 CT aspects of Extended IMS media plane security [eMEDIASEC-CT]
Work item is 100% completed. There's one missing piece, the lack of signalling of PSK information across Mp, which requires firstly an update of the ITU-T H.248.90 TLS session negotiation package by ITU-T.
Furthermore, there's TLS and DTLS terminology related clarifications on-going between ITU-T Q.3/16 and IETF WG TLS (SA3 was contacted, too). Based on these semantic clarifications, a revision of H.248.90 (TLS) and H.248.93 (DTLS) is expected, with the goal in getting a more precise model concerning the distinction between (D)TLS session and (D)TLS connection level, as well as (D)TLS protocol procedures related to renegotiation and resumption.
These results will be useful for WEBRTC and the progress of DTLS-SRTP and DTLS usage for WebRTC data channels.

## Slide 24: Rel-12 Overview
7.1.12 P-CSCF restoration enhancements [PCSCF_RES]
CT4 agreed a CR against TS 23.380 to add the option for the S-CSCF to trigger again a P-CSCF restoration when terminating requests are received for a UE after a previous P-CSCF restoration failed, e.g. due to the UE being temporarily out of coverage (C4-150320).

## Slide 25: Rel-12 Overview
7.1.13 Study on Shared Data Update for Multiple Subscribers [FS_SHARED_SubData_UPD]
A CR to TS 29.328 introduced an informative annex for the description in TS 29.364 of a possible solution (cf. TR 29.854) to avoid a massive amount of update operations for shared data over the Sh interface. The description of the solution in TS 29.364 is expected at the next meeting.
A CR addressed the partial failure case, where, if the service node cannot identify or mark or update all the users impacted by the shared data update, a DIAMETER_UNABLE_ TO_COMPLY is returned.
From the TR analysis, a CR concluded that it is not required to create a new mechanism for Shared data update over Cx, which was not added in the normative WI.
For S6a/d, the discussion on cost versus benefit (as for the previous CR) did not drive to recommend a solution. It was only concluded that the existing Reset procedure without modifications can be used to update shared data impacting all users belonging to either a single HSS or a single UDR or UDRs when the UDC architecture is applied.

## Slide 26: Rel-12 Overview
7.1.17 Diameter Overload Control mechanisms [DOCME]
The reference to the version 07 of the IETF draft-ietf-dime-ovli-04 was updated in TS 29.345. The same update should also be made in other specs.

## Slide 27: Rel-12 Overview
7.1.18 Dual Connectivity for LTE [LTE_SC_enh_dualC-CT]
CT4 noted an incoming RAN3 LS regarding how to handle bearers which fail to be switched across eNBs during an E-RAB modification procedure. CT4 agreed that in any case, there is no need for new GTP-C cause codes over S11/S4 for Dual Connectivity. CT4 will follow the outcomes of the on-going exchanges between SA2 and RAN3, but no CT4 impact is anticipated.

## Slide 28: Rel-12 Overview
7.2.4 Proximity Services [ProSe]
The ProSe Service Authorization Procedure (TS 29.345) was modified to:
  reverse the direction of message flow from the HPLMN to the VPLMN/local PLMN according to stage 2;
  correct the wrong AVP "ProSe-Permission-List";
  add Authorization policy’s validity-time AVPs for each ProSe direct service allowed.
The ProSe Match Report Procedure (TS 29.345) was modified by introducing a new ProSe-App-Code-Info AVP to contain ProSe-App-Code, MIC and UTC-based counter.
The Authorised discovery range for announcing per PLMN is added as subscription data in the ProSe-Allowed-PLMN AVP in TS 29.344 and is also transferred in the Prose Service Authorization Answer in TS 29.345.
A set of location update related AVPs are added to the Prose Proximity Request in TS 29.345.
In TS 23.003, the format of the ProSe Application Code is updated to indicate the exact format of the PLMN ID part, the introduction of a spare bit and the length of the temporary identity which is equal to either 160 bits (E=1) or 180 bits (E=0).

## Slide 29: Rel-12 Overview
7.2.5 IMS WebRTC [WebRTC]
A few CRs were agreed to update some IETF draft references. See the new Rel-13 WI on WebRTC_DC_C4 for H.248 control of WebRTC data channels.

## Slide 30: Rel-12 Overview
7.2.7 IMS based Telepresence [IMS_TELEP]
The final piece for a complete telepresence solution is given by the CLUE data channel in order to carry the CLUE protocol between a UE and the MRFP/MRFC. This objective was the primary goal of this meeting and technically challenging due to some dependencies on the still on-going H.248 and IETF products. The CLUE data channel represents an application specific instantiation of a "WebRTC data channel", hence there's a tight relation between WebRTC and Telepresence.
The finally agreed solution for Rel-12 represents a minimum, basic solution. The majority of discussions were related to the identification of all boundary conditions and assumptions, which were incorporated as explicit sections in stage 2 (TS 23.333; see new subclause "5.xx.2 Characteristics of the Telepresence support").
There were also quite extensive discussions whether IMS_TELEP has some impacts again on the IMS-AGW when the CLUE data channel traffic is routed via an IMS-AGW.
The results of that "impact analysis" are not yet documented but they should be added at a later point in time to the Iq profile.

## Slide 31: Acknowledgements
The Chairman wants to thank
  the delegates for their dedication, hard work and the willingness to be cooperative which resulted in fair discussions and achieved excellent results.
  Lionel Morand and Yvette Koza for expertly taking care of the parallel sessions.
  to my MCC support, Kimmo Kymäläinen, for providing wonderful assistance during and between the meetings.
  Finally, the hosts of our meetings, for the chance to visit the beautiful Sorrento and Amalfi Coast.

## Slide 32: Thank You
32
32
Nigel Berry
3GPP TSG CT WG4 Chairman
+44 7880 786 684
nigel.berry@alcatel-lucent.com