## Slide 1
TSG CT WG4 Chairman
Nigel Berry (Alcatel-Lucent)
CT WG4 Status Report to TSG CT #69
3GPP TSG CT Plenary Meeting #69 CP-150420
Phoenix, USA; 14 – 15 September 2015 Revision of

## Slide 2: TSG CT WG4 Organisation
Meetings
  CT4 has had one meeting since the last CT plenary:
    CT4#70 (Vancouver), co-located with CT1, CT3 and SA6;
      The Meeting Report is in CP-150421.
  CT4 will have two meetings during the next plenary cycle:
    CT4#70bis (Belgrade) co-located with CT1 and CT3;
    CT4#71 (Anaheim) co-located with all CT, RAN, SA and GERAN WGs
TSG CT WG4 officials are:
  Chairman:
    Nigel Berry (Alcatel-Lucent / ETSI)
  Vice chairs:
    Lionel Morand (Orange / ETSI)
    Yvette Koza (DT / ETSI)
  MCC support:
    Kimmo Kymäläinen
Legend Blue – (re)elected since previous plenary Red – for (re)election in coming plenary period
Notes: 2

## Slide 3
TSG CT WG4 Statistics
TSG CT WG4 statistics:
  84 Change Requests agreed
  Rel-13 Work Items / Study Items approved
    3 new Work Item(s)
    2 revised Work Item(s)
    5 endorsed Work Item(s)
  0 Rel-13 TS/TRs for approval
  0 Rel-13 TSs for information
  CT4#70:
    XX Registered Participants
    ~69 Participants Attending

## Slide 4
Rel-13 WIs Status – CT4 Led
voE_UTRAN_PPD-CT4 100%
RTCP_MUX-C4 100%
EVSoCS-CT 95%
SHARED_SubData_UPD 95% => 100%
PCSCF_RES_WLAN-CT4 75% => 85%
FS_DLoCME 10%
WebRTCH248DC 10% => 20%
FS_EPC_SIG_RACE 80% => 95%
MONTE-CT 5% => 50%
MEI_WLAN 40% => 90%
FS_SCCAS_RES 5% => 20%
SDPCN_IMS 0% => 5%
Legend Blue – new since previous plenary
Green – progressed since previous plenary
HLcom-CT 0% => 80%
GROUPE-CT 0% => 80%
ROI-CT 0% => 5%
FS_eSDU 0% => 20%
EPC_SIG_RACE 0% => 95%
DECOR-CT 0% => 70%
FS_DBPU 0%

## Slide 5
Rel-13 WIs Status – CT4 Supported
UPCON-DOTCON-CT4 90% => 100%
QOSE2EMTSI-CT4 0%
ePCSCF_WLAN-CT4 100%
WSR_EPS 0%
ISAT 90%
eProSe-EXT-CT 0% => 10%
NBIFOM-CT 0% => 20%
AESE-CT 0% => 40%
SEW1-CT 0%
eDRX-CT 0% => 40%
MCPTT-CT 0%
Legend Blue – new since previous plenary
Green – progressed since previous plenary
eWebRTCi_CT 0%

## Slide 6: Agreed New WIs
Tdoc CP-15# | Tdoc Title | Source | Notes
0424 | WID new Rel-13 New WI on EPC Signalling Improvements for race scenarios | Huawei | WI EPC_SIG_RACE CT4 led.
0423 | WID new Dedicated Core Networks CT aspects | Huawei, NTT DOCOMO, NEC, Ericsson | DÉCOR-CT CT4 led.
0426 | WID new New SID on Impacts of the Diameter Base Protocol Specification Update | Huawei | FS_DBPU CT4 led.

## Slide 7: Agreed Revised WIs
Tdoc CP-15# | Tdoc Title | Source | Notes
0422 | WID revised Rel-13 WID on Monitoring Enhancements CT aspects | Huawei | WI MONTE-CT CT4 led.
0425 | WID revised Rel-13 CT Aspects of Video Enhancements by Region-of-Interest Information Signalling | Intel Corporation | ROI-CT CT4 led.

## Slide 8: Endorsed WIs
CP-15xx | WIDs Endorsed |  | 
1411 | WID new New WID on CT aspects of Support of Emergency services over WLAN – phase 1 | Alcatel-Lucent, Alcatel-Lucent Shanghai Bell | SEW1-CT CT1 led.
1370 | WID revised Rel-13 Revised WID on CT aspects of IP Flow Mobility support for S2a and S2b Interfaces (NBIFOM) | ZTE Corporation | NBIFOM CT1 led.
1408 | WID new CT aspects of extended DRX cycle | QUALCOMM Incorporated | WI eDRX-CT CT1 led.
1359 | WID new New WID on Mission Critical Push To Talk over LTE protocol aspects | Alcatel-Lucent, Alcatel-Lucent Shanghai Bell | MCPTT-CT CT1 led.
1410 | WID new enhancements to WebRTC interoperability stage 3 | China Mobile | eWebRTCi_CT CT1 led

## Slide 9: Technical Reports and Specifications for Approval

## Slide 10: Technical Reports for Information

## Slide 11: CT4 Summary for CT Plenary
CT4 has agreed or endorsed 10 new Rel-13 Work Items and has just started stage 3 work for several of them.
Good progress has been made on many work items: IMEI signalling over WLAN, EPC Signalling Improvements for Race scenarios, P-CSCF Restoration for WLAN access, High Latency Communications, Monitoring enhancements and Architecture Enhancements for Service Capability Exposure.
CT4 has not agreed yet on the protocol to retain over the new T6a/T6b reference points between the MME/SGSN and the SCEF (Service Capability Exposure Function). A conference call will take place after CT#69 to decide between HTTP Rest, Diameter or a TLV based application protocol.
Dedicated Core Networks raised system-wide questions and comments, which also require further offline discussion (some aspects may require some stage 2 updates).
CT4 is going to start a new study, in cooperation with CT3 and SA5, to analyse the impacts of the latest IETF Diameter Base Protocol specification on the 3GPP Diameter based interfaces.

## Slide 12: Incoming liaisons to CT plenary
None

## Slide 13: CRs for Conditional Approval (CT4)

## Slide 14: CRs to Plenary
CRs agreed at: CT4#70
  Rel-8 =
  Rel-9 =
  Rel-10 =
  Rel-11 =
  Rel-12 =
  Rel-13 =
  No mirror CRs are included in these figures
  Rel-8 to Rel-12 CRs are under FASMO acceptance, i.e. CRs that solve Frequent and Serious Mis-operation Only are accepted.

## Slide 15: Rel-13 Overview
6.1.3 P-CSCF Restoration Enhancements with WLAN [PCSCF_RES_WLAN]
Stage 2 CRs to TS 23.380 were agreed. They cover the P-CSCF restoration basic mechanism for WLAN (IMS PDN connection release by the PGW), and the extension with an additional information transferred to the UE requesting a new IMS registration. This extension is specified for trusted and untrusted WLANs. Stage 3 CRs will be addressed in the next meeting.

## Slide 16: Rel-13 Overview
6.1.5 Study on EPC Signalling Improvement for Race Scenarios [FS_EPC_SIG_RACE]
An pCR (C4-151304) was agreed clarifying the conclusions of the TR 29.811. Solution 5 (based on the Maximum Wait Time parameter) may also be used over roaming interfaces, if allowed by operator policy (e.g. in shared networks). TR 29.811 v1.1.0 is available in C4-151407. The study is now complete but the TR still requires some minor updates regarding the PCRF behaviour (see CT3 Reply LS in C3-153436).

## Slide 17: Rel-13 Overview
6.1.7 CT aspects of EVS in 3G Circuit-Switched Networks [EVSoCS-CT]
CT4 sent a Reply LS to SA4 in C4-151290 with our comments.

## Slide 18: Rel-13 Overview
6.1.8 H.248 Aspects of WebRTC Data Channel on IMS Access Gateway [WebRTCH248DC]
Inputs were provided for MSRP.
A related 23.334 CR was agreed in C4-151318.

## Slide 19: Rel-13 Overview
6.1.9 Monitoring Enhancements CT aspects [MONTE-CT]
An important discussion occurred about the selection of the protocol for the T6a/b interface between the MME/SGSN and the SCEF (Service Capability Exposure Function).
No agreement was reached in the meeting. A conference call will be organized the week after CT Plenary for companies to voice their preference and a decision taken on the protocol choice.
For other interfaces, major stage 3 work occurred in this meeting with:
  a discussion paper addressing the points requiring investigation with proposals for many of them;
  a big CR to TS 29.336 describing the procedures, commands and AVPs to configure and report the MONTE events over the S6t interface between the HSS and the SCEF.
  another big CR to TS 29.272 with the impacts on existing procedures to configure and report MONTE events;
  a CR to TS 23.008 identifying the new subscriber data with a table for the AESE related data.

## Slide 20: Rel-13 Overview
6.1.10 Mobile Equipment signalling over the WLAN access [MEI_WLAN]
The following CRs were agreed:
C4-151327: IMEI(SV) signalling for untrusted WLAN access:
  A new Terminal-Information IE is added to the SWm Authentication and Authorization Request to enable the ePDG to forward the IMEI(SV) received from the UE via IKEv2 to the 3GPP AAA Server.
C4-151419: IMEI(SV) signalling for trusted WLAN access
  A new Terminal-Information IE is added to the STa Authentication and Authorization Answer to enable the 3GPP AAA Server to send the IMEI(SV), received from the UE via EAP-AKA', to the TWAN.
C4-151331: IMEI(SV) signalling during Non-3GPP IP Access Registration
  A new Terminal-Information IE is added to the SWx Non-3GPP IP Access Registration Request to enable the 3GPP AAA Server to send the IMEI(SV) to the HSS.
This completes the CT4 work.

## Slide 21: Rel-13 Overview
6.1.11 Study on SCC AS Restoration [FS_SCCAS_RES]
Two pCRS were agreed to be incorporated in TR 29.812:
  one on introduction and use cases focuses on the SCC AS and SRVCC (3rd party registration, originating and terminating calls);
  the second describes the solution with call flows based on transparent data storing the ATCF-Path-URI and ATCF management URI.

## Slide 22: Rel-13 Overview
6.1.12 SDP Capability Negotiation for IMS Media Plane [SDPCN_IMS]
Detailed use case examples are required.

## Slide 23: Rel-13 Overview
6.1.13 CT aspects of Optimizations to Support High Latency Communications [HLcom-CT]
CT4 agreed several CRs to support extended buffering at SGW of DL user plane packets received for a UE making use of a power saving mechanism (e.g. extended DRX or Power Saving Mode).
This completes most of the CT4 normative work.

## Slide 24: Rel-13 Overview
6.1.14 CT aspects of Group based Enhancements [GROUPE-CT]
The identification of the groups to which a UE belongs is a part of the subscription data stored in the HSS (CR to TS 23.008).
A discussion occurred on the definition of the IMSI-group ID in TS 23.003 with a CR finally agreed.
A CR to TS 29.272 specifies the way this information is transferred over S6a/d, here through several AVPs in a grouped AVP.

## Slide 25: Rel-13 Overview
6.1.15 CT Aspects of Video Enhancements by Region-of-Interest Information Signalling [ROI-CT]
There are three ROI modes, the impacts of each one on Iq and Mp need to be specified in more detail.

## Slide 26: Rel-13 Overview
6.1.16 S6a/S6d Shared Data Update [FS_eSDU]
This work is starting with the first version of TR 29.813.
An pCR serves as a reminder for the existing mechanisms (bunch of individual updates, individual updates spread over time, reset with Reset-ID) with their drawbacks.

## Slide 27: Rel-13 Overview
6.2.6 IP Flow Mobility support for S2a and S2b Interfaces on stage 3 (CT1) [NBIFOM]
The stage 3 CRs to specify the new GTP protocol extensions for NBIFOM were postponed to leave time to review the CT1 outputs and ensure a consistent end-to-end encoding between the UE and the PGW/PCRF.
A simple GTPv2 CR was agreed to signal the support of NBIFOM by the MME/SGSN, SGW, TWAN/ePDG to the PGW (C4-151428), and a 29.273 CR specifying a new requested/selected Default Access Type over STa for SCM (C4-151366).

## Slide 28: Rel-13 Overview
6.2.7 CT aspects of enhancements to Proximity-based Services extensions (CT1) [eProSe-Ext-CT]
This Work item addresses Rel-13 Prose extensions.
A CR to TS 23.003 specifies a FQDN format for the Prose Function when it is self-constructed by the UE.
A open point is about the addition of the ProSe discovery service authorization for restricted discovery which impacts the description of the existing Prose Discovery command pair with possible backward compatibility aspects and this will need to be further investigated.

## Slide 29: Rel-13 Overview
6.2.8 CT aspects of Architecture Enhancements for Service Capability (CT3) [AESE-CT]
Major stage 3 work occurred in this meeting with:
  a discussion paper addressing the points requiring investigation with proposals for many of them;
  a CR to TS 29.336 describing the complements to bring to the MONTE CR: procedures impacts, new AVPs to configure the communication patterns over the S6t interface;
  a CR to TS 29.272 with the impacts on existing procedures to send communication patterns to the MME.
The main CT4 decisions and the remaining open points are hereafter listed:
  a SCEF reference id can be associated to several communication patterns sets;
  an overwrite of a communication pattern is accepted when coming from the same SCEF;
  a command request (CIR) from an SCEF can contain MONTE events and communication patterns (multiple SCEF reference IDs);
  the HSS sends the acknowledgement to the SCEF before the MME is updated with the communication patterns;
  the deletion of a communication pattern is waiting for a stage 2 input;
  a supported feature bit is added on S6a for the support of communication patterns;

## Slide 30: Rel-13 Overview
6.3.9 EPC Signalling Improvement for Race Scenarios [EPC_SIG_RACE]
CT4 agreed normative CRs implementing all the solutions agreed to be standardized in the conclusions of the TR.
This completes all the CT4 normative work. CT3 is expected to specify the corresponding Gx protocol updates at their next meeting (in October).

## Slide 31: Rel-13 Overview
6.3.11 Dedicated Core Networks [DECOR-CT]
CT4 discussed the procedure that an MME/SGSN should invoke, to retrieve the UE Usage Type from the HSS. Stage 2 suggests an Update Location Request with a new 'No Registration' flag but this approach causes concerns as it misuses the ULR for purposes other than registering the user and, for the first time over S6a/S6d, this would require to set the M bit of the Supported-Features AVP to force an HSS not supporting DÉCOR to reject the request (rather than registering the user). It was questioned whether this M bit behaviour is well supported by all legacy HSS implementations.
Possible alternatives have been suggested to retrieve the UE Usage Type:
  Authentication Information Request/Answer exchange;
  Notification Request/Answer exchange;
  Define a new Application ID and Command Pair
It was agreed to further discuss offline these different alternatives

## Slide 32: Rel-13 Overview
6.3.12 eDRX [eDRX]
eDRX will NOT apply to users with CS subscription or PS+SMS subscriptions with SMS delivered via NAS over the Iu/A interfaces, i.e. the NAS Location Updates procedure over A/Iu will NOT be extended to enable the negotiation of extended DRX.
A new 'Delay Tolerant Connection' indication has been introduced in the GTPv2 Create Session Response message (C4-151321) and GTPv1 Create PDP Context Response (C4-151343) to indicate to the MME/SGSN that the PDN Connection is Delay Tolerant, i.e. for that PDN connection
A new GTP cause was also specified for the Create Bearer Response and Update Bearer Response messages to enable the MME/SGSN to reject a network initiated control plane procedure initiated for a UE temporarily not reachable due to power saving and to request the PGW/GGSN to hold the ongoing network initiated procedure until the UE is available again for end to end signalling.
How the PGW/GGSN determines whether a specific PDN connection is Delay Tolerant or not is currently not detailed in stage 2 and thus was left For Further Study.

## Slide 33: Rel-12 Overview
7.1.12 P-CSCF restoration enhancements [PCSCF_RES]
A CR to TS 29.228 complements the HSS behaviour which shall clear the S-CSCF Restoration Information when a SAR with SAT=UNREGISTERED_USER and with the P-CSCF-Restoration-Indication is received, the Public Identity being registered and IMS Restoration Procedures being supported.
A CR to TS 29.229 adds the case where a SAR is sent with a SAT=UNREGISTERED_USER for a UE being registered with only one Private User Identity and the S-CSCF starting a P-CSCF Restoration procedure with the HSS.

## Slide 34: Rel-12 Overview
7.2.4 Proximity Services [ProSe]
The ProSe Function Identity is added as a temporary data in TS 23.008.
The ProSe Application Code size of 184 bit was confirmed in TS 23.003.

## Slide 35: Rel-12 Overview
7.2.9 MTCe-UEPCOP-CT [MTCe-UEPCOP-CT]
The Active Time Value for PSM parameter is added in the TS 23.008 storage tables for GPRS and EPS for MME, S4-SGSN and Gn/Gp-SGSN.

## Slide 36: Acknowledgements
The Chairman wants to thank
  the delegates for their dedication, hard work and the willingness to be cooperative which resulted in lively discussions and achieved excellent results.
  Lionel Morand and Yvette Koza for expertly taking care of the parallel sessions.
  to my MCC support, Kimmo Kymäläinen, for providing wonderful assistance during and between the meetings.
  Finally, the hosts of our meeting, for the chance to visit beautiful Vancouver.

## Slide 37: Thank You
37
37
Nigel Berry
3GPP TSG CT WG4 Chairman
+44 7880 786 684
nigel.berry@alcatel-lucent.com