## Slide 1: Proposed guidance on OAuth 2.0 misalignment between CT4 and SA3
Mr Lionel Morand
CT Chair, Orange

## Slide 2: Some background: NRF services
The Nnrf_NFManagement service:
  allows an NF instance in the serving PLMN to register, update or deregister its profile in the NRF or an NRF to register, update or deregister its profile in another NRF in the same PLMN
The Nnrf_NFDiscovery service:
  allows a NF Instance to discover other NF Instances with the potential services they offer, by querying the local NRF.
Nnrf_AccessToken service:
  Allows an NF Service Consumer to request an OAuth 2.0 access token from the NRF acting as OAuth 2.0 authorization server.
  The token is then presented to the Service provider to grant access to the services

## Slide 3: Stage 2/3 Misalignment since Rel-15
NOTE in clause 13.3.1 of TS 33.501
  "NOTE 1: When a NF accesses any services (i.e. register, discover or request access token) provided by the NRF, the OAuth 2.0 access token for authorization between the NF and the NRF is not needed."
  Which could imply that token-based authz shall not be used over Nnrf_NFManagement/NFDiscovery API
Not aligned with TS 29.510, which allows token-based authz for the management and discovery service of the NRF:
  "If Oauth2 authorization is used, an NF Service Consumer, prior to consuming services offered by the Nnrf_NFManagement/NFDiscovery API, shall obtain a "token" from the authorization server, by invoking the Access Token Request service, as described in clause 5.4.2.2."
  Which implies that, if OAuth 2.0 not used, static authz based on local policy at the NRF (section 13.3.0 of TS 33.501)
Moreover, TS 33.501 states that
  Oauth 2 client registration shall be done by invoking the NFManagement_Register service operation
  Whereas OAuth client here is an NF Service Consumer that are not supposed to register to NRF (only service producers), as stated by CT4 in LS to SA3 (C4-184465) in May 2018 and documented in TS 23.501/502.

## Slide 4: Joint SA3/CT4 confcall on March 2021
Report from the CT4 chair:
Output: Proposed way forward
  It was proposed to discuss separation of Oauth2.0 Authorization and NRF registration. This would be a possible discussion in SA3 for Rel-17. We need to find a pragmatic solution for Rel-15 and Rel-16.
  We agreed to work first on the two open issues:
    Correct the stage-2 (TS 33.501), clauses 13.4.1.1 and 13.4.1.2, for the definition of the Oauth2 Client Registration process by defining for Rel-15/16 a kind of Static Authorization/O&M configuration process.
    The NOTE in TS 33.501 clause 13.3.1.3 should be changed to normative text clarifying that the usage of Oauth2 in the NRF APIs (NFManagement and NFDiscovery) is optional.

## Slide 5: Following SA3#103-e May 2021
Two proposed solutions going into opposite directions:
  E///, Nokia, Nokia Shanghai Bell: S3-211753 & S3-211756
    The NOTE in clause 13.3.1 is removed. Add normative text to clarify that the usage of Oauth2 in the NRF APIs (NFManagement and NFDiscovery) is optional.
    Removal of OAuth client registration with NF Register, using instead local configuration as requested in LS C4-185505
  Huawei, HiSilicon: S3-211888
    Changing the Note to a normative language, that token for NRF service are not required and use of static authorization instead.
    Clarify how to implement the Oauth client registration.
Output: no conclusion, despite joint effort to follow the compromise proposal

## Slide 6: Clarification: Oauth 2.0 Client registration
RFC6749:
  The Oauth 2.0 client MAY register to Authorization server to be assigned with a "Client_id" and a Client Secret (password) generated by the Authorization Server
  Client_id and PW are used for password-based HTTP authentication schemes if used
In SBA, Rel-15 and onwards:
  Client_id = NF instance id, configured in the NF and not retrieved from NRF
  HTTP based authentication schemes are not used. No need to retrieve a password
Conclusions:
  Oauth 2.0 Client registration not required in SBA
  Compliant with RFC6749: "This specification does not exclude the use of unregistered clients."
  "Oauth 2.0 client registration" shall not be confused with "NF registration" in NRF (see slide 2)

## Slide 7: Guidance from the TSG CT chair
5G Rel-15/Rel-16 is deeply frozen, widely implemented and deployed
In case of misalignment, Stage 3 (protocol specifications) should prevail over Stage 2
  interface implementations and interoperability test specifications are based on stage 3
An implementation compliant with a stage 3 specification cannot become suddenly non-compliant due to a change to correct misalignment between stage 2 and stage 3
  For frozen specifications, it is not important to determine who was right or wrong.
  Only the impacts on the running implementations should be evaluated.
  If token-based authz for NRF service access were possible, they cannot become "forbidden"
If the stage 3 is correct and consistent, the stage 2 should be aligned with stage 3 for Rel-15 and Re-16 to remove any ambiguity
Further functional changes can be introduced in Rel-17 (if required)
  Such as introduction of a specific Oauth 2.0 client registration

## Slide 8: Proposed way forward
Stick to the conclusion of the CT4/SA3 confcall:
  Correct the stage-2 (TS 33.501), clauses 13.4.1.1 and 13.4.1.2, for the definition of the Oauth2 Client Registration process by defining for Rel-15/16 a kind of Static Authorization/O&M configuration process.
  The NOTE in TS 33.501 clause 13.3.1.3 should be changed to normative text clarifying that the usage of Oauth2 in the NRF APIs (NFManagement and NFDiscovery) is optional.
  Keep Stage 3 (TS 29.510) unchanged, in which the use of Oauth 2.0 authorization framework is optional. It is then up to vendor/operator to decide to use it or not
      Could be further clarified (if deemed required) to clarify that static authorization based on local authorization policy at the NRF (section 13.3.0 of TS 33.501) is used when Oauth 2.0 authorization model is not used..

## Slide 9: Thank You!
Lionel Morand
3GPP TSG CT Chair
ETSI
lionel.morand@orange.com