## Slide 1: Country-specific Emergency URN

## Slide 2: Problem
IMS requires that a special SIP registration is used for emergency session requests: an “emergency registration”
A UE undetected emergency call may be “redirected” to ‘use’ an emergency registration
A UE detected or redirected emergency INVITE contains an emergency services URN: e.g. urn:service:sos
  Only a redirected emergency INVITE may contain a different emergency URN than urn:service:sos, urn:service:sos.police, urn:service:sos.fire, urn:service:sos.ambulance, urn:service:sos.mountain, urn:service:sos.mountain. This different emergency URN is derived by the network from the received dialed digits.
This different URN preferably includes a/the number specific to the country’s numbering plan; a number that was allocated to the emergency service by the country’s regulator
RFC 7163 does not foresee in country specific emergency service identifiers to be used in redirected emergency SIP INVITE requests

## Slide 3: 3GPP have requested the following:
This sub-service URN needs to be defined in the Service URN Labels registry with the "sos" URN Service Labels subregistry.
Contact name, email address, and telephone number:
3GPP Specifications Manager
3gppContact@etsi.org
Type of Assignment:
Assignment of a service URN with the "sos" service type as specified in RFC5031 [69], section 4.2.
The following service URN is proposed to be registered:
urn:service:sos.country-specific
Description:
This sub-service type is used before an appropriate sub-service type is registered with IANA for a specific emergency service. This sub-service type is not used where an appropriate sub-service type has been registered with IANA for the specific emergency service.
The next level of sub-services indicates the country where the specific emergency service is used. Subtypes below this are defined by national regulation of that country and are not registered with IANA.

## Slide 4: Receiving the following response:
I believe this request is not consistent with the words and the intent of the registry.
“country-specific’ is not an emergency service.
Since the management policy of the emergency service is “expert review”, the barrier to adding new, possibly experimental services is low, and the consequences of having services that are not eventually deployed persisting in the registry is minimal.
The URN was not intended to have a generic X- service or equivalent, which is what this registration attempts to do. New services, even experimental services, should register the service with IANA following the normal procedure.
Therefore, I recommend that we deny this request and suggest that the specific services be registered with IANA as they are deployed.
This decision has been reviewed with the ecrit working group.

## Slide 5: 3GPP needs “sos.country-specific” sub-service type
Emergency services are regulated services
In Europe alone there is a wide variety of emergency services per country. A large number of registations may need to be processed by
  https://ec.europa.eu/digital-single-market/en/112-your-country
Registering a URN for each emergency service type delays deployment of IMS:
  It is unclear who (regulator? One or all of the country’s operators?) is responsible for registering
  It is unclear how the various entities resolve conflicts
  It is unclear if the various entities involved wish to coordinate
As a consequence national governments and operators will see that the individual registration causes a lot of administrative overhead and therefore will lower the acceptance of the mechanism.
Operators need to have unique emergency URNs for each emergency service defined in the country at the time of rolling out Voice over IP. Initially, PSAPs are still PSTN based; yet emergency URNs are used in operator's IMS network.

## Slide 6: 3GPP’s response to ECRIT
“country-specific” is an emergency service: the semantic of the URN urn:service:sos.country-specific can be the same as urn:service:sos
The URN is not intended to represent a generic X- service or equivalent. Subtypes of the URN are defined by national regulation of that country and need not registered with IANA.
  EXAMPLE: urn:service:sos.country-specific.xy.567 can identify a type of emergency service identified by an emergency number 567 in a country identified by "xy" ISO 3166-1 alpha-2 code.
Registering specific services with IANA as they are deployed is impractical and unrealistic.