## Slide 1: C1-180397
Additional considerations for 5G PWS Architecture Selection
Nokia, Nokia Shanghai Bell
<Change information classification in footer>
3GPP TSG-CT WG1 Meeting #108
Gothenburg (Sweden), 22-26 January 2018

## Slide 2: Architecture Options
For PWS in 5G, two architecture options are captured in TR 24.890:
  Option 1) AMF<-> CBC via Service based Interface
    The AMF interfaces with CBC and NG-RAN to enable PWS service with the interface between AMF and CBC implemented as service based interface. CBC uses AMF communication services to forward warning messages to NG-RAN and to subscribe to receive warning delivery related notifications.
  Option 2) AMF <->CBC via SBc like Interface
    The AMF interfaces with CBC and NG-RAN to enable PWS service by using SBc-like protocol interface (referred to as "NBc" interface in the diagram) between AMF and CBC. Same protocol stack and procedures for SBc interface will be re-used for NBc interface.

## Slide 3: Solution Evaluation (from CT1#107 – C1-174770)
Evaluation Criteria | Option 1 (Direct SBI between AMF<->CBC ) | Option 2 (AMF<->CBC via SBc interface) | Comments
Support existing CBC deployments | No | Yes | Option 1 requires all CBCs to be upgraded
Impact to AMF | Yes (AMF to provide both routing and PWS handling functionality) | Yes (AMF to provide both routing and PWS handling functionality) | 
Impact to CBC | Yes | No | 
Implementation Efforts | new protocol stack and interface | reusing existing SBc Protocol, only AMF requires change | 
Maintenance Efforts on CBC side | Require maintaining additional interface (for 5G RAT) | Same interface as 4G | 
Future evolution & Architecture Flexibility | Both AMF and CBC need to be upgraded | Both AMF and CBC need to be upgraded | 

## Slide 4: Additional evaluation considerations
  Additional factor need to be considered: Protocol and message interface
  Existing SBc interface are primitive based and maps to S1-MME interface messages between eNB and MME:
Write-Replace Warning Request /Response
Write-Replace Warning Indication
Stop warning request / Confirm
Stop warning Indication
Restart Indication
…
Primitive based
Primitive based
Write-Replace Warning Request /Response
Kill Request / Response
Restart Indication
Failure Indication
…
…

## Slide 5: Additional evaluation considerations
  For 5G, according to TS 23.501, N2 interface between NG-RAN and AMF is NOT service based:
  Therefore PWS message interface between NG-RAN and AMF remains to be message/primitive based
  In addition, it is expected that definitions for N2 PWS related messages/primitives in 5G to be pretty much the same as messages/primitives in 4Gin 5G will be pretty much the same as in 4G

## Slide 6: Additional evaluation considerations
  For 5G option 1, if AMF<-> CBC is via Service based interface, extra conversion is needed to map CBC primitives to service based interface and then back to PWS primitives:
Write-Replace Warning Request /Response
Write-Replace Warning Indication
Stop warning request / Confirm
Stop warning Indication
Restart Indication
…
PWS primitives
PWS Primitives
Write-Replace Warning Request /Response
Kill Request / Response
Restart Indication
Failure Indication
…
…
Namf_Communication.N1N2MessageTransfer
Namf_Communication.N2InfoSubscribe
Namf_Communication.N2InfoNotify
…
Namf operations
Ncbc operations
Convert
Convert
Service based
Primitive based

## Slide 7: Additional evaluation considerations
  For 5G option 2, if AMF<-> CBC is via SBc based interface, then same primitive based interfaces are used:
Write-Replace Warning Request /Response
Write-Replace Warning Indication
Stop warning request / Confirm
Stop warning Indication
Restart Indication
…
Primitive based
Primitive based
Write-Replace Warning Request /Response
Kill Request / Response
Restart Indication
Failure Indication
…
…

## Slide 8: Additional evaluation considerations
  Observation: if Option 1 Service Based interface is used, additional mapping/conversion between service operation and PWS primitives is needed (double conversion), which would result in extra processing overhead.

## Slide 9: Proposal
It is proposed to include these additional factors into consideration when making 5G PWS architecture selection.
Based on evaluation and additional considerations, overall there are significant advantages for reusing existing SBc interface.