## Slide 1: Avoidance of NAS messages getting queued because of CP CIoT data transmission
Vodafone
C1-192204
3GPP TSG-CT WG1 Meeting #116
Xi'an, P.R. of China, 8-12 April 2019
Agenda item 16.2.8 (5G_CIoT)

## Slide 2: NAS signalling and CIoT data
Suppose a number of N CIoT data units needs to be delivered and the security (pre)computation (MAC calculation and encryption) has been run for all CIoT data units. NAS COUNT 1 to N are assigned and each unit will be included in a NAS message.
Then a NAS signaling message (e.g., Mobility and periodic registration update) has to be sent. Without optimizations, only the NAS COUNT = N+1 can be allocated for this NAS signaling message. It means that this message is queued and can be only delivered after all the N CIoT data units have been successfully transferred.
Given the NAS timer for CIoT has an extension value of 240s (MM messages) and 180s (SM messages), respectively, the waiting-time of delivery of the NAS signaling message can be significant.

## Slide 3: Proposal
Separate the NAS signaling message and the CIoT data transfer by introducing different NAS COUNTs (i.e., different crypto streams) so that the NAS signaling message can be delivered without getting queued behind the CIoT data transfer.
LS to SA3