## Slide 1: Overview
UE
TAS
Operator
Provisioning
of service data
UE ability to activate address

## Slide 2: MiD configuration discussion, user using a shared identity
The UE needs to know the identities the UE can use:
  Identities in the IRS are transferred in PAU
  External alternative identities using new mechanisms
  The user shall be able to activate/deactivate these identities
The AS needs to know the identities the user is allowed to use
  The AS can use the list to authorize use of PPI or Additional-Identity header for originating calls
  The AS can use the list and activation state to reject terminating calls

## Slide 3: MiD configuration discussion, options to inform UE
To inform the UE about usable identities there are several options:
  Device configuration
    New specification for MuD/MiD related configuration
    Not clear how the UE can activate an identity this way
  Ut interface
    Follows specification of earlier experience
    A list of identities with activation status is needed
  Means outside the specification, e.g. web portal
    In 24.174 only a statement that configuration is out of scope
  Combinations are possible
    device configuration to push changes, Ut to activate/de-activate

## Slide 4: MiD configuration AS owning external alternative identity
The AS needs:
  List of identities that can share the served identity (belongs to a group)
  The list is used for authorizing originating calls (group members can use the group)
  The list is used for distributing terminating calls (send to group members)
  Configuration alternatives as for the originating AS
The served user:
  shall be able to activate/deactivate each of the above identities
If the shared identity is a group:
  An administrator could be able to add members
  Such procedure requires consent by operator and member
    Hence not suitable for this specification

## Slide 5: Combination MuD and MiD
Activation of identities per Contact can be of interest
  Re-registration can be used to activate identities per Contact
  Media feature tag can be used for this purpose

## Slide 6: Proposal
Specify Ut interface:
  Operator provisions a list of identities, each with an "active" attribute
  User only allowed to change the "active" attribute
  The list applies to the originating AS and the AS serving the external alternative identity
Specify device configuration to push usable identities to devices
No procedures for administrative actions like adding group members specified in 24.174
Propose device configuration to push identities to the UE
  or indication to fetch configuration over Ut
Possibility to support activation of identities to a specific device using re-registration
  policy needed to solve clashes when an identity is in deactivate state but activated on a device