## Slide 1: Discussion on UE consideration for "a CAG cell" and "not a CAG cell“ for TS23.122 / TS24.501
MediaTek Inc.
3GPP TSG-CT WG1 Meeting #124-e C1-203300
Electronic meeting, 2-10 June 2020 Agenda Item 16.2.7.2

## Slide 2: Outline
TS23.122 Problem and Solution Proposal
TS24.501 Problem and Solution Proposal
References

## Slide 3: TS23.122 Problem and Solution Proposal

## Slide 4: TS23.122 Problem statement
According to 38.331 V16.0.0, definition of "CellAccessRelatedInfo information element"
  When taking CAG into considering, there are 3 categories of cells (PN Only, PN+PNI-NPN, PNI-NPN Only), which can be illustrated below
PN +
PNI-NPN
PNI-NPN
Only
PN Only
38.300: CAG Cell: a cell broadcasting at least one Closed Access Group identity
38.304: CAG cell: A cell broadcasting at least one Closed Access Group Identifier
23.501: A CAG cell broadcasts one or multiple CAG Identifiers per PLMN
Therefore, “not CAG Cell” are
38.300: CAG-only cell: a cell that is only available for normal service for CAG UEs
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}
Example 38.331 NR SIB1 config
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
//Don’t care this (ex: PLMN1 or 000.00 or…)
}
cellReservedForOtherUse: true
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
}
CAG
Cell
Therefore, “not CAG-only Cell” are
CAG-only
Cell

## Slide 5: TS23.122 Problem statement
When “CAG information list” content:
  PLMN1-CAG1, "indication that the MS is only allowed to access 5GS via CAG cells" is not included
PN +
PNI-NPN
PNI-NPN
Only
PN Only
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}
Example 38.331 NR SIB1 config
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
}
4.4.3.1.1 Automatic Network Selection Mode Procedure
m) In i to v, if the MS supports CAG and is provisioned with a non-empty "CAG information list", the MS shall not consider a PLMN indicated by an NG-RAN cell unless:
1) the cell is a CAG cell and broadcasts a CAG-ID for the PLMN such that there exists an entry with the PLMN ID of the PLMN in the "CAG information list" and the CAG-ID is included in the "Allowed CAG list" of the entry; or
2) the cell is not a CAG cell and:
- there is no entry with the PLMN ID of the PLMN in the "CAG information list"; or
- there exists an entry with the PLMN ID of the PLMN in the "CAG information list" but the "indication that the MS is only allowed to access 5GS via CAG cells" is not included in the entry.
According to 23.122 4.4.3.1.1 the UE will not consider the PLMN of a cell support both PN and PNI-NPN, which is wrong UE behavior
not a CAG Cell
a CAG Cell
a CAG Cell
Cell Type
According to 2), UE consider PLMN1 for NW selection, Correct behavior
According to 1), UE not consider PLMN1 for NW selection because the CAG2 supported by the cell is not contained in UE’s PLMN1 “Allowed CAG list”, which only supports CAG1, Wrong behavior
According to 1), UE not consider PLMN1 for NW selection because the CAG2 supported by the cell is not contained in UE’s PLMN1 “Allowed CAG list”, which only supports CAG1, Correct behavior
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
//Don’t care this (ex: PLMN1 or 000.00 or…)
}
cellReservedForOtherUse: true
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}

## Slide 6: TS23.122 Solution => Change "not a CAG cell" to "not a CAG-only" cell
MS “CAG information list”
  PLMN1-CAG1, "indication that the MS is only allowed to access 5GS via CAG cells" is not included
PN +
PNI-NPN
PNI-NPN
Only
PN Only
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}
Example 38.331 NR SIB1 config
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
}
not a CAG Cell
a CAG Cell
a CAG Cell
Cell Type
According to 2), UE consider PLMN1 for NW selection, Correct behavior
According to 1), UE not consider PLMN1 for NW selection because the CAG2 supported by the cell is not contained in UE’s PLMN1 “Allowed CAG list”, which only supports CAG1
According to 1), UE not consider PLMN1 for NW selection because the CAG2 supported by the cell is not contained in UE’s PLMN1 “Allowed CAG list”, which only supports CAG1, Correct behavior
4.4.3.1.1 Automatic Network Selection Mode Procedure
m) In i to v, if the MS supports CAG and is provisioned with a non-empty "CAG information list", the MS shall not consider a PLMN indicated by an NG-RAN cell unless:
1) the cell is a CAG cell and broadcasts a CAG-ID for the PLMN such that there exists an entry with the PLMN ID of the PLMN in the "CAG information list" and the CAG-ID is included in the "Allowed CAG list" of the entry; or
2) the cell is not a CAG-only cell and:
- there is no entry with the PLMN ID of the PLMN in the "CAG information list"; or
- there exists an entry with the PLMN ID of the PLMN in the "CAG information list" but the "indication that the MS is only allowed to access 5GS via CAG cells" is not included in the entry.
a CAG-only Cell
not a CAG-only Cell
not a CAG-only Cell
According to 2), UE consider PLMN1 for NW selection, Correct behavior
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
//Don’t care this (ex: PLMN1 or 000.00 or…)
}
cellReservedForOtherUse: true
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}

## Slide 7: Proposal
It is proposed that CT1 discusses the solution
A CR corresponding solution proposed in C1-203301

## Slide 8: TS24.501 Problem and Solution Proposal

## Slide 9: TS24.501 Problem statement
According to 38.331 V16.0.0, definition of "CellAccessRelatedInfo information element"
  When taking CAG into considering, there are 3 categories of cells, which can be illustrated below
PN +
PNI-NPN
PNI-NPN
Only
PN Only
38.300: CAG Cell: a cell broadcasting at least one Closed Access Group identity
38.304: CAG cell: A cell broadcasting at least one Closed Access Group Identifier
23.501: A CAG cell broadcasts one or multiple CAG Identifiers per PLMN
Therefore, “not CAG Cell” are
38.300: CAG-only cell: a cell that is only available for normal service for CAG UEs
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}
Example 38.331 NR SIB1 config
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
}
CAG
Cell
Therefore, “not CAG-only Cell” are
CAG-only
Cell
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
//Don’t care this (ex: PLMN1 or 000.00 or…)
}
cellReservedForOtherUse: true
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}

## Slide 10: TS24.501 Problem statement
For an UE not operates in SNPN access mode, there are three types of cells for the UE to consider
        Cell type 1): the cell only provides PLMN service
        Cell type 2): the cell only provides CAG service (this cell fits the definition of a "CAG Cell").
        Cell type 3): the cell provides CAG service as well as PLMN service (this cell fits the definition of a "CAG Cell")
When considering the “CAG cell”, these subclauses only consider Cell type 2) properly, but not consider Cell type 3) properly
  4.14.3 Public network integrated non-public network (PNI-NPN)
  5.1.3.2.1.3.3 5GMM-DEREGISTERED.LIMITED-SERVICE
  5.4.4.2 Generic UE configuration update procedure initiated by the network
  5.4.4.3 Generic UE configuration update accepted by the UE
  5.5.1.2.5 Initial registration not accepted by the network
  5.5.1.3.5 Mobility and periodic registration update not accepted by the network
  5.5.2.2.7 Abnormal cases in the network side
  5.5.2.3.2 Network-initiated de-registration procedure completion by the UE
  5.6.1.4.1 UE is not using 5GS services with control plane CIoT 5GS optimization
  5.6.1.5 Service request procedure not accepted by the network
a CAG cell
not a CAG cell

## Slide 11: TS24.501 Problem statement (1 example)
Take 5.5.2.2.7 as an example for a MS
  with “CAG information list” = PLMN1-CAG1,
  "indication that the MS is only allowed to access 5GS via CAG cells" is not included
PN +
PNI-NPN
PNI-NPN
Only
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}
Example 38.331 NR SIB1 config
a CAG Cell
a CAG Cell
Cell Type
UE initiates a de-registration procedure not due to “switch off”, the AMF send DEREGISTRATION REQUET message including cause #76, which is a wrong behavior, because UE can use the PLMN1 service due to “indication that the MS is only allowed to access 5GS via CAG cells” is not included
5.5.2.2.7 Abnormal cases in the network side
c) De-registration request received in a CAG cell with a CAG-ID which is not included in the UE's "allowed CAG list" for the current PLMN
If the UE initiates a de-registration procedure in a CAG cell with a CAG-ID which is not included in the UE's "allowed CAG list" for the current PLMN and the de-registration procedure is not due to "switch off", the AMF shall initiate the de-registration procedure. The AMF shall send a DEREGISTRATION REQUEST message including the 5GMM cause #76 "Not authorized for this CAG or authorized for CAG cells only".
UE initiates a de-registration procedure not due to “switch off”, the AMF send DEREGISTRATION REQUET message including cause #76, which is a correct behavior, because UE can use the PLMN1 service due to “indication that the MS is only allowed to access 5GS via CAG cells” is not included
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
//Don’t care this (ex: PLMN1 or 000.00 or…)
}
cellReservedForOtherUse: true
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}

## Slide 12: TS24.501 Solution (1 example)
Take 5.5.2.2.7 as an example for a MS
  with “CAG information list” = PLMN1-CAG1, "indication that the MS is only allowed to access 5GS via CAG cells" is not included
PN +
PNI-NPN
PNI-NPN
Only
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}
Example 38.331 NR SIB1 config
a CAG Cell
a CAG Cell
Cell Type
UE initiates a de-registration procedure not due to “switch off”, the AMF send DEREGISTRATION REQUET message not including cause #76, which is a correct behavior, because UE can use the PLMN1 service due to “indication that the MS is only allowed to access 5GS via CAG cells” is not included
5.5.2.2.7 Abnormal cases in the network side
c)De-registration request received in a CAG cell with a CAG-ID which is not included in the UE's "allowed CAG list" for the current PLMN
If the UE initiates a de-registration procedure in a CAG cell with a CAG-ID which is not included in the UE's "allowed CAG list" for the current PLMN and the de-registration procedure is not due to "switch off", and
  1)the CAG cell does not support PLMN service for the current PLMN; or
  2)the CAG cell supports PLMN service for the current PLMN but the entry for the current PLMN includes an "indication that the UE is only allowed to access 5GS via CAG cells",
the AMF shall initiate the de-registration procedure. The AMF shall send a DEREGISTRATION REQUEST message including the 5GMM cause #76 "Not authorized for this CAG or authorized for CAG cells only".
UE initiates a de-registration procedure not due to “switch off”, the AMF send DEREGISTRATION REQUET message including cause #76, which is a correct behavior, because UE can use the PLMN1 service due to “indication that the MS is only allowed to access 5GS via CAG cells” is not included
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
//Don’t care this (ex: PLMN1 or 000.00 or…)
}
cellReservedForOtherUse: true
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}

## Slide 13: Proposal
It is proposed that CT1 discusses the solution
A CR corresponding solution proposed in C1-203302

## Slide 14: References

## Slide 15: Reference
23.501 V16.4.0
  5.30.3.2 Identifiers
    The following is required for identification:
    ……
    A CAG cell broadcasts one or multiple CAG Identifiers per PLMN
    ……
  5.18.1 General concepts
    ……
    5G MOCN also supports the following sharing scenarios involving non-public networks:
      NG-RAN is shared by multiple SNPNs (each identified by PLMN ID and NID);
      NG-RAN is shared by one or multiple SNPNs and one or multiple PLMNs;
      NG-RAN is shared by one or more PNI-NPNs (with CAG) and one or more SNPNs; and
      NG-RAN is shared by one or multiple PLMNs and one or multiple PNI-NPNs (with CAG).
      NOTE 1: PNI-NPNs (without CAG) are not explicitly listed above as it does not require additional NG-RAN sharing functionality compared to sharing by one or multiple PLMNs.
    ……

## Slide 16: Reference
38.300 V16.1.0
  3.2 Definitions
    CAG Cell: a cell broadcasting at least one Closed Access Group identity.
    CAG-only cell: a cell that is only available for normal service for CAG UEs.
    SNPN-only cell: a cell that is only available for normal service for SNPN subscribers
38.304 V16.0.0
  3.1 Definitions
    CAG cell: A cell broadcasting at least one Closed Access Group Identifier
38.331 V16.0.0
  3.1 Definitions
    NPN-only Cell: A cell that is only available for normal service for NPNs' subscriber. An NPN-capable UE determines that a cell is NPN-only Cell by detecting that the cellReservedForOtherUse IE is set to true while the npn-IdentityInfoList IE is present in CellAccessRelatedInfo.

## Slide 17: Misc

## Slide 18: Misc
PN +
PNI-NPN
CellAccessRelatedInfo {
PLMN-IdentityInfoList{
PLMN1
}
cellReservedForOtherUse: not present
NPN-IdentityInfoList-r16{
NPN-IdentityInfo-r16{
NPN-Identity-r16{
pni-npn-r16{
PLMN1,
CAG2
}
}
}
}
}
R15 UE
Access PLMN1 Service