## Slide 1: Annex-V Signing CR 24.229, 17.5.0
3GPP TSG-CT WG1 Meeting #134-e
Supporting Members

## Slide 2
Background
STIR/SHAKEN is mandated by national regulators in both the United States and Canada
STIR/SHAKEN standards were primarily published by ATIS and IETF
Many operators in both countries have implemented the SHAKEN REST APIs as published in ATIS-1000082
In parallel, 3GPP defined SHAKEN REST APIs (24.229, Annex-V, Ms reference point)
ATIS/SIP Forum, specifically the IP-NNI Task Force, recently decided (late 2021) that future work on SHAKEN REST API standards be pursued in 3GPP (deprecating ATIS-1000082)
As STIR/SHAKEN standards have expanded, more vendor-specific API implementations are being introduced to address ATIS-1000082 limitations
Supporting companies in this CR are proposing signing modifications to more uniformly address limitations for current country adoption and global expansion
Such modifications are based on direct ATIS and IETF standards leadership and, more importantly, implementation experience from supporting billions of daily STIR/SHAKEN transactions since regulatory mandated dates

## Slide 3
Summary of proposed 17.5.0 Annex-V Signing
Proposed Functional Modification (Annex-V Section) | Reason For Functional Modifications | Consequence If Not Approved
Resource structure – Introduce a single /v2 signing resource in Figure V.2.2-1 | Existing /v1 signing approach is to continue adding resources for each new functionality – e.g., “div”, “rph”, etc. Not preferred by implementors and can be greatly simplified (see signing on next Slide) | Functionally equivalent but preferred approach for implementation and future extensibility

## Slide 4
Summary of proposed 17.5.0 Annex-V Signing (Continued)
Proposed Functional Modification (Annex-V Section) | Reason For Functional Modifications | Consequence If Not Approved
signing – Introduce a single /v2 resource as a result of pre-meeting feedback that backwards compatibility needs to be preserved. NOTE: These modifications can (and probably should) be incorporated into the current /v1 in a way to minimize any backwards compatibility concerns. | No proposed functional modification to /v1 signing For /v2, introduces a “ppt” parameter to eliminate the need to proliferate number of required resources Updates the names of “iat” and “orig” to “time” and “from”, respectively, to align with /v1 verification Separates existing “dest” parameter in /v1 signing into “to” and “dest” parameters to clarify their use, especially for “div” Introduces an optional “profileId” parameter for flexibility as a result of broad implementation experience Updates “Description” for “tn” parameter to require that the client perform canonicalization, not the SAS | Fail to address simplicity, flexibility and extensibility early on Implementation issues due to confusion as to why different names are used within SAS and VAS for same parameters (also, aligns with SIP header parameter names) Proper distinction between the “to” and “dest” parameters to facilitate client implementation (already separated in /v1 verification) The optional “profileId” parameter to allow flexibility based on direct implementation experience should be embraced Adds SAS complexity when the core network (client) is in much better position to canonicalize telephone numbers