## Slide 1: Discussion on Constrained device support for MSGin5G
Sapan shah
Samsung

## Slide 2: Content
Architecture
Gateway UE
Relay UE
Protocol Aspects

## Slide 3: Architecture
The MSGin5G UE-2 is a constrained device which does not have enough capability to communicate with MSGin5G Server.
Discussion is focused on red highlighted part of the architecture.
The MSGin5G UE-1 may be constrained devices and unconstrained devices with advanced capabilities, and can communicate with MSGin5G Server over MSGin5G-1 reference point.
The MSGin5G UE-2 is a constrained device which does not have enough capability to communicate with MSGin5G Server.

## Slide 4: Architecture
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.

## Slide 5: Gateway Functionality
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.
Gateway

## Slide 6: Gateway Functionality
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.
Gateway
MSGin5G-5
The interactions related to enabling MSGin5G message related information exchange between an Application Client and an MSGin5G Client are supported by the MSGin5G-5 reference point. This reference point supports:
Providing information from Application Clients required to enable the MSGin5G Client to construct an MSGin5G message to be delivered to other MSGin5G Service endpoints.
Configuring application clients with information required to enable the MSGin5G Client and MSGin5G Server to exchange and route MSGin5G messages to other MSGin5G Service endpoints.
Sending notifications and information in the incoming MSGin5G messages received by the MSGin5G Client to the Application Clients from other MSGin5G Service endpoints.

## Slide 7: Gateway Functionality
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.
Gateway
Procedures
Clause 8.11.2 (Registration)
Clause 8.11.3 (Deregistration)

## Slide 8: Gateway Functionality
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.
Gateway
Procedures
Clause 8.11.4 (Sending message)

## Slide 9: Gateway Functionality
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.
Gateway
Procedures
Clause 8.11.5 (Receiving message)

## Slide 10: Architecture
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.
Gateway

## Slide 11: Relay Functionality
Relay
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.

## Slide 12: Relay Functionality
Relay
MSGin5G-6
The MSGin5G Client of MSGin5G UE-2 communicates with MSGin5G Client of MSGin5G UE-1 over MSGin5G-6 reference point. The interface is based on NR PC5.
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.

## Slide 13: Relay Functionality
Relay
Procedures
??
NOTE 5: When both MSGin5G UE-1 and MSGin5G UE-2 support MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a relay for the MSGin5G Client in MSGin5G UE-2 to receive MSGin5G Service. When MSGin5G UE-2 does not support an MSGin5G Client and only MSGin5G UE-1 supports an MSGin5G Client, MSGin5G Client in MSGin5G UE-1 acts as a gateway for the Application Client in MSGin5G UE-2 to receive MSGin5G Service.

## Slide 14: Protocol Aspects
On application client on MSGin5G UE-2
  Wrap the information (from Application Clients required to enable the MSGin5G Client to construct an MSGin5G message) into application layer off-network message – which will be sent over point-to-point PCS direct communication.
On MSGin5G client on MSGin5G UE-1,
  Receive the data, unwrap the data,
  Construct the CoAP message from the provided information
  Send the CoAP message to the server.
Gateway
Relay
On MSGin5G client on MSGin5G UE-2
  CoAP message will be generated (just like normal point-to-point or group message procedures defined in the specification)
  Send it to MSGin5G server using MSGin5G UE-1 as a relay (It is like a mobile is connected to server using a hotspot)
On MSGin5G client on MSGin5G UE-1,
  No action needed. It just act as a hotspot to provide transport layer connectivity to the MSGin5G UE-2 to connect it to MSGin5G server.
No specific procedures required to be defined.

## Slide 15
Thank you !!