## Slide 1: Mini-Study on QoS for MC clients behind NAT device (e.g. MCGWUE)
Magnus Tränk (magnus.trank@ericsson.com)
Ericsson

## Slide 2: Background
QoS and priority are key requirements for MC services in general and for MCGWUE specifically. MC systems utilize Rx, N5, N33 reference points to request, modify and release 3GPP network resources with needed QoS for mission critical users.
The service data flows are uniquely identified by a 5-tuple (source IP address, source port, destination IP address and destination port and transport). One 5-tuple is needed in uplink and one in downlink and defines the packet filters. Network devices such as UEs and packet gateways can use the 5-tuple information to classify and prioritize traffic based on the assigned PCC rules. Multiple service data flows may be carried in a single QoS Flow (or EPS bearer).
The IP address and ports used for media are negotiated with SDP offer/answer procedures. The SDP information includes only the destination IP address and destination port (TS 24.379). The SDP does not include the source IP address and ports. In the packet filters the source IP address and source port can be wildcarded which implies that the packet filter would match any source IP address and source port.
When using MC clients behind NAT the IP address and ports are modified by the NAT function, and the information in the SDP might not be correct for the MC system to use when requesting network resources via Rx, N5, N33.

## Slide 3: Protocol Stack with MCGWUE

## Slide 4: Key Issues
To request resources with QoS for MC clients behind NAT (e.g. by using local IP addresses with MCGWUE) requires additional functionality. The following issues has been identified.
Key issue #1: How does the server know if QoS should be requested or not?
Key issue #2: How to define packet filters for MC clients behind NAT?
Key issue #3: Availability of packet filter details to AF (i.e. entity sending the Rx request).

## Slide 5: Key issue #1: QoS or not?
The MC system needs to support a variety of MC clients and access networks.
In the figure the MC system shall request network resources for MC client 1 and MC client 2 but not for MC client 3 and MC client 4.
Currently there is no information available to the MC system to decide on requesting resources with QoS or not.
Decision based on IP address cannot be used since MC client 1, 2 and 3 may use same IP network.
Solution proposal: For MC clients behind NAT and using MCGWUE the MC client need to inform the server that a MCGWUE is used. Proposed in contribution C1-240071, C1-240072 and C1-240073.
Note: For MC client 3 and MC client 4 the MC system can decide to not request resources based on e.g. P-Access-Network-Info header. This does not work for MC client 1.

## Slide 6: Key issue #2: Packet filters
Service data flows are identified by a 5-Tuple, one uplink and one downlink.
The media streams destination IP address and ports are shared in the SDP offer/answer at session establishment.
MC client destination IP address and ports from the SDP are useless to packet filters and MC server since it is not reachable from MC server.

## Slide 7: NAT traversal techniques
Managing Client-Initiated Connections in the Session Initiation Protocol (SIP), RFC 5626
  To manage SIP traffic though NATs and firewalls
Interactive Connectivity Establishment (ICE), RFC 8445, RFC 8839
  Used to share transport address candidates between clients (via offer/answer procedures)
Session Traversal Utilities for NAT (STUN), RFC 5389
  Used to identify address candidates and to perform connectivity checks of these
Traversal Using Relays around NAT (TURN), RFC 5766
  Traffic relayed to a relay node to be able to traverse NATs
Latching: Hosted NAT Traversal (HNT) for Media in Real-Time Communication, RFC 7362 (Informational)
  The server wait for the first incoming RTP packet and sends downlink RTP packets to the same IP:port as the source IP:port of the first incoming packet.

## Slide 8: NAT traversal in 3GPP specs
MCPTT TS 24.379
  Only a reference to ICE (RFC 8445) Pre-established session procedures
  Reference to RFC 5626 for SIP traffic
MCVideo TS 24.281
  Only a reference to RFC 5626 for SIP traffic
MCData TS 24.282
  Only reference to ICE (RFC 8445) Pre-established session procedures
Policy and Charging Control signalling flows TS 29.213
  Annex C (normative): NAT Related Procedures
    C.1 Support for media traversal of NATs using ICE
    C.2 P_CSCF procedures to support media traversal through hosted NAT without ICE
Nothing specified about NAT in TS 29.513
  5G System; Policy and Charging Control signalling flows and QoS parameter mapping; Stage 3
IMS TS 24.229
  Annex F.5 NAT Traversal for media flow
  Annex K Additional procedures in support of UE managed NAT traversal

## Slide 9: Key issue #2: Summary
Currently it unclear (not specified) how to set packet filters for QoS flows to MC clients behind NATs
TS 29.213 Annex C provides requirements for packet filters:
  Utilizing a relay server (STUN Relay/TURN server) – Is this applicable for MC services?
  NAT traversal not using ICE with wildcards in the packet filters and usage of UDP source address in packet filters
TS 29.513 is missing NAT requirements on packet filters
Proposal:
  Proposal 1: Specify QoS requirements in NAT traversal use cases including ICE, STUN, Latching usage
  Proposal 2: New annex to specify guidelines/recommendations on QoS management in NAT traversal, references to CT3 specs.

## Slide 10: Key issue #3: packet details availability
Currently SDP offer/answer include destination IP address and ports for media streams
Packet filters can include both source and destination addresses both uplink and downlink. Although source address are typically wildcarded since they are not in the SDP offer/answer
TS 29.213 specifies for NAT traversal that source ports for downlink data (i.e. source ports on MCPTT server) shall be used since the destination ports on NAT device may not be available (note that client ports in SDP are behind NAT).
TS 23.280 specifies that Rx can be used from MCPTT server or SIP core (P-CSCF)
Issue 1: If Rx is used from P-CSCF, the P-CSCF does not have the source port information from the MCPTT server, hence the P-CSCF can not evaluate correct packet filters.
Issue 2: If Rx is used from MCPTT server it is not possible to include e.g. RTP proxy, STUN relay server, BGF in media path, since then the source ports would be available to MCPTT server for sending Rx request.
Potential solution in TS 23.280 subclause 10.11.2a, which would require additional stage-3 work in TS 24.379

## Slide 11: Thank You!