## Slide 1: Network Location & RAN/NAS Cause Codes for VoLTE 3GPP R12
July 4, 2014
David Sanders
Jim Oliver
Martin Dolly
C3-143159

## Slide 2: Overview
Note: This overview is based on reading of the March, 2014, version of 3GPP TS 23.401, 23.203, 29.274. 29.212. 29.213 and 29.214 plus CR 1186 for 29.213 and CR 333 for TS 29.214. It must be vetted within AT&T and with its vendors.
P-CSCF requesting Specific-Action = ACCESS_NETWORK_INFORMATION results in a one-time report of ULI from the PCRF when bearer resources are successfully or unsuccessfully allocated or modified. Successful allocation is shown on slide 3. The failure case is discussed in item 4, below.
Reporting of ULI for a dropped call (MME initiated bearer or IP-CAN session termination) requires that Specific-Action = ACCESS_NETWORK_INFORMATION be armed in Rx AAR from the P-CSCF when bearer resources are requested. If available, ULI is always included in S11/S5 (Delete Bearer Request and Delete Session Request), but conditionally in Gx (CCR-U or CCR-T) based on Event-Trigger = ACCESS_NETWORK_INFORMATION.
  In the case were all flows are affected, ULI is reported to the P-CSCF in Rx STA only if requested in Rx STR. Rx RAR is not triggered by the PCRF in this case. This is shown on slides 5 and 6.
  In the case where two bearers are associated with an Rx session (e.g., IR.94) and only one bearer is terminated by the MME and ANI has been previously been reported (i.e., on notification ANI after success), ULI may be reported in Rx RAR with Specific-Action = ACCESS_NETWORK_INDICATION, but only if the P-CSCF requests it in a subsequent Rx AAR after Specific-Action = INDICATION_OF_FAILED_RESOURCES_ALLOCATION has been reported. This is highlighted in the notes on slide 5. It is not clear in Standards how this is achieved.
RAN/NAS Cause reporting is triggered by the P-CSCF arming Specific-Action = ACCESS_NETWORK_INFORMATION in Rx AAR; it is not specified in the Required-Access-Info AVP and is always reported by the PGW/PCEF in Gx CCR-U (MME initiated bearer termination) or CCR-T (MME initiated session termination) based on Event-Trigger = ACCESS_NETWORK_INFORMATION. It is assumed that RAN/NAS cause is reported by the PGW/PCEF in Rx STA or RAR in the same manner as ULI (above) without needing a separately defined value in the Required-Access-Info AVP. Needs validation.
Reporting of ULI for bearer setup or modification failure is not clearly defined in Standards; however, it is similar to reporting ULI for a dropped call (MME bearer/session termination in item 2, above). When all service flows are affected, ULI is only provided in Rx STA if requested in Rx STR and provided in Gx CCR-U as shown on slide 7. When only a subset of service flows are affected, Rx RAR with Specific-Action = ACCESS_NETWORK_INFORMATION includes ULI as is shown on slide 8. Note that RAN/NAS Cause is not reported in these cases since it is not sent from the MME since the IE is not defined for S11 Create Bearer Response or Update Bearer Response.

## Slide 3: Successful Call Setup
AAR – P-CSCF arms Specific-Action= ACCESS_NETWORK_INFO_REPORT and requests ULI using Required-Access-Info
Gx RAR – PCRF requests installation of charging rules for the specified service flows and arms Event-Trigger = ACCESS_NETWORK_INFO_REPORT requests ULI using Required-Access-Info
Create Bearer Response (not shown) – MME returns ULI
CCR-I – PGW/PCEF asserts Event-Trigger = ACCESS_NETWORK_INFO_REPORT and reports ULI
Rx RAR – PCRF asserts Specific-Action=ACCESS_NETWORK_INFO_REPORT and reports ULI
Note: Step d (SIP continues) may be delayed by the P-CSCF until Rx RAR with ULI is received

## Slide 4: Normal Call Termination
STR – P-CSCF requests ULI using Required-Access-Info
Gx RAR – The PCRF requests removal of the associated charging rules; Event-Trigger = ACCESS_NETWORK_INFO_REPORT is included in Gx RAR
Steps d-g – The GW requests deletion of the dedicated bearer; the MME returns ULI in Delete Bearer Response
CCR-U – PGW/PCEF asserts Event-Trigger = ACCESS_NETWORK_INFO_REPORT and reports ULI
STA – PCRF provides ULI

## Slide 5: Dropped Call - MME Initiated Bearer Deactivation
MME provides ULI and RAN/NAS Cause in Delete Bearer Command (recent AT&T CRs to 3GPP) – 23.401 5.4.4.2
PGW/PCEF provides ULI and RAN/NAS Cause in CCR-U – 23.203 6.1.4 and 24.212 4.5.22; Event-Trigger = ACCESS_NETWORK_INFO_REPORT is reported since it was armed when the charging rules were installed at the beginning of the call
Steps e-h are per 29.213 4.3.2. Not sending RAR is as specified in TS 29.214:
  4.4.6.2 – only Rx ASR is sent when all flows are affected (deactivated) – this is the PCRF behavior introduced in CPM 6.x, which has been discussed with the P-CSCF vendors
  4.4.6.7 and 5.3.13 – Specific-Action ACCESS_NETWORK_INFO_REPORT is a one time report, e.g., sent at successful bearer creation so will not be triggered
  Note: For IR.94 when failure of a single bearer (e.g., video) is reported by the MME, ULI and RAN/NAS Cause is reported only if the P-CSCF requests it in a subsequent Rx AAR. It is not clear in Standards how this is achieved.
STR – P-CSCF requests ULI using Required-Access-Info – not explicitly stated in 29.213 4.3.2, but is consistent with 29.213 4.3.1.2.3.1 and 29.214 4.4.6.7
STA – PCRF provides ULI and RAN/NAS Cause as received in step c

## Slide 6: Dropped Call – UE/MME Initiated Detach (IP-CAN Release)
For MME Initiated Detach, MME provides ULI and RAN/NAS cause in Delete Session Request – 23.401 5.3.8.3.
For UE Initiated Detach, MME provides ULI in Delete Session Request – 23.401 5.3.8.2.1 (RAN/NAS cause is not provided – gap in standards)
Steps c,d and g-j are the same as MME Initiated Bearer Deactivation steps c-g

## Slide 7: Call Setup Failure (Cannot Create Dedicated Bearer)
Assumption: An AAR is issued prior to step a from the P-CSCF to the PCRF to initiate a bearer creation, and that AAR includes Specific-Action = ANI with the Required-Access-Info AVP set.
MME provides ULI in Create Bearer Response (failure); RAN/NAS Cause IE is not defined for CBRsp – (gap in standards)
GW provides ULI in CCR-U – 24.212 4.5.22; Event-Trigger ACCESS_NETWORK_INFO_REPORT is reported since it was armed when installation of the charging rules was requested in Gx RAR (refer to slide 3)
Steps e-h are per 29.213 4.3.2. Not sending RAR is as specified in TS 29.214:
  4.4.6.2 – only Rx ASR is sent when all flows are affected (deactivated) – this is the PCRF behavior introduced in CPM 6.x, which has been discussed with the P-CSCF vendors
  Note: For IR.94 when failure of a single bearer is reported by the MME, PCRF asserts Specific-Action=ACCESS_NETWORK_INFO_REPORT and reports ULI (similar to slide 8).
STR – P-CSCF requests ULI using Required-Access-Info
STA – PCRF provides ULI as received in step c

## Slide 8: Dedicated Bearer Modification Failure
Assumption: An AAR is issued prior to step a from the P-CSCF to the PCRF to initiate a bearer modification, and that AAR includes Specific-Action = ANI with the Required-Access-Info AVP set.
MME provides ULI in Update Bearer Response (failure); RAN/NAS Cause IE is not defined for UBRsp – (gap in standards)
CCR-U – PGW/PCEF asserts Event-Trigger = ACCESS_NETWORK_INFO_REPORT and reports ULI
Rx RAR – PCRF asserts Specific-Action=ACCESS_NETWORK_INFO_REPORT and reports ULI
Steps h-o are as described on slide 4

## Slide 9: Standards Gaps
If the bearer is not successfully created or modified, then the desire is for the ANI to also include the RAN/NAS cause information. However, this is NOT currently defined in standards – MME will not include RAN/NAS cause to the PGW if the bearer creation/modification fails since that IE is not defined in Create Bearer Response or Update Bearer Response (29.274).
If UE initiated detach is performed when dedicated bearer exists, then the desire is for the ANI to also include the RAN/NAS cause information. However, this is NOT currently defined in standards – MME will not include RAN/NAS cause to the PGW in the Delete Session Request (23.401 5.3.8.2.1) if the detach is initiated by the UE.
It is recognized that the method used for propagation of RAN/NAS cause information to the IMS core is undefined at this time. This item will need to be defined in standards. One method to consider is to use the Reason header for propagating the RAN/NAS cause information to the IMS core, perhaps in the text portion of the Reason header. Which forum should be consulted on this?

## Slide 10: BACKUP

## Slide 11: TS 23.203 Reporting of Access Network Information
6.1.4 Event Triggers
  At PCC rule activation, modification and deactivation the ERF shall send, as specified in the PCC/QoS rule, the User Location Report and/or UE Timezone Report to the PCRF.
  NOTE 3: At PCC rule deactivation the User Location Report includes information on when the UE was last known to be in that location.
  The PCRF shall send the User Location Report and/or UE Timezone Report to the AF upon receiving an Access Network Information report corresponding to the AF session from the ERF.
  If the event trigger for Access Network Information reporting is set, the ERF shall check the need for access network information reporting after successful installation/modification or removal of a PCC/QoS rule or upon termination of the IP-CAN session/bearer. The ERF shall check the Access Network Information report parameters (User Location Report, UE Timezone Report) of the PCC/QoS rules and report the access network information received in the corresponding IP-CAN bearer establishment, modification or termination procedure to the PCRF. The ERF shall not report any subsequent access network information updates received from the IP‑CAN without any previous updates of related PCC/QoS rules unless the associated IP-CAN bearer or connection has been released. The ERF shall also provide, if available, the reason why resources are released, i.e. RAN/NAS Release Cause, when the associated IP-CAN bearer is released or the IP-CAN session is terminated.
  If the ERF receives a request to install/modify or remove a PCC/QoS rule with Access Network Information report parameters (User Location Report, UE Timezone Report) set and there is no bearer signalling related to this PCC/QoS rule (i.e. pending IP-CAN bearer signalling initiated by the UE or bearer signalling initiated by the ERF), the ERF shall initiate a bearer signalling to retrieve the current access network information of the UE and forward it to the PCRF afterwards.
  If the Access Network Information report parameter for the User Location Report is set and the user location (e.g. cell) is not available to the ERF, the ERF shall provide the serving PLMN identifier to the PCRF which shall forward it to the AF.
  6.2.3 Application Function (AF)
  The AF may request the PCRF to report any combination of the user location and/or UE Timezone at AF session establishment, modification or termination. For AF session termination the communication between the AF and the PCRF shall be kept alive until the PCRF report is received. If IP-CAN bearer resources corresponding to the AF session are released, the PCRF reports to the AF, if available, the reason why IP-CAN bearer resources are released i.e. RAN/NAS Release Cause, together with the User Location Information and/or the UE Timezone.

## Slide 12: TS 29.214 Reporting of Access Network Information
4.4.6.7 Reporting Access Network Information
  If the AF requests the PCRF to report the access network information (e.g. user location and/or user timezone information), the AF shall subscribe to the "ACCESS_NETWORK_INFO_REPORT" within the Specific-Action AVP and shall include the required access network information within the Required-Access-Info AVP. The AF may request the PCRF to report the access network information in conjunction with providing the PCRF with the AF session information, refer to subclause 4.4.1. Optionally, the AF may request the PCRF to report the access network information without providing service information (see subclause A.10.2). In the latter case the AF establishes an Rx session for the AF session upon requesting the access network information from the PCRF with an AA-Request command, containing information required for the session binding in the Framed-IP-Address AVP, the Framed-IPv6-Prefix AVP Subscription-Id AVP, the Called-Station-Id AVP and/or the IP-Domain-Id AVP.
  The AF may also request the PCRF to report the access network information at Rx session termination. To do so, the AF shall include the required access network information within the Required-Access-Info AVP in the corresponding ST-Request.
  When the PCRF receives a request to report the access network information from the AF, it shall immediately configure the PCEF or BBERF to provide such access network information. When the PCRF then receives the requested access network information from the PCEF/BBERF, the PCRF shall provide the corresponding access network information to the AF within the 3GPP-User-Location-Info AVP (if available), TWAN-Identifier AVP (if available), User-Location-Info-Time AVP (if available), 3GPP-SGSN-MCC-MNC AVP (if location info is not available) and/or 3GPP-MS-TimeZone AVP. If the information is requested as part of an AA-Request command, PCRF shall also provide the ACCESS_NETWORK_INFO_REPORT within Specific-Action AVP. If the PCRF receives the serving PLMN identifier from the PCEF/BBERF instead of the requested access network information, the PCRF shall provide the serving PLMN identifier within 3GPP-SGSN-MCC-MNC AVP to the AF.
  6.2.3 Specific-Action AVP
  Within an initial AA request the AF may use the Specific-Action AVP to request specific actions from the server at the bearer events and to limit the contact to such bearer events where specific action is required.
  For one time specific actions, as identified in the value descriptions below, the AF may provide the Specific-Action AVP with the applicable one-time-specific-action value(s) in subsequent AA-Requests.
  NOTE 1: One time specific actions are reported once the required action is fulfilled and are not reported again unless the AF sends a new request.
  ACCESS_NETWORK_INFO_REPORT (12)
  In the RA-Request (RAR), this value shall be used by the PCRF to report access network information when the PCRF receiving an Access Network Information report corresponding to the AF session from the PCEF/BBERF.
  In the AA-Request (AAR), this value indicates that the AF requests PCRF to report one time access network information when the PCRF receives the first Access Network Information report corresponding to the AF session from the PCEF/BBERF after the AF request for the access network information. The required access information is provided within the Required-Access-Info AVP. Applicable to functionality introduced with the NetLoc feature as described in subclause 5.4.1.
  The Specific-Action AVP with this value indicates a one time specific action.