## Slide 1
Robo-Calling and Spoofing of Telephone Numbers and Need for Verification Tel URI Parameter
Martin Dolly
Lead Member of Technical Staff
Core Network & Gov’t/Regulatory Standards
md3135@att.com
10/4/2016

## Slide 2: Spoofed Calls Versus Robo-Call
    Spoofed calls
The Truth in Caller ID Act prohibits spoofing, or deliberately falsifying the telephone number (TN) and/or name relayed as the caller ID information to disguise the identity of the caller for harmful or fraudulent purposes. However, the law only applies to callers within the United States.
Robo-Calling
A robocall is a phone call that uses a computerized autodialer to deliver a pre-recorded message, as if from a robot. Robocalls are often associated with political and telemarketing phone campaigns, but can also be used for public-service or emergency announcements.

## Slide 3: We know how we got here
Robocalls & Spoofing is the #1 complaint to the FCC and FTC.
    https://consumercomplaints.fcc.gov/hc/en-us/articles/204009760-Consumer-Complaint-Charts-and-Data-Overview
Robocalls & Spoofing is the #1 complaint to the CRTC in Canada
Robocalls & Spoofing is the # 1 complaint to OFCOM and the UK ICO
    https://ico.org.uk/action-weve-taken/nuisance-calls-and-messages/
There have been 6-8 different bills in Congress looking at this. Hearings you name it.
      FCC FTC CRTC [CA] OFCOM [UK] have held workshops. I wrote one of the reports.
      http://stakeholders.ofcom.org.uk/binaries/market-data-research/Ofcom_VoIP_RPKI_Report.pdf
      US Congress had endless hearings.
      https://energycommerce.house.gov/hearings-and-votes/hearings/modernizing-telephone-consumer-protection-act
The PSTN is undergoing a radical transition
    With VoLTE IP based voice will be 75% of the market in 3 years in the US.
Existing PSTN Class 5 TDM/SS7 equipment is at or near End of Life [EOL] and cannot be modified.
All IP Interconnection now a reality US CA EU

## Slide 4: Robocalling/ Spoofing Timeline

## Slide 5
The IETF STIR (Secure Telephone Identity Revisited) Working Group is developing a mechanism to allow phone numbers to be “signed” at the origin, and “verified” at the termination. ATIS has proposed enhancements to make this mechanism practical in the near-term by allowing service providers to perform the “validation” and “verification” on the user’s behalf. Approval at the IETF is expected this year, and will set the stage for the following additional steps:
SHAKEN: A service provider profile for STIR will provide implementation guidelines and specify options within the protocol to ensure interoperability between all service providers. The ATIS/SIP Forum IP-NNI Task Force will complete this profile framework (SHAKEN) before the end of this year. Additional enhancements to the profile will be developed in 2017.
Display Framework: A framework is required to allow for the display of validated Caller ID information to end users in a consistent and secure format. The ATIS/SIP Forum IP-NNI Task Force is developing this framework, with the initial deliverable expected by the end of 2016.
Root Certificate Authority: the signing and verification of calling party information is based on certificates issued by a recognized certificate authority. ATIS is working with the IP-NNI task force to specify the technical requirements and operational procedures for the SHAKEN Root CA.
Testbed: ATIS is facilitating a testbed activity where they have developed a detailed test plan to validate the SHAKEN framework. This will verify the protocol and ensure interoperability between service providers. The STIR/SHAKEN Testbed is targeted to begin 4Q2016 and continue into 2017.
ATIS has established a test plan for Testbeds Focus Group (TFG) Service Provider to Service Provider use cases related to STI (Secure Telephone Identity). It focuses on the approach under development in draft-ietf-stir-rfc4474bis (currently at version -10) and draft-ietf-stir-passport (currently at version -04). The scope of this test plan is to exercise the protocols involved in signing and validating the SIP INVITE when an E.164 telephone number is used as the calling number. The main objective is to demonstrate that the Identity header is created and processed correctly. The intent is to provide assurance that the calling number is a secure telephone identity.
STIR & SHAKEN Working Group

## Slide 6
STIR/SHAKEN Limitations
STIR can be used to validate SIP calls in real-time or to trace calls after the fact.
GW may sign its identity for traceability purposes, without verifying calling number.
Calls from outside SIP network cannot be verified.
  Domestic SIP only
  No support for TDM

## Slide 7
SHAKEN reference architecture
Authentication
Service
Function
Verification
Service
Function
TN Certificate Repository
Call Validation
Treatment
Secure Key Store
STI - Secure Telephone Identity

## Slide 8: This SHAKEN reference architecture includes the following functions:
SIP UA - SIP User Agent that is authenticated by the service provider network is considered secure and the calling party identity is “known” since it is under direct management by the telephone service provider. It initiates the SIP INVITE as the calling party.
IMS/CSCF - This component represents the SIP registrar and routing function. It also has a SIP application server interface.
IBCF/TrGW - This function is at the edge of the service provider network and represents the NNI or peering interconnection point between telephone service providers. It is the ingress and egress point for SIP calls between providers.
Authentication Service (STI-AS) - The SIP application server that performs the function of the authentication service defined in 4474bis. It SHOULD either itself be highly secured and contain the Secure Private Key Store (SKS) or have an authenticated, TLS encrypted interface to the SKS which stores the secret private key(s) used to create the PASSporT signature.
Verification Service (STI-VS) - The SIP application server that performs the function of the verification service defined in 4474bis. It has an HTTPS interface to the TN Certificate Repository, that is referenced in the Identity header field to retrieve the provider public key certificate.
Call Validation Treatment (CVT) - This is a logical function that could be an application server function or a third party application for applying anti-spoofing mitigation techniques once the signature is positively or negatively verified and then provides a response to signal the display response for the end user.
SKS – Secure Key Store is a logical highly secure element to store private key(s) for the authentication service (STI-AS) to access.
Certificate Provisioning Service – A logical service used to provision certificate(s) used for STI.
TN Certificate Repository (TN-CR): This represents the publically accessible store for public key certificates. This should be an HTTPS web service that can be validated back to the owner of the public key certificate.
The focus of this document is on the STI-AS and STI-VS functionality and the relevant SIP signaling and interfaces. Detailed functionality for the Certification Provisioning Service, the TN-CR, the SKS and the CVT will be provided in separate document(s).

## Slide 9
STIR/SHAKEN Basic Call Flow

## Slide 10: Call Flow
The originating SIP UA, which first REGISTERs and is authenticated to the CSCF, creates a SIP INVITE with a telephone number identity.
The CSCF of the originating provider adds a P-Asserted-Identity header field asserting the Caller ID of the originating SIP UA. The CSCF then initiates an originating trigger to the STI-AS for the INVITE.
The STI-AS in the originating SP (i.e., Service Provider A) securely requests its private key from the SKS.
The SKS provides the private key in the response, and the STI-AS signs the INVITE and adds an Identity header field per RFC 4474bis using the Caller ID in the P-Asserted-Identity header field.
The STI-AS passes the INVITE back to the SP A CSCF.
The originating CSCF, through standard resolution, routes the call to the egress IBCF.
The INVITE is routed over the NNI through the standard inter-domain routing configuration.
The terminating SP (Service Provider B) ingress IBCF receives the INVITE over the NNI.
The terminating CSCF initiates a terminating trigger to the STI-VS for the INVITE.
The terminating SP STI-VS uses the “info” parameter information in the Identity header field per RFC 4474bis to determine the TN-CR URI and makes an HTTPS request to the TN-CR.
The STI-VS validates the certificate, which can include these steps: check the validity dates, check the certificate’s signature, check chain of trust, and check certificate validity via CRLs and/or OCSP. It then extracts the public key. It constructs the RFC 4474bis format and uses the public key to verify the signature in the Identity header field, which validates the Caller ID used when signing the INVITE on the originating service provider STI-AS.
The CVT is an optional function that can be invoked to perform call spam analytics or other mitigation techniques and return a response related to what should be displayed to the user for a legitimate or illegitimate call. The CVT may be integrated in the service provider network or outside the service provider network by a third party.
Depending on the result of the STI validation, the STI-VS determines that the call is to be completed with any appropriate indicator (that may be defined outside of this document) and the INVITE is passed back to the terminating CSCF which continues to set up the call to the terminating SIP UA. Note: Error cases where verification fails are discussed in Section 6.
The terminating SIP UA receives the INVITE and normal SIP processing of the call continues, returning “200 OK”, or optionally setting up media end-to-end.

## Slide 11: Certificate Attestation Policy Indication
A. Full Attestation: The signing provider:
    is responsible for the origination of the call onto the IP based service provider voice network
    has a direct authenticated relationship with the customer and can identify the customer
    has established a verified association with the telephone number used for the call.
      Note: The legitimacy of the telephone number(s) the originator of the call can use is subject to signer specific policy
B. Partial Attestation: The signing provider:
    is responsible for the origination of the call onto the telephone network
    has a direct authenticated relationship with the customer and can identify the customer
    has NOT established a verified association with the telephone number being used for the call
      Note: Each customer will have a unique identifier, The unique identifier also provides a reliable mechanism to identify the customer for forensic analysis or legal action where appropriate.
C. Gateway Attestation: The signing provider:
    is the entry point of the call onto the telephone network
    has no relationship to the initiator of the call (e.g., international gateways).
        Note: The signature will provide a unique identifier of the node. (The signer is not asserting anything other than “this is the point where the call entered my network”.)

## Slide 12
Signaling Verification and Analytics Info
Page 12
Note: Interface between VF and Data Analytics Server is outside Industry
Standards and may not be available in initial deployments
& Some Analytics may be performed in the network element that performs the VF
Data Analytic Server may be added
to the architecture over time
VF - Verification Function
Verstat Tel
URI Parameter

## Slide 13: Signaling Verification
  Verstat
      TN Validation Passed
      TN Validation Failed
      No TN Validation
      Future: same values above for CNAM
Security Considerations
    The Verification Function must drop a verstat tel URI parameter received in an INVITE
    If the terminating UE does not support the "verstat" parameter value, it must discard the parameter
    The terminating UE will act on the "verstat" parameter value, if the 200 (OK) response to the UE REGISTER includes a Feature-Caps header field, as specified in RFC 6809°[190], with a "+g.3gpp.verstat" header field parameter
tel URI parameter in the P-Asserted-Identity
or FROM header field in a SIP requests
P-Asserted-Identity: tel:+14085264000;verstat=TN-Validation-Passed