## Slide 1: Comparison of Encoding Proposals for Npcf_PolicyAuthorization
Source: Nokia, Nokia Shanghai-Bell
3GPP TSG CT3 Meeting #94 C3-180050
Gothenburg, Sweden, 22 - 26 January 2018

## Slide 2
Stage 2 requirements
Service Operation Name | Description | Initiated by
Npcf_PolicyAuthorization_Create | Determines and installs the policy according to the service information provided by an authorized NF service consumer. | AF, NEF
Npcf_PolicyAuthorization_Update | Determines and updates the policy according to the modified service information provided by an authorized NF service consumer | AF, NEF
Npcf_PolicyAuthorization_Delete | Provides means to delete the application session context of the NF service consumer | AF, NEF
Npcf_PolicyAuthorization_Notify | Notifies NF service consumer of the subscribed events | PCF
Npcf_PolicyAuthorization_Subscribe | Allows NF service consumers to subscribe to the notification of events | AF, NEF
Npcf_PolicyAuthorization_Unsubscribe | Allows NF service consumers to unsubscribe to the notification of events | AF, NEF

## Slide 3
Issue: Are event exposure and service information provisioning related?
Npcf_PolicyAuthorization service
Related considerations:
Desire to be able to use only event exposure or only service information provisioning, or both in combination.
Some events may be related to an application (e.g. start and stop of application traffic, requested QoS not available)
Stage 2 indicates that Subscribe depends on Create, but service information within Create is optional
Procedures: | Input (required) | Input (optional)
Npcf_PolicyAuthorization_Create | IP address of the UE, application session context identifier | SUPI if available, DNN if available, Media type, Media format, bandwidth requirements, sponsored data connectivity if applicable, flow description, AF application identifier, AF Communication Service Identifier, AF Record Identifier, Flow status, Priority indicator, emergency indicator, Application service provider, resource allocation outcome
Npcf_PolicyAuthorization_Subscribe | List of events, application session context identifier, Notification URI | none

## Slide 4
Encoding Proposal 1 (recommended): event subscriptions as sub-resource
Npcf_PolicyAuthorization service
Resource name | Resource URI | HTTP method | Meaning
Npcf policy authorization | {apiRoot}/ npcf-policyauthorization/ v1/ sessions | POST (FFS) | Requests that the PCF creates a new session for Npcf policy authorization.
Individual Npcf policy authorization | {apiRoot}/ npcf-policyauthorization/ v1/ sessions/ {Sessionid} | PUT (FFS) | Request that the PCF updates an existing session.
 |  | PATCH (FFS) | Partially updates session for Npcf policy authorization
 |  | GET | Provides information about a session for Npcf policy authorization.
 |  | DELETE | Instructs the PCF server to delete a session for Npcf policy authorization.
Media Components | {apiRoot}/ npcf-policyauthorization/ v1/ sessions/ {Sessionid}/ media-components | PUT (FFS) | Requests that the complete set of media components for a session is added or replaced.
 |  | GET | Gets information about the complete set of media components for a session
Individual Media Component | {apiRoot}/ npcf-policyauthorization/ v1/ sessions/ {Sessionid}/ media-components/ {mcNbr} | PUT (FFS) | Request that the server creates a new media component, if it does not exist or updates an existing media component.
 |  | PATCH (FFS) | Partially updates a media component
 |  | GET | Provides information about a media component.
 |  | DELETE | Instructs the PCF to delete a media component.
NPCF policy authorization event subscription | {apiRoot}/ npcf-policyauthorization/ v1/sessions/[Sessionid}/event-subscription | PUT | Allows the NF service consumers to subscribe to the notification of events or modify that subscription.
 |  | DELETE | Allows the NF service consumers to unsubscribe to the notification of events.

## Slide 5
Encoding Proposal 2: event subscriptions as separate resource
Npcf_PolicyAuthorization service
Resource name | Resource URI | HTTP method | Meaning
Application sessions | //{apiRoot}/npcf-policy-authorization/v1/application-sessions | POST | Npcf_PolicyAuthorization_Create. Creates a new individual Application session context resource.
Individual Application session context | //{apiRoot}/npcf-policy- authorization/v1/application-sessions/{appSessionContextId} | PUT (FFS) | Npcf_PolicyAuthorization_Update. Creates a new or updates an existing individual Application session context resource.
 |  | PATCH (FFS) | Npcf_PolicyAuthorization_Update. Updates an existing individual Application session context resource.
 |  | DELETE | Npcf_PolicyAuthorization_Delete. Deletes an existing individual Application session context resource.
 |  | GET | Reads an existing individual Application session context resource.
Event Subscriptions | //{apiRoot}/npcf-policy-authorization/v1/event-subscriptions | POST | Npcf_PolicyAuthorization_Subscribe. Creates a new event subscription resource for a given Application session context identifier.
Individual Event Subscription | //{apiRoot}/npcf-policy-authorization/v1/event-subscriptions/{eventSubId} | PUT | Npcf_PolicyAuthorization_Subscribe. Modifies an existing event subscription resource.
 |  | DELETE | Npcf_PolicyAuthorization_Unsubscribe. Deletes an event subscription.
 |  | GET | Reads an event subscription resource.

## Slide 6
Comparison of Proposals
Npcf_PolicyAuthorization service
 | Proposal 1 | Proposal 2
Separate usage of Event exposure | Yes: All service information related attributes are optional | yes
Seperate Evolution of event exposure to group communication | Possible as long as service information related attributes remain optional | yes
Combined Evolution of event exposure and service information provisioning to group communication. | yes | More complex
Support of Events related to particular service media flows (e.g. QoS not available) | yes | Complicated, e.g. via URL to related resource
Combined operations of event subscriptions and service information provisioning at start of application | yes | No. Two HTTP interactions required,
Combined operations of event unsubscriptions and service information revócation at stop of application | yes | No. Two HTTP interactions required,
Multiple Event Subscriptions for the same Application session | No | Yes

## Slide 7
Any ideas and desire for new concepts to describe service information?
Npcf_PolicyAuthorization service
Stage 2 requirements are very high-level and open (also for Rx)
Rx was developed mainly with IMS and SDP service description in mind.
Early Npcf_PolicyAuthorization service applications might be in non-IMS areas:
  IMS integration via Rx is allowed by stage 2 as alternative
  But IMS support remains a requirement for Npcf_PolicyAuthorization
Previous attempts in TS 29.201 to convert Rx to HTTP via protocol converter with strong alignment to Diameter encoding were not commercially successful.
But implementation complexity is likely to increase if service information description changes fundamentally.