## Slide 1: Comparison of Encoding Proposals for Npcf_SMPolicyControl
Source: Nokia, Nokia Shanghai-Bell
3GPP TSG CT3 Meeting #94 C3-180050
Gothenburg, Sweden, 22 - 26 January 2018

## Slide 2
Issue: How to enable an effective update of extensive policy information?
Npcf_SMPolicyControl
Stage 2 requires that Policy information can be provided both as response to a GET, and as UpdateNotify request. The information is quite extensive and includes a possibly high number of PCC rules.
Related Issues:
How to achieve maximum communality in the implementation for GET and UpdateNotify?
How to enable an effective update for both cases?
Should we model the policy resource to be located both at PCF and SMF?

## Slide 3
Proposal 1 in TR 29.890 (previously the only proposals)
Npcf_SMPolicyControl
Resource name | Resource URI | HTTP method | Meaning
SM Policies | {apiRoot}/ npcf_sm_policy_control/ v1/ policies | GET | Read all SM Policies resources at an AS. Query parameters are FFS and can contain the NotificationURI (to identify all resources related to a given SMF).
Individual SM Subscriber Policy | {apiRoot}/ npcf_sm_policy_control/ v1/ policies/ {supi} | GET | Read the Individual SM Subscriber Policy resources.
 |  | DELETE | Delete the Individual SM Subscriber Policy resource for.
Individual SM PDUSessioPolicy | {apiRoot}/ npcf_sm_policy_control/ v1/ policies/ {supi}/ {sessionID} | PUT (FFS) | Create a new or update an existing Individual SM PDUSession Policy resource.
 |  | PATCH (FFS) | Update an existing Individual SM PDUSession Policy resource.
 |  | GET | Read the Individual SM PDUSession Policy resource.
 |  | DELETE | Delete the Individual SM PDUSession Policy resource.
Policies are modeled at resource at the PCF only.
Notifications are done in RPC like fashion, providing only deltas

## Slide 4
Npcf_SMPolicyControl
Proposal 2 (1/2): Subscription resources at the PCF
Resource name | Resource URI | HTTP method | Meaning
SM Policie Subscriptions | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions | GET | Read all SM Policies resources at an AS. Query parameters are FFS and can contain the NotificationURI (to identify all resources related to a given SMF).
Individual SM Subscriber Policy Subscription | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions/ {supi} | GET | Read the Individual SM Subscriber Policy resources.
 |  | DELETE | Delete the Individual SM Subscriber Policy resource for.
Individual SM PDUSessioPolicy Subscription | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions/ {supi}/ {sessionID} | PUT | Create a new or update an existing Individual SM PDUSession Policy resource for a SUPI and sessionID supplied by the SMF. If an Individual SM Subscriber Policy Resource for the SUPI does not yet exist, it is also created.
 |  | PATCH | Update an existing Individual SM PDUSession Policy resource.
 |  | GET | Read the Individual SM PDUSession Policy resource.
 |  | DELETE | Delete the Individual SM PDUSession Policy resource.
Policies are modeled as resource at the SMF only.
Within the Npcf_SMPolicyControl_Get (HTTP PUT or POST), the SMF provides the root URL for the policy resource.
The PCF does not return policies in the HTTP response to the Npcf_SMPolicyControl_Get. The PCF rather immediately executes an UpateNotify (i.e. sends an HTTP PUT or POST to the designated URL at the SMF), to create or update the policy resource at the SMF (see next slide for resource model and service operations.

## Slide 5
Proposal 2 (2/2): Policy resources at the SMF
Npcf_SMPolicyControl
Resource name | URI | HTTP method | Meaning
SM Policies | {notificationURI}/ policy | PUT | Install new policies or replace existing SM policies at the service consumer
 |  | PATCH | update existing SM policies at the service consumer
 |  | GET | Read existing SM policies
 |  | DELETE | Delete existing SM policies at the service consumer and request termination of corresponding PDU session
PCC Rules | {notificationURI}/ policy/ pcc-rules | PUT | Install new PCC Rules or replace existing PCC Rules at the service consumer
 |  | PATCH | update existing PCC rules at the service consumer
 |  | GET | Read existing PCC rules
 |  | DELETE | Delete existing PCC rules at the service consumer
Individual PCC Rule | {notificationURI}/ policy/ pcc-rules/ {PCCruleId} | PUT | Install new PCC rule or replace existing PCC rule at the service consumer
 |  | PATCH | update existing PCC rule at the service consumer
 |  | GET | Read existing PCC rule
 |  | DELETE | Delete existing PCC rule at the service consumer

## Slide 6
Raised Concerns against Proposal 2 and replies
In previous discussions and CT3 Telcos, the following concerns were raised:
PCF looses control over policies
Reply: This is a misunderstanding: It is a frequent practise for restful interfaces that the client decides the contents of resources and the server merely stores the resources or acts based on their contents.
In proposal 1, the policy resource at the PCF is a mixture of information provided by the client and information selected by the server. Proposal 2 uses a more consistent and clearer model where the client selects the contents of resources.
2. Restoration procedures do not work
Reply: At least in 4G, restoration focused on the continuation of ongoing user plane connections for cases where the PCF was not reachable (due to connection loss, reboot etc).
For such cases it is decisive that the SMF has knowledge of the policies.
For PCF restoration, proposal 2 is even superior to proposal 1, as it allows the PCF to read out the installed policies of ongoing sessions in order to take over control.

## Slide 7
Proposal 3 (policy resources at PCF only. Notifications only as triggers for new Get)
Npcf_SMPolicyControl
Resource name | Resource URI | HTTP method | Meaning
SM Policies | {apiRoot}/ npcf_sm_policy_control/ v1/ policies | GET | Read all SM Policies resources at an AS. Query parameters are FFS and can contain the NotificationURI (to identify all resources related to a given SMF).
Individual SM Subscriber Policy | {apiRoot}/ npcf_sm_policy_control/ v1/ policies/ {supi} | GET | Read the Individual SM Subscriber Policy resources.
 |  | DELETE | Delete the Individual SM Subscriber Policy resource for.
Individual SM PDUSessioPolicy | {apiRoot}/ npcf_sm_policy_control/ v1/ policies/ {supi}/ {sessionID} | PUT (FFS) | Create a new or update an existing Individual SM PDUSession Policy resource.
 |  | PATCH (FFS) | Update an existing Individual SM PDUSession Policy resource.
 |  | GET | Read the Individual SM PDUSession Policy resource.
 |  | DELETE | Delete the Individual SM PDUSession Policy resource.
Policies are modeled at resource at the PCF only, as in proposal 1
Notifications are done in RPC like fashion, providing only triggers for new Get

## Slide 8
Npcf_SMPolicyControl
Proposal 4 (1/2): Subscription resources at the PCF, Policy resources at PCF and SMF
Resource name | Resource URI | HTTP method | Meaning
SM Policie Subscriptions | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions | GET | Read all SM Policies resources at an AS. Query parameters are FFS and can contain the NotificationURI (to identify all resources related to a given SMF).
Individual SM Subscriber Policy Subscription | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions/ {supi} | GET | Read the Individual SM Subscriber Policy resources.
 |  | DELETE | Delete the Individual SM Subscriber Policy resource for.
Individual SM PDUSessioPolicy Subscription | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions/ {supi}/ {sessionID} | PUT | Create a new or update an existing Individual SM PDUSession Policy resource for a SUPI and sessionID supplied by the SMF. If an Individual SM Subscriber Policy Resource for the SUPI does not yet exist, it is also created.
 |  | PATCH | Update an existing Individual SM PDUSession Policy resource.
 |  | GET | Read the Individual SM PDUSession Policy resource.
 |  | DELETE | Delete the Individual SM PDUSession Policy resource.
Policies are modeled as resource at the PCF and SMF.
Within the Npcf_SMPolicyControl_Get (HTTP PUT or POST), the SMF provides the root URL for the policy resource.
The PCF does return policies in the HTTP response to the Npcf_SMPolicyControl_Get.
To PUSH update policies, the PCF can use Restful methods (PATCH, PUT, addressing individual resources, rather than .Custom Operations)

## Slide 9
Proposal 4 (2/2): Policy resources at the PCF and SMF, Subscription resources at the SMF
Npcf_SMPolicyControl
Resource name | URI | HTTP method | Meaning
SM Policies | {notificationURI}/ policy | PUT | Install new policies or replace existing SM policies at the service consumer
 |  | PATCH | update existing SM policies at the service consumer
 |  | GET | Read existing SM policies
 |  | DELETE | Delete existing SM policies at the service consumer and request termination of corresponding PDU session
PCC Rules | {notificationURI}/ policy/ pcc-rules | PUT | Install new PCC Rules or replace existing PCC Rules at the service consumer
 |  | PATCH | update existing PCC rules at the service consumer
 |  | GET | Read existing PCC rules
 |  | DELETE | Delete existing PCC rules at the service consumer
Individual PCC Rule | {notificationURI}/ policy/ pcc-rules/ {PCCruleId} | PUT | Install new PCC rule or replace existing PCC rule at the service consumer
 |  | PATCH | update existing PCC rule at the service consumer
 |  | GET | Read existing PCC rule
 |  | DELETE | Delete existing PCC rule at the service consumer

## Slide 10
How to combine proposals with Event Notifications as part of Npcf_SMPolicyControlService (1/3)
As discussed during the CT3 preparatory Telcos, there are proposals to modify stage 2 in such a manner that event exposure is made part of the SMF policy control functionality (in a similar way as for 4G Gx interfaces). Reasons include
Optimize performance by reducing the number of message exchanged between SMF and PCF
Upon reception of information about events from AMF, give SCF an indication whether it needs to wait for updated policies before replying to AMF
Handling of events related to particular applications and PCC rules

## Slide 11
How to combine proposals with Event Notifications as part of Npcf_SMPolicyControlService (2/3)
Subscription to event Notifications:
Proposals 1 and 3 would likely model the event subscription (list of events,) as part of the policy resource at the PCF.
Proposals 2 and 4 would handle the event subscription (list of events, notification URI) as part of the policy resource at the SMF.
Proposals 2 and 4 are thus more aligned with the SMF_EventExposure service and normal design pattern for Notification's in Restfull interfaces

## Slide 12
How to combine proposals with Event Notifications as part of Npcf_SMPolicyControlService (2/3)
Event Notifications:
Proposals 1 and 3 would likely model the event to be notified (observed events and related parameters) as part of the policy resource at the PCF. The HTTP method used for event notification requires discussion:
  HTTP GET seems not suitable, as it does not allow to modify the policy resource in order to report the event.
  HTTP PATCH allows the SMF to modify the observed event at the server, but it is unclear if it can return a policy resource representation that only contains the modified policies in the response
  Most likely a custom method based on HTTP POST is required
Proposals 2 and 4 would likely model the event to be notified (observed events and related parameters) as part of the subscription resource at the PCF. HTTP PATCH seems a suitable method to report events. Updated policies can then be supplied using HTTP PATCH
  This is not optimal for purposes 1 and 2 of the combination
  Alternatively, a custom operation can again be used

## Slide 13
Comparison of Proposals (1/2)
Npcf_SMPolicyControl
 | Proposal 1 | Proposal 2 | Proposal 3 | Proposal 4
Communality of policy provisioning between Get (Pull operation) and Notify (Push operation) | No | Yes | Yes | No
Efficient policy provisioning for initial GET | Yes | Less Efficient, as two HTTP Request response pairs required. | Yes | Yes
Efficient policy provisioning for subsequent GET (Pull operation, FFS if this is required) | For HTTP GET only complete policy but no deltas can be provided. Thus most likely custom operation required | Alternatives: 1. Two HTTP interactions, but possibility to provide only deltas in Policy 2. Custom Operation | For HTTP GET only complete policy but no deltas can be provided. Thus most likely custom operation required | Alternatives: return policies in HTTP GET response: Only complete policy but no deltas can be provided. 2. Use two HTTP interactions: Only complete policy but no deltas can be provided. 3. Custom Operation
Efficient policy provisioning for Notify (Push operation) | Yes (Depends on Custom Operation design) | Yes | No, two HTTP interactions, and no possibility to provide only deltas in policy | Yes

## Slide 14
Comparison of Proposals (2/2)
Npcf_SMPolicyControl
 | Proposal 1 | Proposal 2 | Proposal 3 | Proposal 4
RESTful design | Only small fractions: A substantial part of the functionality (PUSH policy provisioning and most likely also subsequent PULL operation) uses Custom Operations. | Yes (Evolution to combination with event exposure might require custom operation for subsequent GET) | Partial: most likely subsequent PULL operation requires custom operations (Evolution to combination with event exposure might require custom operation for subsequent GET) | Partial (Duplicated resource is not a usual pattern) (Evolution to combination with event exposure might require custom operation for subsequent GET)
PCF restoration | PCF will not be able to obtain information about ongoing PDU CAN sessions | PCF can obtain information about ongoing PDU CAN sessions | PCF will not be able to obtain information about ongoing PDU CAN sessions | PCF can obtain information about ongoing PDU CAN sessions
Efficient Deletion | OK | OK (assuming policy resources at SMF are implicitly deleted when SMF deletes subscription resource) | OK | OK (assuming policy resources at SMF are implicitly deleted when SMF deletes subscription resource)
Confirmation of Policy installation for PULL | seprate operation | Synchronous confirmation | Separate operation | Synchronous confirmation at subsequent PULL, but separate operation at session establishment

## Slide 15
SUPI as resource identifier?
Npcf_SMPolicyControl
All 3 encoding proposals use the SUPI and PDUSessionId as resource identifier for resources at the PCF and use PUT for creation. But this aspect is marked as FFS:
  Editor's note: It is FFS whether to use PUT or POST for the creation of resources. If POST is used, the supi and pduSessionId in the URI will need to be replaced with a server-assigned resource identifier.
SUPI and PDUSessionId need to be provided by SMF, thus resource creation by PUT is required if they are used as resource identifier.
However, resource creation by POST is usually preferred to allow server to select URI for resource (might be related to internal storage distribution)
Also, possible security concerns about exposing SUPI in URI (message body can be encrypted, but URI needs to be visible to HTTP proxies)
  Related LS sent by CT4 to SA3
  Npcf_SMPolicyControl service probably only used on network-internal interfaces
Recommendation to remove SUPI from resource identifier and use HTTP POST for resource creation

## Slide 16
Summary and Conclusions
A new proposal 4 that is an enhancement of proposal 2 is added: It includes subscription and a policy representation in the resource at the PCF and policies at the resource at the SMF.
  The motivation is a more efficient policy provisioning at session establishment than for proposal 2
Proposal 1 will need to rely on custom operations for a very substantial part of its functionality
Proposal 2 is most Restfull, provides an efficient PUSH of policies, and allows the PCF to update
The possible evolution to a combination with event provisioning is possible with all proposals and will likely require a custom operation for the combined event reporting and subsequent policy updates for any proposal
Either proposal 2 or 4 are recommended.
It is also recommendation to remove SUPI from resource identifier of resources at the PCF and use HTTP POST for resource creation