## Slide 1: SM_PolicyControl policy decision data model design
C3-180180
Oracle

## Slide 2: Policy decision data model

## Slide 3: Problem statement
Current SM_PolicyControl’s policy decision data model is based on the Gx data model
  PCC rules are used to describe inline all aspects of policy and charging control for flows
  Session level policies (e.g. APN-AMBR) used to cover session scoped policy decisions
While this works, there are certain aspects that can be improved:
  Modularity: by separating the various policy control constructs (e.g. QoS, Traffic Steering, etc) into their own objects, we can:
    Re-use policy decision information across flows to avoid duplication of information
    Independently evolve the various policy decision constructs
  Inheritance: leveraging common functionality across various policy constructs, we can use inheritance to define the various types of policy rules in a class hierarchy
3

## Slide 4: New Encoding Proposal (a.k.a. reference based encoding)

## Slide 5: PccRule
5
  *: As opposed to having QoS, charging, traffic steering and other parameters specified inline within the PccRule, the corresponding information is organized into its own set of rules and referenced within the PccRule via rule ids.
Attribute name | Data type | P | Cardinality | Description
ruleId | string | M | 1 | Uniquely identifies the PCC rule, within a PDU session.
scope | PolicyScope | M | 1 | Determines the scope of the PCC rule: session, flows, application,predefined or predefined group
precedence | interger | O | 0..1 | Determines the order, in which service data flow templates consisting of service data flow filters are applied at service data flow detection at the UPF.
decisionDataIds* | string | C | 0..N | A list of decision data ids (QoS, charging, etc) associated with this rule.
activationTime | datetime | O | 0..1 | The time when the PCC rule shall be activated.
deactivationTime | datetime | O | 0..1 | The time when the PCC rule shall be deactivated.

## Slide 6: DecisionData’s class hierarchy
6
As specified in the previous slide, QoS, Charging, traffic steering and other parameters associated with a PCC rule are organized into their own groups of data referenced by the PCC rule
These decision data have common properties but simply are different types of decision data. As such, they are defined following the below class hierarchy
DecisionData
QoSData
ChargingData
TrafficControlRule
…
Attribute name | Data type | P | Cardinality | Description
decisionId | string | M | 1 | Uniquely identifies the decision data within a PDU session.
activationTime | datetime | O | 0..1 | The time when the decision data shall be activated.
deactivationTime | datetime | O | 0..1 | The time when the decision data shall be deactivated.
DecisionData

## Slide 7: Example inheritance schema
7
QoSData is a subclass of DecisionData and as such inherits all of the attributes from the parent class DecisionData
This can be expressed with Swagger/OpenAPI using the allOf keyword (https://swagger.io/docs/specification/data-models/oneof-anyof-allof-not)
DecisionData:
type: object
required:
- decisionId
properties:
decisionId:
type: string
…
QoSData:
allOf: #inherits all of the DecisionData properties
- $ref: '#/DecisionData‘
- type: object
properties:
5QI:
type: integer
maxRequestedBw:
type: Bitrate
…

## Slide 8: Policy Decision
Policy decision is organized into a set of PCC rules and a map (https://swagger.io/docs/specification/data-models/dictionaries) of rules referenced by the PCC rules as follows:
8
PolicyDecision
Attribute name | Data type | Cardinality | Description
policies | PccRule | 0..N (Map) | A map of PCC rules provisioned by the PCF keyed by ruleId
decisionData | DecisionData | 0..N (Map) | A map of domain specific decision data (QoS, Charging, traffic steering, etc) keyed by decision id
NOTE 1: Session level policies (e.g. Session-AMBR and Default-QoS-Information) can be expressed as policies with “Session” level scope. Exact encoding is FFS
NOTE 2: Using maps as opposed to arrays works quite well if Merge Patch is used to update sub resources

## Slide 9: Decision Data re-use scenarios
Under what circumstances does DecisionData get shared across PCC rules?
  Charging information, e.g RTP and RTCP flows of an IMS session
  TrafficControl can be shared across rules, e.g. controlling the gate status of multiple rules at once
  QuotaData could be shared across PCC rules, e.g. to group the usage across multiple rules
  SponsoringData is shared as it is common to all flows belonging to an Rx/N5 session

## Slide 10: Encoding efficiency 1/3
There is a bit of overhead in the encoding of a single PCC rule as follows:
  The decisionDataIds which is an array of ids within a PCC rule
  The map of DecisionData at the PDU session level:
    The decision id as the key used in the map
    The decision id within each Decision Data
      Note that as an optimization, the decision id may be omitted from the Decision Data and just used as the key
  So the total overhead of one PCC rule encoding (when compared with an inline encoding of the decision data witin the PCC rule) is:
    2 * average (size( DecisionId)) * average (number of decision data per rule)
  The average number of decision data per rule will probably be about 3 (QoS, Charging, TrafficControl, QuotaData, SponsoringData). So as long as the decision id size is kept small, the overhead can be minimal.

## Slide 11: Encoding efficiency 2/3
Although there is overhead relative to encoding all the decision data within the PCC rule, there are encoding savings when DecisionData can be shared by multiple PCC rules
Let’s take an example for clarity where two PCC rules share the same charging information (e.g. RTP and RTCP related rules)
  ChargingData consists of: serviceId, ratingGroup, reportingLevel, online, offline, meteringMethod, which will be encoded in JSON as follows:
    { “serviceId” : “1234”, “ratingGroup” : “5678”, “reportingLevel” : “SERVICE_IDENTIFIER_LEVEL”, “online” : “true”, “offline” : “true”, “meteringMethod” : “DURATION” }, which is 211 bytes
  Let’s compare the inline based encoding vs the reference based encoding (new proposal):
    Inline based encoding overhead: duplicated ChargingData, i.e. 211 bytes
    Reference based encoding overhead: 24 bytes
      ids for qos, charging and traffic control decision data within the pcc rule, so 3* average (size(id))
      ids used in the decision data map for the above decision data so another 3* average (size(id))
      If we assume the id size is encoded as a hex value, an id in this case would take one character (as there are fewer than 16 data decisions) so the total overhead is: 2*3 = 6 bytes. Even if we used 4 hex characters for the id, it’ll be 24 bytes.

## Slide 12: Encoding efficiency 3/3
You can see from the previous example the encoding gains with the reference based encoding (187 bytes = 211 - 24). The gains can be much more significant when more data sharing exists (e.g. QoS, TrafficControl, SponsoringData, etc or more PCC rules share decision data)
There is an additional efficiency advantage with the new encoding which opens up the possibility to update shared data decisions without the need to update the corresponding PCC rules

## Slide 13: Encodings’ comparison summary
Encoding proposal | Efficiency | Complexity | Extensibility
Inline encoding | Basis of comparison | Basis of comparison | New decision data type requires updates to the PCC rule schema
Reference based encoding | Much more efficient in the vast majority of cases. Slightly less efficient when there is no decision data sharing | Slightly more complex to manage the additional referenced decision data | New decision data type can be separately defined without impacting PCC rule schema

## Slide 14: Recommendations

## Slide 15: Recommendations
Recommendation is to go with the new “reference based” encoding proposal
pCR C3-180066 against TS 29.512 defines the high level structure of policy decision based on this new proposal.