## Slide 1: Rollback Behavior in EPC during TAU/RAU (When Location Update to HSS Fails)
3GPP TSG CT WG4 Meeting #61
Chengdu, The People's Republic of China; 20th – 24th May 2013
C4-131005
Cisco

## Slide 2: Introduction
SA2 has sent LS Response in C4-130540 to CT4 LS (C4-130417)
In the LS, SA2 highlighted following scenario during TAU/RAU procedures
  New node (MME/SGSN) queries for context from the old node (MME/SGSN)
  If successful, then new node (re-) establishes EPS Bearers/PDP Contexts on (new or same) SGW and PGW/GGSN
  If successful, performs update location procedure with HSS/HLR
  HSS rejects the above request for any reason (e.g. access restriction)
Issues during above scenario
  System rollback behavior during step 2 is not defined currently in either stage 2 or stage 3
  i.e. what happens to the session(s) modified/created on SGW and PGW by MME/SGSN is unclear
Action to CT4
  To further study system rollback behaviour to provide recommendations to SA2 for possible changes to specifications under SA2’s remit

## Slide 3: Discussion
Target node is configured to perform authentication with the HSS during TAU/RAU procedures (as specified by SA2 in LS C4-130540)
  If the authentication fails, the target node sends Context Acknowledge ("UE Authentication Failed") to the source node
  The target node does not establish any session towards the SGW (existing or new SGW) and hence there is no need for any rollback behavior
  However, this may result in increased signaling towards HSS
Target node is not configured to perform authentication with the HSS during TAU/RAU procedure
  The target node selects new/existing SGW and establishes session with it
  This will create new control/data path: "target node" => existing/new SGW => PGW
  The rollback behavior is needed to switch back the control/data path to: "source node" => existing SGW => PGW

## Slide 4: Scenario Classification
During TAU/RAU procedure, the target node may or may not select new SGW
  Scenario A:
    During TAR/RAU procedure, the target node selects new SGW
    The HSS rejects the location update request message and hence the RAU/TAU is rejected
  Scenario B:
    During TAR/RAU procedure, the target node selects same SGW as currently serving SGW
    The HSS rejects the location update request message and hence the RAU/TAU is rejected
NOTE:
  The source node provides the S11/S4 control plane F-TEID of the currently serving SGW, for the specific UE, to the target node within Context Response message.

## Slide 5: Scenario A: Reference Call Flows (3GPP TS 23.401 clause 5.3.3.1)

## Slide 6: Scenario A: Solution 1
Rollback behavior of the target node
  Target node sends Delete Session Request message with "Scope Indication =1" and "Operation Indication=0"
  The new SGW releases the resources corresponding to the UE, locally, without sending any message to the PGW
Open Issues
  The PGW switched the S5/S8 control and data path towards the new SGW (at step 9, 10 in the reference call flows)
  Since the new SGW has released all the UE related resources, for the given UE, the S5/S8 path is broken for the time until the PGW receives MBReq message from any SGW
  If the PGW sends downlink data (while the S5/S8 path is broken), it will receive an Error Indication and hence might release the corresponding bearer/PDN connection
Behavior of source node
  The source node does not send Delete Session Request message (with SI=1, OI=0) to old SGW while the "context transfer guard timer" is running (i.e. step 18 is executed only after expiry of the timer)
  If the UE comes back while the timer is running, the source node shall send MBReq (and include one of RAT, ULI, UCI etc.) message to SGW to re-establish the broken S5/S8 path
Evaluation
  No new protocol changes
  New behavior of the source node as highlighted in red color; new/existing behavior of the target node is highlighted in dark red color
  The downlink data (while S5/S8 path is broken) may cause release of corresponding bearer/PDN connection

## Slide 7: Scenario B: Reference Call Flows (3GPP TS 23.401 clause 5.3.3.2)

## Slide 8: Scenario B: Solution 1
Rollback behavior of the target node
  The target node releases the resources corresponding to the UE, locally, without sending any message to the SGW
Open Issues
  The SGW switched the S11/S4 control and data path towards the target node (at step 9, 13 in the reference call flows)
  Since the target node has released all the UE related resources, for the given UE, the S11/S4 path is broken for the time until the SGW receives MBReq message from MME/SGSN. SGW is unaware about the broken S11/S4 path
  On reception of downlink data (while the S11/S4 path is broken), the SGW will send DDN message to target node. The target node will reject the message with "Context Not Found" and this will cause the SGW to release the UE session
Behavior of source node
  If the UE comes back while the timer is running, the source node shall send MBReq message to SGW to re-establish the broken S11/S4 path
Evaluation
  No new protocol changes
  New behavior of the source node as highlighted in red color; new/existing behavior of the target node is highlighted in dark red color
  The DDN message (while S11/S4 path is broken) may cause release of corresponding bearer/PDN connection at SGW and hence at PGW

## Slide 9: Conclusion
The proposed solution may cause release of bearer/PDN connection only if downlink data arrives between T2 and T1, where
  T1: time when the path is switched to (target node => existing/new SGW => PGW)
  T2: time when the path is switched back to (source node => existing/new SGW => PGW)
The time (T2-T1) may be small and the probability of arrival of downlink packet within this time will be further very very small
Hence, it may sufficient/reasonable to rely on the simple solution (as mentioned in solution 1) to handle this rare condition
CT4 response to SA2:
  To consider solution 1 as probable solution, for the use case provided, and consider making changes to the specification under your remit.

## Slide 10: Discussion during CT4#61
The scenario suggest that the MME/SGSN rejects the TAU/RAU procedure and the UE re-selects the old RAT.
  However, appropriate NAS cause code should be defined by CT1 (if not already defined) to ensure that the UE re-selects old RAT
  Some of the existing reject cause code may cause UE to re-attach to network
In solution 1 scenario A (slide 6), when the source node sends MBReq message to SGW, it shall be ensured that the SGW sends MBReq message including Bearer Context(s) and Control-plane F-TEID IEs to the PGW, to ensure the re-establishment of S5/S8 path
Potential problem of hanging resources at PGW in following cases
  The timer in source node expires before the UE performs procedure in the source node
  The UE detaches from the network when the TAU/RAU is rejected