## Slide 1: WebRTC gateway – Status of IMS WebRTC CT4 work:
3GPP TSG CT4 Meeting #67 C4-142465
San Francisco; 17th – 21st November 2014
H.248. WebRTC gateway (eIMS-AGW / eIMS-ALG): | 
Supported capabilities (in Rel-12): | 
1 | ICE/STUN for UDP
2 | ICE/STUN for TCP (audio & video only)
3 | STUN Consent Freshness
4 | UDP- & TCP-based transport of audio & video
5 | End-to-access-edge security (SRTP) with DTLS-SRTP based key management
6 | Audio transcoding (to/from OPUS)
7 | optional Video transcoding

## Slide 2: WebRTC data channels:
3GPP TSG CT4 Meeting #67 C4-142465
San Francisco; 17th – 21st November 2014
H.248. WebRTC gateway (eIMS-AGW / eIMS-ALG): |  | Dependencies to other SDOs: | 
Open items: |  | IETF | ITU-T
1 | Binding of bearer-level SCTP streams (data channels) to call-level WebRTC data applications | No | Yes (H.248.SCTP, H.248.STGROUP)
2 | Vertical protocol stack separation in "Data channels" and common transport "SCTP/DTLS/UDP/IP" | No | Yes (H.248.STGROUP)
3 | Handling of SCTP association (for multiple data channels) | Yes (draft sctp-sdp) | Yes (H.248.SCTP)
4 | H.248 Context internal interconnection of data channels between WebRTC and non-WebRTC domain | No | Yes (H.248.STGROUP)