## Slide 1: Reserved TMGI for MBMS service for receive only mode

## Slide 2: Receive only mode
Receive only mode is a UE mode of operation where the UE:
  Does not need USIM (no subscription)
  Is only capable of receiving eMBMS broadcast
    No unicast capability as part of ROM
    No signaling with the network (no registration/authentication/authorization)
Receive Only Mode UE decides to camp on a PLMN in order to receive MBMS TV broadcast based on the broadcast “standardize TMGI range”
  Stage 2 requirement in 23.246:
    A UE configured to operate in Receive Only Mode shall camp on a network cell in an eMBMS Broadcast carrier, shall attempt to receive MBMS service based only on a standardised TMGI value range for Receive Only Mode. The UE shall not attempt to receive MBMS service for TMGIs outside the standardized TMGI range
There is a requirement to standardize a range of TMGI for MBMS service for receive only mode

## Slide 3: TMGI structure and encoding
TS 23.003 describes a structure of the TMGI
TS 24.008 defines the TMGI IE and its encoding
The encoding in 24.008 is used in all stage 3 specs
  for TMGI AVP over BM-SC interfaces (CT3 29.061)
  over Sm interface between MME and MBMS-GW (CT4 29.274)
8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 
Temporary Mobile Group Identity IEI |  |  |  |  |  |  |  | Octet 1
Length of Temporary Mobile Group Identity contents |  |  |  |  |  |  |  | Octet 2
MBMS Service ID |  |  |  |  |  |  |  | Octet 3 Octet 4
 |  |  |  |  |  |  |  | Octet 5
MCC digit 2 |  |  |  | MCC digit 1 |  |  |  | Octet 6*
MNC digit 3 |  |  |  | MCC digit 3 |  |  |  | Octet 7*
MNC digit 2 |  |  |  | MNC digit 1 |  |  |  | Octet 8*
TS 24.008
TS 23.003

## Slide 4: Two possible options for reserving the TMGI range
Reserve dedicated “well-known” PLMN ID in ITU-T for MBMS service in receive only mode
Reserve range of MBMS Service ID
Option 1 is cleaner
  Opens up a brand new range of TMGI values for receive only mode
  Enables fast service detection
  No backward compatibility issues
  No impact on 24.008
  OK from RAN point of view: “eNB announces a MBMS session TMGI whose PLMN ID is not in the SIB1 PLMN ID list. ” (23.246)
  Has been done in the past (MCC/MNC 901/89 was reserved as “escape PLMN ID” in GSM)
Option 2 does not require external SDO involvement

## Slide 5: TMGI for Service Announcement
There is the following requirement in 23.246:
The UE may be configured to receive TMGI(s) via Service Announcement
Within the reserved TMGI range, some TMGI values should be reserved for Service Announcement
  A single value could be sufficient

## Slide 6: Proposal
Option 1 (preferred)
    Reserve well-known PLMN ID for MBMS service in Receive Only Mode
    Reserve one MBMS Service ID under well-known PLMN ID for service announcement
Option 2 (less preferred)
  Reserve one MBMS Service ID value for Service Announcement
  Mandate Service Announcement for MBMS service in Receive Only Mode