## Slide 1
3GPP TSG CT4 Meeting #77 C4-172007
Spokane, US; 03rd – 07th April 2017
Source: Cisco
Title: Service based architecture
Spec: 3GPP TR 29.891 v0.1.0
Agenda item: x.x
Document for: Discussion
1. Reason for Change
Discuss service based architecture

## Slide 2: Agenda
A view on services and how it translates to 3GPP functions
  What is a service
  What is service based architecture.
  What are the benefits of service based architecture
  Desired properties of a service based architecture.
  Service based architecture in 5G.

## Slide 3: What is a service
A service is a discrete unit of functionality that can be accessed remotely and acted upon and updated independently.

## Slide 4: What is a service based architecture
A service based architecture in an architecture services are provided to the other components by application components, through communication over a network.
The basic principles of service based architecture are independent of vendors, products and technologies.

## Slide 5: Monolithic architecture
Memory
Function1
Function2
Function3
Monolithic architecture
server
Strong coupling via memory
The application can be difficult to understand and modify. As a result, development typically slows down.
There are not hard module boundaries, modularity breaks down over time.
It can be difficult to understand how to correctly implement a change the quality of the code declines over time.
Continuous deployment is difficult

## Slide 6: Distributed but still monolithic
Memory/Database…
Function1
Function2
Function3
Monolithic architecture
server3
Still logically a monolithic architecture with strong coupling.
But with more issues
  Race conditions
  Overhead
  More failure points
server1
server3
server2

## Slide 7: The evolution to service based arch
Memory/Database…
Service 1
Service 2
Service 3
Service based architecture
Server3
Split the task into a number of independent autonomous services
Communicating over a network
Avoid race conditions
Avoid unnecessary latency
Avoid reachability issues.
Reduce number of failure points for any single service
Server1
Memory/Database…
Memory/Database…
Server 2

## Slide 8: What do you gain by using a service based architecture.
Tune the network for specific applications and services for better customer experience
Better maintainability
Simplify operations
Independent upgrade/downgrade for different services.
Easier hosting of 3rd party services in the network.
Easier enablement of functionalities like Network Slicing

## Slide 9: Desired properties of services
  It has to logically represent an activity with a specified outcome.
  It has to be self-contained and relatively autonomous
  It has to appear as a black box for its consumers.
  It may consist of other underlying services.
  It has to be discoverable
  It has to expose a clear standardized service contract
  It has to provide some sort of Access control

## Slide 10: Network functions , Services , API ‘s and protocols
Network functions (eg. SMF, AMF …) implements a plurality of Services
Network Functions exposes Services as API’s
The API’s are registered with a well known registry (e.g DNS ) to allow discovery by other services.
The API’s are serialized for transport in a specified format( binary , textual …) when different services communicate with each other.
The serialized data is transported via one of the protocols which handles transaction/reliability aspects ( HTTP/Diameter …)
The transport is done over a packet routed network (IPv4, IPv6)

## Slide 11: Services based architecture and NG* interfaces
Think of NG* interfaces defined in 3GPP as relationships between NF’s that are mandatory.
Each NG * uses a set of services exposed by each party in the relationship
NF1
NF2
APIzz:
APIyy:
NGxx

## Slide 12: Service based architecture and 5G
Each network NF is a compound service ( i.e consisting of multiple internal services communicating over network) ( SMF , AMF etc are compound services )
Each NF exposes a well defined service contract over the NG* interfaces. Think of NG* interfaces defined in 3GPP as relationships between NF’s that are mandatory.
The service contract can follow different communication patterns ( client-server , peer to peer , pub sub etc) based on the specific service requirements

## Slide 13: Service based architecture and 5G
Interface |  | Interface communication pattern
NG1 ( ?? ) | UE <-> AMF | Client – Server, bi directional
NG2 ( ?? ) | RAN <-> AMF | Client – Server , bi directional
NG3 ( SBA not applicable) | RAN <-> UPF | Data plane
NG4 | UPF <-> SMF | Peer to peer
NG5 | PCF <-> AF | Client – Server , bi directional
NG6 ( SBA not applicable) | UPF <-> DN | Data plane
NG7 | SMF <-> PCF | Client Server , bi directional
NG8 | AMF <-> UDM | Client Server , Request response

## Slide 14: Service based architecture and 5G
Interface | Between | Interface communication pattern
NG9 | UPF <-> UPF | Peer to peer
NG10 | SMF <-> UDM | Client-Server,Request - response
NG11 | AMF <-> SMF | Peer to peer
NG12 | AMF <-> AUSF | Client-Server, Request - response
NG13 | AUSF <-> UDM | Client-Server, Request - response
NG14 | AMF <-> AMF | Peer to peer
NG15 | PCF <-> AMF | Client Server , bi directional
NG16 | SMF <-> SMF | Peer to peer