## Slide 1
3GPP TSG CT4 Meeting #78 C4-173010
Zhangjiajie, CN; 15th – 19th May 2017
Source: Cisco
Title: Discussion on usage of HTTP in SBA
Spec: 3GPP TR 29.891 v0.2.0
Agenda item: x.x
Document for: Discussion
1. Reason for Change
Discussion on usage of HTTP in SBA for discovery and communication

## Slide 2: Problem
A number of different types of functional API’s are needed in the network for exposing different services
A number of instances of functional API’s are needed to scaling those services.
Scalable and secure discovery and assignment of the functional elements in a network a key problem in the deployment of services
With micro-services the problems become exacerbated
The API’s can be deployed in multiple networks , need to establish trust between networks.

## Slide 3: Goals
Use webscale techniques for discovery and selection of function API’s in a network
Zero configuration discovery for function API’s in the network
Webscale security mechanisms for peer authentication
Webscale security mechanisms for attack prevention ( DoS and others)
Easy automated creation and updation of function API’s in the network
Web protocols (HTTP/WEBSOCKET) for simple world wide reach
Compatible with microservices

## Slide 4: Key Infrastructure required
DNS infrastructure capable of being dynamically updated.
HTTP redirect agent capable of being dynamically updated with instance information.

## Slide 5: An example interaction
ROOT DNS
Function API instance selector
Orchestration
Function requesting element
1.DNS Request
gtpc.033.11.3gpp.org
2. DNS response
A : 10.10.10.11
A : 10.10.10.12
3. HTTP:
http://10.10.10.11/gtpc/<imsi>
4. HTTP REDIRECT:
http://192.168.1.1/gtpc/<imsi>
Gtpc
Function
instance
5. HTTP :
http://192.168.1.1/gtpc/<imsi>
Function
API type
update
6. HTTP :
Switch to web socket
7. GTP-C over websocket
DNS UPDATE
DB UPDATE

## Slide 6: An example interaction with recursion
ROOT DNS
Function API instance selector
Orchestration
Function requesting element
1.DNS Request
gtpc.033.11.3gpp.org
2. DNS response
NS : 10.10.10.11
5. HTTP:
http://10.10.10.11/gtpc/<imsi>
6. HTTP REDIRECT:
http://192.168.1.1/gtpc/<imsi>
Gtpc
Function
instance
7. HTTP :
http://192.168.1.1/gtpc/<imsi>
Function
API type
update
8. HTTP :
Switch to web socket
9. GTP-C over websocket
DNS UPDATE
DB UPDATE
AUTHORITATIVE
DNS
3.DNS Request
gtpc.033.11.3gpp.org
4. DNS response
A : 10.10.10.11
A : 10.10.10.12

## Slide 7: Security
DNSSEC for DNS security
SSL/TLS for HTTP/websocket security
Standard web security infrastructure can be applied for all the interfaces for DoS and other attach prevention.
Certificates can be used for validating the originator
Token based authentication/authorization can be used for short term services