## Slide 1: SRv6 for Mobile User-Plane
3GPP TSG CT4 Meeting #74 “First presentation was in DMM WG meeting@IETF99 based on: draft-matsushima-spring-dmm-srv6-mobile-uplane”
S.Matsushima, C.Filsfils

## Slide 2: Abstraction
This document discusses the applicability of SRv6 (Segment Routing IPv6) to user-plane of mobile networks that SRv6 source routing capability with its programmability can fulfill the user-plane functions, such as access and anchor functions.
It takes advantage of underlying layer awareness and flexibility to deploy user-plane functions that enables optimizing data-path for applications. Network slicing and an interworking way between SRv6 and existing mobile user-plane are also discussed in this document.

## Slide 3: A Current Mobile Network Example
SGi
EPC
RAN
Access Node (eNode-B)
GTP-U Tunnel
GTP-U Tunnel
L2 Anchor Node (Serving Gateway)
L3 Anchor Node (Packet Data Network Gateway)
Service Functions
IPv4
IPv4
VLAN, etc.,
IPv4/IPv6
Data-plane Role
Internet,
Service network
Well fragmented to RAN, EPC and SGi.
Per-session tunnel creation and handling.
Non-optimum data-path.

## Slide 4: What if SRv6 Becomes An Alternative of GTP-U Tunnel?
IPv4
IPv4
Well fragmented to RAN, EPC and SGi.
Per-session tunnel creation and handling.
Non-optimal data-path.
IPv6 integrates networks of the mobile and others.
A SID represents data-plane role and function.
SRv6 Network
Access Node (eNode-B)
SRv6 SIDs
L2 Anchor Node (Serving Gateway)
L3 Anchor Node (Packet Data Network Gateway)

## Slide 5: SRv6 in A Nutshell
SRH (Segment Routing Header)
4
Segment ID (SID)

## Slide 6: SRv6 in A Nutshell (Cont’d)
Internet,
Service network
SA=S::
DA=D::
NH=TCP
Payload
SA=S::
DA=B::
NH=SRH(43)
Payload
SL=2
SID[0]=D::
SID[1]=C::
SID[2]=B::
SA=S::
DA=C::
NH=SRH(43)
Payload
SL=1
SID[0]=D::
SID[1]=C::
SID[2]=B::
SA=S::
DA=D::
NH=TCP
Payload
MN
S::
CN
D::
C::
B::
SRv6 Network
IPv6 Header
SRH
SRH
IPv6 Header

## Slide 7: SRv6 in A Nutshell (Cont’d)
SRv6 Function* Name | Forwarding
END | Lookup SRH
END.X | L3 cross-connect to next-hop
END.T | L3 lookup IPv6 table
END.DT6 | Decap outer IPv6 hdr and lookup IPv6 table
END.DT4 | Decap outer IPv6 hdr and lookup IPv4 table
END.DX6 | Decap outer IPv6 hdr and IPv6 cross-connect
END.DX4 | Decap outer IPv6 hdr and IPv4 cross-connect
END.B6 | Bound to an SRv6 policy(SID list)
SRv6 Function* Name | Forwarding
T | Pure IPv6 transit
T.Insert | Insert an SRv6 policy (SID list)
T.Encaps | Encap SRv6 policy (SID list) by outer IPv6 hdr
* SRv6 Network Programming

## Slide 8: SID Functions* for Mobile Data-Plane Roles
SRv6 Network
Access Node (eNode-B)
SRv6 SIDs
L2 Anchor Node (Serving Gateway)
L3 Anchor Node (Packet Data Network Gateway)
Uplink
Downlink
 | Uplink | Downlink
Access Node | T.Insert | END.X
L2 Anchor Node | END | END
L3 Anchor Node | END.T | T.Insert
* SRv6 Network Programming
Internet,
Service network

## Slide 9: Stateless Interworking Segment
SRv6 Enabled IPv6 Network
Existing IPv4 Network
Internet,
Service network
Internet,
Service network
SA
Tun-ID
User pkt
DA
SA
DA
Interwork-SID
User pkt
Locator
DA(v4)
SA(v4)
Tun-ID
128-a-b-c
a
b
c
IPv4
header
Tunnel
header
IPv6
header
SRH
header

## Slide 10: E2E Mobile Orchestration with SRv6
SRv6 Network
Orchestrator /Controller
Mobile Control-Plane & Apps
UL:T.Insert DL:END.X
UL:END.T DL:T.Insert
Data-plane nodes are NOT dedicated to specific roles.
  -> SID represents each data-plane role.
Orchestrator puts SIDs to the nodes with its functions
  -> It requires some data models to instantiate the data-plane
Internet,
Service network

## Slide 11: Data Model for Mobile Orchestration with SRv6
SRv6 Network
Orchestrator /Controller
Mobile Control-Plane & Apps
UL:T.Insert DL:END.X
UL:END.T DL:T.Insert
Slice1a
Slice2a
SliceNa
CE
BBU
S/PGW
PE
S/PGW
PCEF
Slice1x
Slice2x
SliceNx
CPE
WiFi-AP
S/PGW
IoT-GW
WiFi-AC
PCEF
Abstracted Tenants/Slices NW on Orchestrators
Tenant A
Tenant X
・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・
ietf-dmm-fpc.yang
Internet,
Service network

## Slide 12: SRv6 for Network Slicing
SRv6 Network
A set of SIDs represents Network Slice. -> Sharing same prefix among SIDs in a slice would work.
Then user packets could also indicate Slices by SID. -> Applications in a MN could be able to use SID to do that.
SID set of NetSlice-A
SID set of NetSlice-B
SID set of NetSlice-C
Contents for NetSlice-A
Contents for NetSlice-B
Contents for NetSlice-C
SA
DA
payload
IPv6
header
Slice SID
SRH

## Slide 13: Summary
SRv6 is expected to make mobile network to be:
  Simple to operate in E2E basis.
  Flexible where to deploy various functions.
SID Functions for mobile data-plane can be considered:
  Access-node, L2 Anchor-node and L3 Anchor-node.
To orchestrate mobile user-plane network, SRv6 needs to be integrated into:
  Data model for mobile data-plane.
  5G related standards.
Network Slicing could take advantage of SRv6.

## Slide 14: Nest Step
Studies for supporting more user-plane functions with SRv6.
  QoS
  Accounting
  etc.,
Update the I-D with:
  Outcomes from the studies
  Figure out the sets of SRv6 functions for mobile user-plane which could be standardized.
Collaborations.
  DMM WG items
  Other WG in the IETF (Spring, if any)
  Both operators and vendors those who are interested in SRv6 are welcome.

## Slide 15: References
SRv6 for Mobile User-Plane
  draft-matsushima-spring-dmm-srv6-mobile-uplane
IPv6 Segment Routing Header (SRH)
  draft-ietf-6man-segment-routing-header
SRv6 Network Programming
  draft-filsfils-spring-srv6-network-programming
ietf-dmm-fpc.yang
  A SDO neutral mobile data-plane model as a part of the FPC work in IETF DMM working group.
  draft-ietf-dmm-fpc-cpdp