## Slide 1: Event Exposure Alignment
AMF-UDM-NEF

## Slide 2: NEF Event Exposure (TS 23.502 v15.4.1)
Event | Description | Which NF detects the event
Loss of Connectivity | Network detects that the UE is no longer reachable for either signalling or user plane communication. | AMF
UE reachability | It indicates when the UE becomes reachable for sending either SMS or downlink data to the UE, which is detected when the UE transitions to CM-CONNECTED state or when the UE will become reachable for paging, e.g., Periodic Registration Update timer. | AMF UDM: reachability for SMS
Location Reporting | It indicates either the Current Location or the Last Known Location of a UE. One-time and Continuous Location Reporting are supported for the Current Location. For Continuous Location Reporting the serving node(s) sends a notification every time it becomes aware of a location change, with the granularity depending on the accepted accuracy of location. (see NOTE 1) For One-time Reporting is supported only for the Last Known Location. | AMF
Change of SUPI-PEI association | It indicates a change of the ME's PEI (IMEI(SV)) that uses a specific subscription (SUPI) | UDM
Roaming status | It indicates UE's current roaming status (the serving PLMN and/or whether the UE is in its HPLMN) and notification when that status changes. (see NOTE 2) | UDM
Communication failure | It is identified by RAN/NAS release code | AMF
Availability after DNN failure | It indicates when there has been some data delivery failure followed by the UE becoming reachable. | AMF
Number of UEs present in a geographical area | It indicates the number of UEs that are in the geographic area described by the AF. The AF may ask for the UEs that the system knows by its normal operation to be within the area (Last Known Location) or the AF may request the system to also actively look for the UEs within the area (Current Location). | AMF
NOTE 1: Location granularity for event request, or event report, or both could be at cell level (Cell ID), TA level or other formats e.g. shapes (e.g. polygons, circles, etc.) or civic addresses (e.g. streets, districts, etc.) which can be mapped by NEF. NOTE 2: Roaming status means whether the UE is in HPLMN or VPLMN. |  | 

## Slide 3: NEF service operations information flow
AF subscribe external event to UDM
NEF subscribe UDM events to UDM
UDM subscribe AMF events to AMF
  AMF event subscriptions will be maintained during AMF changes.
UDM event report notified by UDM to NEF
AMF event report notified by AMF directly to NEF

## Slide 4: UDM Event Exposure (TS 29.503 v15.2.0)
Enumeration value | Description
"LOSS_OF_CONNECTIVITY" | Loss of connectivity
"UE_REACHABILITY_FOR_DATA" | UE reachability for data
"UE_REACHABILITY_FOR_SMS" | UE reachability for SMS
"LOCATION_REPORTING" | Location Reporting
"CHANGE_OF_SUPI_PEI_ASSOCIATION" | Change of SUPI-PEI association
"ROAMING_STATUS" | Roaming Status
"COMMUNICATION_FAILURE" | Communication Failure
"AVAILABILITY_AFTER_DNN_FAILURE" | Availability after DNN failure
Attribute name | Data type | P | Cardinality | Description
referenceId | ReferenceId | M | 1 | 
eventType | EventType | M | 1 | String; see subclause 6.4.6.3.3 only the following values are allowed: "UE_REACHABILITY_FOR_SMS" "CHANGE_OF_SUPI_PEI_ASSOCIATION" "ROAMING_STATUS"
report | Report | C | 0..1 | Shall be present if eventType is "CHANGE_OF_SUPI_PEI_ASSOCIATION" or "ROAMING_STATUS"
gpsi | Gpsi | C | 0..1 | shall be present if the report is associated to exposure subscriptions for a group of UEs or any UE.
timeStamp | DateTime | M | 1 | Point in time at which the event occured
Table 6.4.6.2.4-1: Definition of type MonitoringReport
Observations:
Aligned with Stage 2 events
“Number of UEs present in a geographical area” is expected to be directly subscribed to AMF, aligned with 4G.
Events detected by AMF are expected to be delivered directly by AMF to NEF

## Slide 5: AMF Event Exposure (TS 29.518 v15.2.0)
Enumeration value | Description
"LOCATION_REPORT" | A NF subscribes to this event to receive the Last Known Location of a UE or a group of UEs, and Updated Location of the UE or any UE in the group when AMF becomes aware of a location change of the UE.
"PRESENCE_IN_AOI_REPORT" | A NF subscribes to this event to receive the current present state of a UE in a specific Area of Interest (AOI), and notification when a specified UE enters or leaves the specified area. The area could be identified by a TA list, an area ID or specific interest area name like "LADN".
"TIMEZONE_REPORT" | A NF subscribes to this event to receive the current time zone of a UE or a group of UEs, and updated time zone of the UE or any UE in the group when AMF becomes aware of a time zone change of the UE.
"ACCESS_TYPE_REPORT" | A NF subscribes to this event to receive the current access type(s) of a UE or a group of UEs, and updated access type(s) of the UE or any UE in the group when AMF becomes aware of the access type change of the UE.
"REGISTRATION_STATE_REPORT" | A NF subscribes to this event to receive the current registration state of a UE or a group of UEs, and report for updated registration state of a UE or any UE in the group when AMF becomes aware of a registration state change of the UE.
"CONNECTIVITY_STATE_REPORT" | A NF subscribes to this event to receive the current connectivity state of a UE or a group of UEs, and report for updated connectivity state of a UE or any UE in the group when AMF becomes aware of a connectivity state change of the UE.
"REACHABILITY_REPORT" | A NF subscribes to this event to receive the current reachability of a UE or a group of UEs, and report for updated reachability of a UE or any UE in the group when AMF becomes aware of a reachability change of the UE.
"SUBSCRIBED_DATA_REPORT" | A NF subscribes to this event to receive the current Subscribed Data for the UE(s) received from UDM, and notification when AMF received updated subscribed data for the UE(s) from UDM.
"COMMUNICATION_FAILURE_REPORT" | A NF subscribes to this event to receive the Communication failure report of a UE or group of UEs or any UE.
"UES_IN_AREA_REPORT" | A NF subscribes to this event to receive the number of UEs in a specific area.
Observations:
AMF Event exposure includes internal network exposure event (marked), and parts of the NEF exposure events, missing:
  Availability after DNN failure
  Lost of Connectivity
  UE Reachability for Data and UE Reachability for SMS (also detected on AMF but notified by UDM)
AMF Event names are different from UDM events

## Slide 6: ISSUE-1: Subscribe to UDM Event and receive AMF Event in Notification
When NEF creates monitoring configuration on UDM with UDM event type, UDM will relay the subscription to AMF with mapping UDM event type to AMF event type;
The notification sent by AMF only contains AMF event type, which is different to the UDM event type in monitoring configuration set by NEF
Recommendation:
Option-1: Define External Events as common Data type and used by both AMF/UDM (Best approach, but maybe too later for Rel-15?)
Option-2: NEF use AMF event in Notifications from AMF, with aligning AMF event names to UDM EE API event names (Preferred)
  Proposed in C4-191156 (CR0165 TS 29.518)

## Slide 7: ISSUE-2: NEF events are missing on AMF event exposure
Following NEF events are missing on AMF EE API
  Loss of Connectivity
  UE reachable for SMS/Data
  Availability after DNN failure
Possibility for NEF to implement NEF Events based on current AMF event reports
  Map AMF “UE Reachability”(REGULARTOY_ONLY/UNREACHABLE) to “Lost of connectivity” and ignore “UE Reachability”(REACHABLE)
  Map “UE Reachability”(REACHABLE) to “UE reachability for SMS/Data” (Partly)
    Needs additional information from AMF, e.g. when UE can become available (periodic registration timer)
  Implement “Availability after DNN failure” with existing AMF event (Not possible)
    Need to get “DDN delivery failure” and “UE activities” which are very low level information only AMF aware
  Difficult to synchronize report options. E.g. Total number of reports NEF events cannot be mapped to total number of reports on AMF
Recommendation:
Support the missing NEF external events on AMF EE API (Preferred)
  Proposed in C4-191157 (CR0166 TS 29.518) for Loss of Connectivity Event
  Proposed in C4-191158 (CR0167 TS 29.518) for UE Reachability Event