## Slide 1: Refresh mode “Steering of roaming”
Discussion Document
3GPP TSG-CT6 Meeting #80
C6-160220
COMPRION GmbH

## Slide 2: SoR in 3GPP TS 23.122 V12.8.0 / V13.4.0
4.4.6 Steering of roaming
If the MS receives a USAT REFRESH command qualifier (3GPP TS 31.111 [41]) of type "Steering of Roaming", the MS shall:
a) replace the highest priority entries in the "Operator Controlled PLMN Selector with Access Technology" list stored in the ME with the list provided in the REFRESH command;
b) delete the PLMNs identified by the list in the REFRESH command from the Forbidden PLMN list and from the Forbidden PLMNs for GPRS service list, if they are present in these lists. This includes any information stored in the SIM and the ME internal memory;
c) take the new information into account in subsequent attempts to access a higher priority PLMN; and
d) attempt to obtain service on a higher priority PLMN as specified in subclause 4.4.3.3 by acting as if timer T that controls periodic attempts has expired.
In order to avoid unnecessary signalling, the network operator should avoid repeatedly using steering of roaming of a particular MS.

## Slide 3: SoR in 3GPP TS 23.122 V8.12.0/V11.4.0
4.4.6 Steering of roaming
If the MS receives a USAT REFRESH command qualifier (3GPP TS 31.111 [41]) of type "Steering of Roaming", the MS shall:
a) replace the highest priority entries in the "Operator Controlled PLMN Selector with Access Technology" list with the list provided in the REFRESH command;
b) delete the PLMNs identified by the list in the REFRESH command from the Forbidden PLMN list and from the Forbidden PLMNs for GPRS service list, if they are present in these lists. This includes any information stored in the SIM and the ME internal memory;
....

## Slide 4: SoR in 3GPP TS 31.111 V13.3.0
6.6.13 REFRESH
For all REFRESH modes except "Steering of Roaming", see ETSI TS 102 223 [32] clause 6.6.13. For "Steering of Roaming":
Description | Clause | M/O/C | Min | Length
Proactive UICC command Tag | 9.2 | M | Y | 1
Length (A+B+C+D+E+F+G+H) | - | M | Y | 1 or 2
Command details | 8.6 | M | Y | A
Device identities | 8.7 | M | Y | B
Alpha identifier | 8.2 | O | N | C
Icon identifier | 8.31 | O | N | D
Text Attribute | 8.70 | C | N | E
Frame Identifier | 8.82 | O | N | F
PLMNwAcT List | 8.90 | C (see Note 1) | N | G
PLMN List | 8.97 | C (see Note 2) | N | H
Note 1: This parameter is required in case of steering of roaming (according to TS 23.122 [7]). Note 2: This parameter is required in case of steering of roaming for I-WLAN (according to TS 24.234 [42]). |  |  |  | 

## Slide 5: Questions
In TS 31.111 the list in the proactive command is named PLMNwAcT List and therefore it could be assumed that values provided could be considered for the EFPLMNwAcT (User controlled PLMN selector with Access Technology) Comparing this to TS 23.122 shows that here the "Operator Controlled PLMN Selector with Access Technology" list is considered.
Q1 Does the terminal take the values in the proactive command for the operator or user controlled list inside the ME ?
Q2 And does the operator controlled list makes sense at all to be used when the user controlled list has a higher priority ?
Q3 pre Rel-12 of TS 23.122 does not state “…. list stored in the ME with …” therefore the test cases in TS 31.124 make use of changing the EF in the simulated card, so the affected TCs have to be updated ? And do we have to separate pre Rel-12 behavior and Rel-12 and later behavior ?