## Slide 1: eCall modes based on SIM card configuration
22.08.2017 / Olaf Zöllner / Vodafone
3GPP TSG-CT WG6 Meeting #85 Krakow, Poland, 22 - 25 August 2017
C6-170499

## Slide 2: Background
Due to an unclear definition in 3GPP TS 31.102 different interpretations regarding the support of the “eCall only” and “eCall and Normal call” modes are possible.
Vodafone has already experienced that eCall module suppliers have got a different interpretation of 3GPP TS 31.102 than Vodafone.

## Slide 3: 3GPP TS 31.102 Details
For eCall related procedures different modes (“eCall only” & “eCall and Normal call”) are defined in 3GPP TS 31.102 based on different SIM card configurations.
Section 5.3.40. contains following statements/definitions:

## Slide 4: Problem Description
How shall an eCall module/device distinguish between these 2 modes?
“eCall Only”:
3GPP does not clarify if Service n°4 (FDN) has to be set to “not available” in the EF_UST file on the SIM card or if the setting for Service n°4 should not be examined .
“eCall and Normal call”:
3GPP does not clarify if Service n°2 (SDN) has to be set to “not available” in the EF_UST file on the SIM card or if the setting for Service n°2 should not be examined.

## Slide 5: Vodafone Interpretation 1/2
“eCall Only”:
This mode has to be chosen by an eCall device if following is set on the card:
“Service n° 89 and Service n° 2 are "available" and FDN service is enabled in EF_EST” (as per TS 31.102).
Setting of Service n°4 is not relevant (i.e. arbitrary)
“eCall and Normal call”:
This mode has to be chosen by an eCall device if following is set on the card:
“Service n° 89 and Service n° 4 are "available"” (as per TS 31.102)
FDN service is disabled in EF_EST
Setting of Service n°2 is not relevant (i.e. arbitrary)

## Slide 6: Vodafone Interpretation 2/2
By following the interpretation on the previous slide, the changing from on to the other eCall mode could be done by just activating or deactivating the FDN service (in EF_EST).

## Slide 7: Questions to 3GPP TSG CT WG6
Question 1:
“eCall Only” mode:
Has Service n°4 to be set to “not available” in the EF_UST file on the SIM card or is the setting of Service n°4 not relevant (i.e. arbitrary)?
Question 2:
“eCall and Normal call” mode:
Has Service n°2 to be set to “not available” in the EF_UST file on the SIM card or is the setting of Service n°2 not relevant (i.e. arbitrary)?
Question 3:
Is Vodafone’s interpretation (see slides 5&6) correct?