## Slide 1: Source: Qualcomm Incorporated, Neul Ltd, Huawei Technologies Co., Ltd., HiSilicon Technologies Co., Ltd, u-blox AG; Title: EC-GSM frequency tracking and phase requirement challenges (update of GPC150511) Agenda: 1.4.2.1 Document for: Discussion
3GPP TSG GERAN 1/ 2 Ad-hoc #3 Tdoc GPC150520
Kista, Sweden
29 – 2 July 2015

## Slide 2: Extended coverage GSM (EC-GSM) in noise dominated condition
EC-GSM, for example CC6, is supposed to take care of 164dB MCL, with variety of repetitions of 2, 4, 8, 16 and 32. (EC-RACH can have 51 repetitions) as indicated by ref 1.
  CC1, refers to current GPRS coverage, where signals are above noise floor, which is not a concern here.
  CC2/3/4/5/6 are for the actual EC-GSM and is relevant for this discussion, where signals are below noise floor. This discussion assumes CC6.
EC-GSM is keeping the current GSM BW of 200kHz, and basic time frame structure, including 3.69 microsecond symbol duration, which was originally not designed for 164 dB MCL. The basic issues are:
  The 200 KHz wide channel, with the assumed device NF of 5dB, would have noise floor of -116dBm, while a 3.75 kHz channel would have -133 dBm noise floor. The 17dB noise level difference has made EC-GSM unnecessarily challenging without any extra gain.
  The short symbol duration would not help neither.
Hence repetitions are adopted for longer signal energy accumulations.
However effective accumulation is challenging in noise dominated case, in particular, it has particular repetition burst phase requirements which is difficult to guarantee in CC6.

## Slide 3: The EC-GSM requirements on device Tx and BTS Rx
Blind IQ combination of received burst samples
  Receiving end (for both BTS and CIOT devices) needs to know the timing, carrier frequency offset (CFO), and random phase of bursts while signals are below the noise floor.
Detection and compensation of frequency offset
  There is no phase lock mechanism between CIOT devices and BTS.
  Traditionally MSs read DL signal every frame for frequency and time tracking, which is SNR dependant, e.g. CFO follow normal distribution of N(0, 30) in 900 band when SNR is around 4dB.
  In CC6, where CDMA OL is needed, CFO = N(0,10) Hz is assumed for CDMA OL to work well. However the CC6 SNR are mostly < -5dB.
  Hence, it is difficult to achieve N(0,10) in AWGN dominated case. Legacy GPRS would need 2 min based on FCCH repetition rate.
  Introduction of Overlaid CDMA to support improved UL capacity.
  CIOT device needs to control relative phase of repetition bursts, and it is particularly important for OL CDMA.
  Ref 2 has proposed a new method to apply the CDMA phase codes, while the example given works, a few more cases from ref 3 revealed issues of it.

## Slide 4: CFO and random phase impact to blind combine
Blind combine is needed on both UL and DL Rx to accumulate signal energy in AWGN dominated RF condition, as shown by green arrows, to be stronger than the noise and interference, and surpass SNR gating to reach EQU stage
  However it is sensitive to the relative phase of each contributing burst. In reality the blind combine is likely to follow red and blue arrows due to CFO, and could not reach AWGN level, as illustrated of IQ vector signals in the form of repetitions.
  Rx on both CIOT device and BTS side needs to know the phase shifts of the signals below the noise, and correct them more accurately than current GSM handset in order to achieve effective combine. The challenge is to know CFO accurately enough for correction, while they are below the noise floor, in order to have desirable combine.
No guaranteed positive results, as signals to combine are below noise level, and not recognisable.
CFO = 0 Hz
(CFO = LO_fRx – LO_fTx)
CFO = 15 Hz for consecutive frame combine (e.g. EC-RACH);
CFO = 120Hz for consecutive TS combine (e.g. CDMA OL on EC-PDTCH).
SNR gating for EQU/burst processing
  Two types of blind combine have different CFO sensitivities:
    TS based CDMA OL on UL, a continuous Tx case, such as EC-PDTCH, is less sensitive due to smaller phase shift since the smaller time step (557µs) than b between consecutive burst repetitions. Such kind of consecutive TS combine also exists for DL for device’s Rx. Currently no GSM handset is capable of making effective live NW signal combine below noise level.
    Frame based discontinuous Tx case, such as, EC-RACH combine, is 8x more sensitive than the above, as time step is 8x more (4.615ms) than a, hence phase shifts are 8x more sensitive to CFO than a.
CFO < 0
CFO > 0
AWGN level

## Slide 5: EC-GSM burst phase dependent issues
EC-GSM assumed CIOT device has the same capability of BTS in terms of LO phase continuity for Tx and Rx, hence proposed blind combine, which is fundamental to EC-GSM.
  A few fundamental PHY layer details at IQ level have been overlooked;
For CDMA OL (burst by burst repetitions)
  BTS Rx functionalities expect CIOT devices' Tx to follow BTS command on the CDMA phase codes for each repetition burst, as that is essential for CDMA OL.
  Detailed check of CDMA codes in Ref 3 by the proposal in Ref 2 showed that only some combinations of phases can be done, while others are conflicting with GMSK modulation.
For none CDMA OL repetitions (frame by frame)
  CIOT devices and BTS are running on independent LOs, and there is no phase lock mechanism between them, hence a random starting phase is reflected in the TS 45.004, and it would not be realistic to expect the absolute phase to be suitable for blind combine in EC-GSM proposal, especially when the signal is below the noise level.
  Unlike BTS has dedicated Tx and Rx chains working continuously, GSM handsets keep tuning between Rx and Tx, hence no phase continuity for effective blind combining. This would be detrimental for EC-GSM blind combine.
    To BTS Rx, all bursts sent on frame by frame basis from current GSM handset would have random phases to other bursts, hence multiple bursts combine could end up cancelling of the wanted signal (please see animation on random phases).
    To CIOT device Rx, all the repetition bursts on DL bursts, although having phase continuity from BTS, would not have phase continuity due to CIOT device tuning between Tx and Rx bursts, hence having the same blind combine issues of cancelling the signals.

## Slide 6: The two OTA GMSK bursts on two frames (1250 T apart) happen to be 180o apart, blind combining would cancel the signal rather than enhance it
Taking the real GPRS handset bursts IQs OTA, the green arrows indicate the starting phase of the bursts, and the red arrows the ending phase of the bursts. Each burst are 148T in length.
More bursts were also close to 0o and 180o phases, not as random as RACH repetitions, but it cannot be relied upon.

## Slide 7: GSM handset with repeated RACH shows random phases on frame by frame basis
The random phases over many frame by frame RACH repetitions, captured on a real GSM handset over the live NW shows the blind combine would not gain as much as expected (actually nothing in this case). The EC-RACH sent in this way would effectively cancel itself.
Click the figure to see 63 repetitions of RACH burst phase distribution along 67 GSM frames.
All RACHes are from a commercial GSM UE, and have been post-processed with CFO correction (min EVM based).

## Slide 8: Phase drift between Tx & Rx LOs in continuous operation
Number of contiguous bursts (16.5 sec continuous Rx of a BCCH ARFCN)
A GMSK receiver with a good TCXO (25ppb) is tested with Agilent 8960 callbox BCCH for phase drift study in a continuous operation.
The graph here shows the burst phase variations for 70 x 51 multi-frames (28560 bursts, 16.5 sec). It shows that phase, as a result of CFO, is varying by ±120 rad (less than ±20Hz, and within 25ppb) in 8 sec.
The phase drift of each test is different, hence each CIOT device is going to drift differently. This is one of the limiting factor for CDMA OL, as ciot device each has its own CFO.
Tracking each of the CDMA co-user in CDMA OL is needed, and FFS.
While this plot is for gaging the rate of phase change, it worth noting that 0.1ppm Ciot device and 0.05 ppm BTS could be 6x worse than this one, as the test was made with TCXO 25 ppb TCXO.

## Slide 9: The accuracy of the relative phase of repetition and the effect of the orthogonality leakage
The low cost ciot device is assumed to perform ACQ through repeated DL FCCH and up to 7 EC-SCH repetitions, as it is essential to be in sync with NW on both time and frequency
  the more accurate the relative phase, the less the orthogonal leakage among co-users, hence the better CDMA OL mechanism, and the more repetitions and more users can be served effectively.
  Otherwise the UL capacity would be dented a lot.
The Time and Frequency accuracy needs to be maintained whenever CDMA OL is used. It means
  FCCH and EC-SCH must be repeatedly monitored
  Current consumption increases, and battery life is FFS.
GSM ACQ performance is not good enough for CDMA OL, yet in CC6 cases the SNR is 10 dB worse than GSM:
  It is most likely 0.1ppm CFO is not good enough, as the CDMA OL mechanism needs smaller CFO than the existing GSM MS, i.e. N(0,3) Hz, as it relies on the relative phase accuracy of each repetition from multiple ciot devices
    0.1ppm in low band is about 100Hz CFO, and N(0,30), clearly in EC-GSM Ciot device needs to be 10 times better on frequency tracking while the SNR is 10dB worse.
    Accurate Time and frequency tracking are fundamental for OL CDMA.
  CC6, the 20 dB extra MCL area, is AWGN dominated, and possibly with interference area
limitations are foreseen with EC-GSM proposal, and Rx enhancement is a must (current receivers cannot meet such performance)
  As the repetition is needed for getting the meaningful signal, DL coverage would be the first limitation. The major limiting factor is the challenging requirement on frequency tracking to avoid phase uncertainty of blind combine when signals are below the noise.
  The CDMA co-users would have independent CFOs, and it is not clear how to deal with the orthogonal leakages due to this factor.
  The current CDMA OL code implementation in Ref 2 can work for some CDMA codes, but not others.
  For keeping the phase continuity, the device must not tune away as often as GSM. This in turn impacts the AFC. Losing AFC performance certainly impacts the phase alignment required for blind combine.

## Slide 10: Conclusion
This contribution has highlighted the need for accurate phase alignment for EC-GSM to work well, due to the use of blind (IQ) combining and OL CDMA; however it is a challenging task to determine accurate CFO and phase from a burst in CC6 due to the negative SNR at high MCL.
EC-GSM phase requirements are very challenging. The practical achievable level of frequency tracking and coverage in noise dominated conditions (CC6, i.e. SNR<-5dB) is questionable and needs further study.
Due to the requirement to operate in very low SNR for each burst repetition, there are potential issues with blind combination of IQ samples in CC6, and this needs further study.
The approach for handling different CFO from CDMA co-users needs further study.
There are elements of CDMA OL phase code issue with the latest contribution (ref 2). Certain Fourier codes (ref 3) are found to be unachieved by the proposed method.
In noise dominated conditions, CIOT devices may have to re-sync their frequency reference to enable good CFO=N(0,10) for the desirable performance at the BTS. The battery life impact is FFS.
For burst repetitions (especially when non-contiguous), the start phase for each legacy GSM burst is unconstrained, as TS 45.004 states (i.e. the phase is not required to be deterministic between bursts).
  Therefore, it is not clear that all legacy GPRS devices can support EC-GSM simply through a software upgrade.
  In other words, this is an implementation issue that would require detailed analysis, and there is no guarantee that legacy devices can support the phase continuity across different bursts that is required by EC-GSM to achieve the coverage performance

## Slide 11: References
TR 45.820v1.3.0 section 6 EC-GSM
GCP150434 EC-GSM, Coherent transmission and reception
GP-150355 EC-GSM, Overlaid CDMA for extended coverage