## Slide 1
Latest Status of the Clean Slate
Track of Activities
Chris Pudney
Vodafone Group plc (Rapporteur: FS_IoT_LC)

## Slide 2: Outline
Introduction to Cellular IoT (FS_IoT_LC)
  Objectives
  Timeline
Clean slate solutions
Narrow Band M2M (NB M2M)
  Status of evaluation against objectives
Narrow Band OFDMA (NB OFDMA)
  Status of evaluation against objectives
Potential Work Item phase
  Template for RAN WID
  Planned meeting schedule

## Slide 3: Introduction to FS_IoT_LC
In GERAN#62 (May 2014), a study item on “Cellular System Support for Ultra Low Complexity and Low Throughput Internet of Things” was approved.
Objectives of the study:
  The main objective of the study is to evaluate how to support low throughput and low complexity Machine Type Communications.
  Different solutions can be investigated, e.g. a non-legacy based design, and/or a backward compatible evolution of GSM/EDGE.

## Slide 4: Objectives of Fs_IoT_LC
  Provide a data rate of at least 160 bps (on both the uplink and downlink) at the (equivalent of) the SAP to the SNDCP layer with the aim of achieving an extended coverage of 20 dB compared to legacy GPRS (Non EGPRS).
  Scale to support a massive number of MTC Mobile Stations
  Reduce power consumption of MTC Mobile Stations compared with legacy GPRS (non EGPRS) so that they can have up to ten years battery life with battery capacity of 5 Watt-hours
  Maximise the reduction in complexity of the Mobile Termination compared to that of a legacy GPRS (non EGPRS) MT

## Slide 5: Objectives of Fs_IoT_LC (contd…)
  Avoid negative impacts to legacy GSM/WCDMA/LTE system(s) deployed in the same frequency band and adhere to the regulatory requirements applying to the spectrum bands in which the system operates.
  Minimise impacts to the GPRS/EDGE base station hardware.
  Identify Core Network Architecture, security framework and Radio Access Network-Core Network interface (e.g. S1 or Gb), and associated protocol stacks, suitable for the M2M market in the 2017 and onwards timeframe.
  For both options:
    There is no requirement for inter-RAT mobility.
    Intra-RAT mobility is assumed to be based on cell reselection.

## Slide 6: Timeline of Study Item
GERAN#62 (May 2014) – SID approved
GERAN#65 (March 2015) – v1.0.0
GERAN#66 (May 2015) – v1.3.0
Future meeting calendar
GERAN 1/2 CIoT ad hoc#3, 29 June – 2 July 2015
GERAN#67 (August 2015) – Conclude the study (exp)

## Slide 7: Clean Slate Solutions
As of GERAN#66 (May 2015), the candidate clean slate solutions are:
  Narrow Band M2M (NB M2M)
  Narrow Band OFDMA (NB-OFDMA)

## Slide 8: Narrow Band M2M (NB M2M)
Downlink physical layer design
Uplink physical layer design
Link layer aspects
Radio resource management
Concept evaluation

## Slide 9: Status of Evaluation against objectives

## Slide 10: Narrow Band OFDMA (NB-OFDMA)
NB-OFDMA Physical layer design
NB OFDMA MAC layer

## Slide 11: Status of evaluation against objectives

## Slide 12: Potential Work Item phase
Template for RAN WID
Planned Meeting Schedule
  RAN 1/2: 5 – 9 October 2015, Malmo, Sweden
  RAN 4: 12 – 16 October 2015, Sophia Antipolis, France
  RAN WGs: 16 – 20 November 2015, Anaheim, USA
  RAN 1/2 ad hoc: 14 – 18 December 2015, TBD
  RAN 1/2 bis: 11 – 15 January 2016 TBD
  RAN WGs: 15 – 19 February 2016, Malta
Additional meetings