## Slide 1
RP-231245
3GPP TSG RAN Meeting #100
Taipei, June 12-14, 2023
Source: Huawei, HiSilicon
Title: Characterization and form factor for 2Rx XR wearable devices
Document for: Discussion and decision
Agenda Item: 9.3.2.9

## Slide 2
Background of “2Rx relaxation for XR wearable devices”
Discussion history in RAN plenary
  Firstly raised in RAN#96.
  RAN#99 conclusion: endorse way forward in RP-230740
Issue firstly raised
Issue re-submitted, but no discussion
Issue re-submitted, had some discussions, but no conclusion
Endorsed a potential way forward (see RP-230740)
202206 (RAN#96)
202209 (RAN#97)
202212 (RAN#98）
202303 (RAN#99)
RAN#98 discussions (copied from moderator summary RP-223504)
  What type of XR devices can have 2Rx relaxation, what are the exact physical (e.g form factor) limitations that make such a relaxation for these XR devices important?
  How to identify these XR devices in the network?
  How to prevent mis-use of the 2Rx relaxation by other devices (e.g. smartphones)?
  Is any further relaxation foreseen to be needed for these devices, e.g. on BW?
  ……
Expected to be discussed and find a way forward
202306 (RAN#100)
RAN#99 discussions (Endorsed way forward below)

## Slide 3
Discussion – Time plan to address XR 4Rx vs 2Rx issue
XR is one important industry to expand the value for 5G-Advanced
  Annual shipments of XR devices are increasing: about 15 million in 2022, and will go to 26/45 million in 2023/2025 (From Omida [1]).
  Timely readiness from devices helps building up the eco-system of 5G XR industry.
  For XR devices that do have difficulties to support 4Rx (e.g., glasses), lack of 3GPP standards support may decrease the industry interest for applying 5G to XR.
Q1: Time plan for 3GPP to resolve XR 4Rx vs 2Rx issue needs to be discussed according to the marketing trends
  Based on the above, it is better to resolve this issue within Rel-18 timeframe, otherwise the opportunities for cellular system to support XR industry could slip.
  The most important thing for RAN#100 is to decide which type of XR devices do have difficulties for supporting 4Rx.
  Once the above is decided, the remaining work is to provide a suitable mechanism to identify these type of XR devices
    WG-level discussion is required
    Considering some legacy mechanism (e.g. SPID) can be potentially reused, 2 or 3 WG meetings could be sufficient
    RAN#102 can have a final decision on the identification mechanism
  Proposal 1: It is suggested to resolve XR 4Rx vs 2Rx issue in Rel-18 in 3GPP RAN as per the below time plan
  RAN aims to decide which type of XR devices has difficulties to support 4Rx at RAN#100
  RAN2 and RAN4 are tasked to provide candidate solutions to identify this type of XR devices in the network in 2023 H2
  RAN aims to conclude the identification mechanism at RAN#102
[1] https://omdia.tech.informa.com/pr/2023/02-feb/omdia-near-eye-display-shipments-for-xr-applications-will-grow-by-67-in-2023-thanks-to-the-new-model

## Slide 4
Discussion – Technical consideration on XR 4Rx vs 2Rx
  Q2: Ambiguity of the type of XR devices which has difficulty to support 4Rx
  The typical equipments for XR applications are mainly headset and glasses.
    For headset, the size is large enough to mount 4Rx.
    For glasses, the size is small and there is also requirement for the weight (otherwise it is difficult for end users to wear it for a long time).
    Other form factors of XR devices are not seen any bottleneck to support 4Rx.
  Proposal 2: Only define XR wearable glasses for 2Rx XR, as other types of XR devices do not have limitation to support 4Rx (below is one example on how to define it in 3GPP)
  Wearable Glasses XR UE: A wearable glasses UE that supports XR services and is worn on the head, which has a different form factor in contrast to smartphones and XR headsets.
XR headset
XR glass

## Slide 5
Discussion – Technical consideration on XR 4Rx vs 2Rx
  Q3: How to identify 2Rx XR devices in the network
  To further provide flexibility for the network to handle different types of UEs, potential solutions can be further studied.
    Option 1: similar mechanism as REDCAP, e.g. MSG1/MSG3 early identification
    Option 2: similar mechanism as 2Rx for vehicles, e.g. a new SPID (Subscriber Profile ID for RAT/Frequency Priority) value for 2Rx XR devices
  Proposal 3: RAN WGs to further study options for identifying 2Rx XR devices and existing mechanism is preferred to be re-used if possible.
  Q4: Risks on 4Rx mandatory support for smart phones
  The 2Rx XR device type may degrade the performance than UEs supporting 4Rx and therefore it is vital that any potential relaxation of 4Rx to 2Rx shall not impact smart phones.
  In addition to limiting the device type as above, in RAN4 and RAN5, the corresponding requirements and testing shall also be clearly defined to differentiate 2Rx XR device type from smart phones.
  Proposal 4: RAN4 and RAN5 shall clearly differentiate the requirements and test cases between smart phones and the XR device type supporting 2Rx, to ensure 4Rx mandatory support for smart phones is not relaxed.

## Slide 6
Summary
According to the discussion, there could be potential resolutions to address the concerns, and therefore the following way forward is proposed:
  Proposal 1: It is suggested to resolve XR 4Rx vs 2Rx issue in Rel-18 in 3GPP RAN as per the below time plan
  RAN aims to decide which type of XR devices has difficulties to support 4Rx at RAN#100
  RAN2 and RAN4 are tasked to provide candidate solutions to identify this type of XR devices in the network in 2023 H2
  RAN aims to conclude the identification mechanism at RAN#102
  Proposal 2: Only define XR wearable glasses for 2Rx XR, as other types of XR devices do not have limitation to support 4Rx (below is one example on how to define it in 3GPP)
  Wearable Glasses XR UE: A wearable glasses UE that supports XR services and is worn on the head, which has a different form factor in contrast to smartphones and XR headsets.
  Proposal 3: RAN WGs to further study options for identifying 2Rx XR devices and existing mechanism is preferred to be re-used if possible.
  Proposal 4: RAN4 and RAN5 shall clearly differentiate the requirements and test cases between smart phones and the XR device type supporting 2Rx, to ensure 4Rx mandatory support for smart phones is not relaxed.