## Slide 1: Discussion on Rel-18 further NR coverage enhancements
3GPP TSG RAN Meeting #100
Taipei, June 12 - 14, 2023
Source: ZTE, Sanechips
Agenda Item: 9.3.1.3
RP-231406

## Slide 2: Backgroud
It was agreed that final selection of the MPR/PAR reduction methods should be based on net coverage gain results combining transmitter and receiver performance, and the calculation/metric for net gain were apporved in RAN4 #106-bis-e meeting.
In previous RAN4 meetings, RAN4 provided performance evaluation on the selection of MPR reduction schemes, where both frequency ranges (700MHz and 4GHz) are evaluated.
However, no conclusions were reached on the choice between transparent schemes and non-transparent schemes due to different observations from companies.
Also no conclusions on the modifications for RAN4 specification due to missing conclusion on the solution to be considered for MPR/PAR reduction.
The net-gain results from the inputs of different companies were summarized and captured in the R4-2310303.

## Slide 3: Some observations from the results in RAN4 evaluations
The summary for the results in RAN4 evaluation can be found in R4-2310304, in which it was observed that there are positive net-gain for the agreed transparent and non-transparent schemes compared to the baseline, at least when power-boosting is enabled.
However, different companies showed different evulations results on the amount of MPR for different schemes for different configurations, and the results vary quite a bit. It should be noted that not all companies provided results for all configurations, boosting/not, inner/outer, filter type etc.
  Some companies’ results showed transparent schemes performs better than FDSS-SE in some RB allocation configurations, i.e. at inner allocation with certain parameter settings;
  While some other companies’ results showed FDSS-SE performs better than transparent scheme in some other RB allocation configurations, i.e. at outer allocation with certain parameter settings.
FDSS-SE gains over transparent schemes vary with parameter settings: RB size, inner/outer, MCS index, filter type
  Gains may be limited in the edge PRBs when the larger BW/RB is allocated, even gain would be lost in the inner PRBs compared to transparent schemes

## Slide 4: Comparison of transparent techniques and non-transparent techniques
Transparent techniques such as FDSS w/o. SE scheme:
  Simple to be implemented
  Low impact on baseband processing
  Low optimization effort during implementation
  Less RAN4 specification work:
    Spectrum flatness requirement, update MPR table(s), power boost related requirements
  No RAN1 specifications impact.
Non-Transparent techniques such as FDSS-SE scheme
  High optimization effort during implementation
  Extension factor and the adapted MCS should be considered additionally which cause high optimization effort during implementation
  The various data needs to be stored in the UE with large tables creating additional costs as more memory is required
  More RAN4 specification work:
    Spectrum flatness requirement, update MPR table(s), power boost related requirements, In-band emission and EVM requirements
  RAN1 specifications impacts.

## Slide 5: Proposal
Proposal: Due to limited TU left, RAN4 focuses on transparent scheme for MPR/PAR reduction.
  No RAN1 specification impact is expected.

## Slide 6: Thank you