## Slide 1: Network Energy Saving Enhancements in Rel-19
Bangalore, India, September 11th – 15th, 2023
Agenda item: 8A.2.5
Source: Nokia, Nokia Shanghai Bell
RP-231891 3GPP RAN#101

## Slide 2
Overview
Motivations and key proposals for network energy saving enhancements in Rel-19
Energy efficiency is key for mobile networks in general
  It needs to be considered system-wise as well, in all relevant WIs
In Rel-18 only a few of the enhancements identified in TR38.8641 are being specified
  Given that different techniques apply to different deployment and operating points of the system, it is important to continue the work in Rel-19 with relevant techniques
  Another aspect to consider is that Rel-18 has focused primarily on RRC Connected, and hence in Rel-19 the focus should be on RRC Idle/Inactive states and low load scenarios
Some key principles can be considered for Rel-19 normative work:
  Avoid techniques that reduce flexibility for network
  Avoid techniques that constrain gNB implementation
  Legacy devices, and coexistence with them, need to be supported, but not necessarily always on all cells
  Any techniques requiring waveform modifications should wait for 6G
1TR38.864 “Study on Network Energy Savings for NR”
Key areas for enhancements:
SSB/SIB1-less cell and on-demand SSB/SIB
Paging enhancements for low load scenarios
Enhancements for cell shutdown

## Slide 3
SSB/SIB1-less cell
SSB/SIB1-less cell:
Justification:
  Up to Rel-18, a cell needs to transmit SSB and SIB1 regularly to be able to serve RRC IDLE and RRC INACTIVE Ues
  In Rel-19, it would be beneficial to eliminate unnecessary transmissions of SSB and SIB1, and even to eliminate SSB/SIB1 altogether in certain scenarios
  SSB and SIB1 transmissions by a (capacity) cell are unnecessary in collocated scenarios whenever the device would be able to acquire system information and perform the synchronization operation relying on SSBs/SIB1 transmitted by another (collocated) cell.
  Currently, SSB-less SCell is supported for intra-band CA, and SSB-less SCell for the inter-band CA scenario is to be specified in Rel 18, but they support only RRC Connected UEs.
Objective:
  The SSB-less cell operation should be extended so that an SSB-less cell can serve both RRC Connected UEs and at least partially UEs in RRC IDLE/INACTIVE UEs, enabling for example synchronization, paging procedures and/or initial access.
  It can be applied to collocated intra-band contiguous scenarios, and to collocated intra-band non-contiguous and inter-band scenarios reusing the requirements defined in Rel-18.
SSB/SIB1-less cell
SSB/SIB1*
Paging / Initial Access
* May include cross-carrier system information
Coverage Cell
SSB/SIB1-less Capacity Cell

## Slide 4
On-demand SSB/SIB1
On-demand SSB/SIB1 cell:
Justification:
  Up to Rel-18, a cell needs to transmit SSB and SIB1 regularly to be able to serve RRC IDLE and RRC INACTIVE Ues
  In Rel-19, it would be beneficial to eliminate unnecessary transmissions of SSB and SIB1
  SSB and SIB1 transmissions by a (capacity) cell are unnecessary also in non-collocated scenarios whenever there are no devices in RRC INACTIVE/IDLE present that benefit from the signalling
Objective:
  Enable UE triggering on-demand SSB/SIB1 transmission upon need, by sending an uplink wake-up-signal (UL-WUS) to enable UL data transmissions (see figure).
    This technique may require the cell to transmit Discovery Reference Signal DRS (e.g., simplified SSBs) to announce its presence and to support cross-carrier system information (e.g. for UL-WUS configuration).
    A legacy signal or channel can be re-used for UL-WUS transmission such as a PRACH preamble.
    This technique can be supported at least by UEs in RRC IDLE and RRC INACTIVE.
On-demand SSB/SIB1
Legacy PRACH-based wake-up signal **
On-demand
SSB/SIB1 transmission
** May require discovery reference signals (DRS) or cross-carrier system information (WUS config)

## Slide 5
Clustered paging
Paging enhancements for low-load scenarios
SSB
NW paging window
Time
NW paging window
Paging cycle
SSB
SSB
SSB
SSB
UE ID based Paging Occasion (legacy)
(1) Clustered paging (technique A-1-4 in TR 38.864)
Justification: Currently UEs’ paging occasions are distributed in the time domain, which negatively impacts the RAN sleeping opportunities
Objective: reducing the number of paging transmissions in low-load scenarios
  By clustering in time the paging of Rel19 UEs in fewer Paging Occasions
  Legacy UEs can continue using legacy paging
(1) Clustered paging in low load scenarios
(2) AMF paging considering RAN nodes’ availability for paging
Justification: Cell shutdown (and other NES states) of a RAN node impacts the availability of the RAN node to do paging (e.g. a small cell will be unavailable during nighttime when it is deactivated)
Objective: AMF should be aware of the (un)availability for paging of the RAN nodes that are recommended for paging so that it can page a UE accordingly
  No impact foreseen to legacy UE.
AMF
AMF selection of RAN node for paging considering (un)availability for paging of the RAN nodes that are recommended
Availability for paging
(2) RAN nodes’ availability for paging

## Slide 6
Enhancements for cell shutdown
Motivation:
The cell shutdown procedure is one of the most energy-effective means used to save power, but it is currently relatively slow.
In Rel.18, CHO enhancements are considered primarily for robustness of traffic offloading at cell shutdown.
(1) gNB-DU autonomy for cell shutdown
Currently, gNB-CU is responsible of cell switch OFF and ON decisions, and then gNB-CU indicates the decision to gNB-DU for the gNB-DU to initiate offloading and cell deactivation.
  However, cells are managed by the gNB-DU, which is aware of cell load and energy consumption information.
  Thus, gNB-DU autonomous decisions for cell shutdown would be beneficial as the gNB-DU is more capable of determining the possible gains, and can make the procedure faster
  To enable gNB-DU autonomy, new F1-C signalling is necessary
(2) Enable faster decrease of SSB transmit power at cell shutdown
  Cell deactivation is done by multi-step SSB power ramp down (i.e. graceful shutdown), which is slow as it requires SI modification.
gNB-DU autonomy for cell shutdown
Cell 1
CU
DU
Cell 2
Cell 2 shutdown decision at DU
List of cells for gNB-DU autonomous cell shutdown decision
(3) Enable finer control of cell reselection procedures at cell shutdown
  Currently, the network cannot flexibly control to which frequency layer UEs should reselect, after the cell in which they are camping is shutdown.