## Slide 1: Views on NTN for Rel-19
3GPP TSG RAN Meeting #101
Bangalore, India, September 11-15, 2023
Source: ZTE, Sanechips
Agenda: 8A.2.7
RP-232154

## Slide 2: Overview
In Rel-17, the basic architecture of NTN has been established to enable this “new direction” for both NR and IoT device with the following essential assumption:
    Pre-compensation at UE side to simplify the implementation and spec efforts.
    Transparent payload with flexibility to select the Reference point for DL and UL synchronization, which is used to match the different implementation, e.g., co-located gNB & gateway.
    Either one or multiple beams per cell can be supported for NR and IoT according to the RAT, scenarios and implementation, etc.
  The initial trial for commercialization usage are also conducted based on the Rel-17 spec [1][2][3];
    [1] https://www.zte.com.cn/china/about/news/20220826C6.html
    [2] https://finance.sina.com.cn/tech/roll/2023-05-16/doc-imytyfac0093812.shtml
    [3] https://www.zte.com.cn/china/about/news/20230119c2.html;
  In Rel-18, additional enhancements are introduced for both NR- and IoT-NTN with limited scope.
  For Rel-19, the study and potential specified work for NTN should focus on the “essential issue”, which is critical for the deployment of NR-/IoT-NTN and improvement of performance to enable the service.
Essential aspects including performance improvement targeted for the real deployment should be the focus of NTN in Rel-19
instead of “fancy” scenario and functionality .

## Slide 3: Scope of NR-NTN in Rel-19
  DL enhancement:
    Motivation: The DL coverage of NTN system has been impacted by several factors, e.g., power sharing in case of multiple satellite beams. Meanwhile, to support the NR deployment, the target scenario should focus on the LEO@600 km similar to UL enhancement in Rel-18. As the basic assumption for the evaluation, the following two aspects should be considered:
      The realistic assumption of Satellite EIRP density for each beam.
      The maximum available payload and number of simultaneous beams.
    Objective:
      The identification of the bottleneck channel should be considered based on the evaluation and link budget assessment.
      For the detailed approaches for enhancement, both link-level and system-level methods should be considered. More specifically,
        For the link-level enhancement:
          This solution is to improve the link budget for certain channel and among all potential features, the NTN-specific enhancement, i.e., the mitigation of polarization loss, is important to achieve round 3 dB gain. Then, compared to the cell-level indication supported in Rel-17, the indication of polarization information in scheduling-level or beam level is needed.
        For the system-level enhancement:
          This solution is to optimize the system level power allocation per beam with well matching between the beam and scheduling. In this case, the maximum available payload and number of simultaneous beams should be considered. As one example, for the transparent payload, the support of NCR over NTN can be considered.
Proposal-1: For NR-NTN in Rel-19, the DL enhancement can be considered with link-level and system enhancement.

## Slide 4
  Notification/alter message
    Motivation: The intention of this enhancement is to directly indicate the “assistance information” to the “end user” to inform the required information once the signal quality is poor, e.g., due to the large clutter loss in NLoS or self-blockage when the phone is in the pocket, e.g., the UE is in idle or inactive mode.
    Objective: Considering the general impacts on the additional loss, all channels can be affected. Then, the comprehensive should be considered at least with the following cases:
      Case-1: UE with detected synchronization signal but failed to receive others.
      Case-2: All channels includes SSBs failed.
    Then, once the prioritized case is identified firstly, the corresponding enhancement,
    e.g., design of the mechanism for altering, should be considered.
Notification, e.g., poor channel
User
Proposal-2: For NR-NTN in Rel-19, the notification/alter message can be considered with identification of target scenario firstly.
  Mobility enhancement including
    Cell reselection enhancements
      Further optimization on the Time and location based cell reselection enhancements, e.g., Introduce a distance threshold to help down scope the candidate cells for reselection, Prioritize neighbour cells with longer valid time, e.g. longer than a threshold.
      Prioritize TN over NTN or vice versa
        Indicate neighbour cell type (TN or NTN) to UE, e.g., Per frequency indication + NTN cell list.
        Introduce reselection priority offset/cell specific offset to prioritize all the frequencies/cells for a certain NW type.
      Autonomous search for TN/NTN cells when camping on a NTN/TN cell, e.g., An indication is provided from the camped NTN/TN cell to UE to enable autonomous search for TN/NTN cell, and A proximity indication can be sent to the network to indicate that the UE is entering or leaving the proximity of one or more TN/NTN cells which are detected based on autonomous search function.

## Slide 5
    Reduce signalling overhead in NTN-NTN mobility
      HO command based on configuration index
        Define and provide a list of default configuration to UE and each configuration is associated with a index
        The index associated with certain default configuration will be provided in HO command.
      Group based measurement report and mobility
        NW categorize multiple UEs into one group and assign group id.
        Measurement report can be sent from one UE to trigger HO of all the UEs in the same group.
    Address PCI confusion in NTN-TN mobility
        CGI always included in the measurement results for NTN cells to avoid PCI confusion.
Group based measurement report and mobility
Address PCI confusion in NTN-TN mobility
Proposal-3: For NR-NTN in Rel-19, the cell reselection and mobility enhancement can be considered.

## Slide 6
  Views on other aspects:
    UE without GNSS: This aspect should be deprioritized due to the unclear use case, spec effort and non-backward compatible with legacy device for NR-/IoT-NTN.
    Regenerative satellite: This aspects should be deprioritized due to the unclear benefits and specific impacts. More specifically
      For the full-gNB onboard, based on the existing spec, this architecture can already be supported via the implementation, e.g., proper configuration of Common TA and K_mac. For other architecture, e.g., CU-DU split or other, considering dynamic topology due to the movement of satellite, the cost to support split architecture is much larger compared to the TN. Meanwhile, from the perspective of the standardization, since the ISL and feederlink is out of scope of 3GPP, without touching the implementation of these links, it’s failed to identified the gap to support the NG- or F1-interface.
      Additionally, the benefits is not clear since the end-to-end latency is almost same since the CORE-network is still on the ground.
Proposal-3: For NR-NTN in Rel-19, the following aspects should be deprioritized:
UE without GNSS
Regenerative satellite

## Slide 7: Scope of IoT-NTN in Rel-19
  Support the NB-IoT operation in NR in-band over NTN
    Motivation: This feature is already supported in TN network, can be easily supported NTN case, which is beneficial to enable efficient usage of spectrum & satellite capability.
    Objective: This work is mainly done in RAN4.
  5GC supporting IoT-NTN
    Motivation: In Rel-17/18, the IoT with connection to EPC is supported in NTN case. Considering the flexible network deployment, e.g., shared infrastructure for different RAT over satellite, it’s beneficial to enable this feature similar as TN.
    Objective: RAN2/3 work is required to specify the corresponding enhancement.
  Capacity enhancement (mainly for GEO)
    Motivation: The GEO based IoT service is the promising the direction due to the mature eco-system, e.g., reframing of existing GEO constellation with lower cost, available spectrum mainly for L- and S-band usage. From coverage perspective, the large beam footprint will provide the seamless coverage over huge region As analyzed in TR38.821 and TR 36.763, there is potential limitation on the PRACH capacity, also paging capability if large number of UEs (e.g., IoT device) is supported. However, it was concluded that the potential issue of RACH congestion is not to be studied further within Release-17 timeframe.
    Objective: The enhancement on the capacity of UL channel should be considered in RAN1 and RAN2.
  Proposal-4: For IoT-NTN in Rel-19, the following aspects are prioritized:
        Support the NB-IoT operation in NR in-band over NTN
        5GC supporting IoT-NTN
        Capacity enhancement for UL channel (mainly for GEO)

## Slide 8: Conclusion
Based on the analysis before, regarding the scope of NR-NTN and IoT-NTN in Rel-19, following proposals are listed:
  Proposal-1: For NR-NTN in Rel-19, the DL enhancement can be considered with link-level and system enhancement.
  Proposal-2: For NR-NTN in Rel-19, the notification/alter message can be considered with identification of target scenario firstly.
  Proposal-3: For NR-NTN in Rel-19, the following aspects should be deprioritized:
        UE without GNSS
        Regenerative satellite
  Proposal-4: For IoT-NTN in Rel-19, the following aspects are prioritized:
        Support the NB-IoT operation in NR in-band over NTN
        5GC supporting IoT-NTN
        Capacity enhancement for UL channel (mainly for GEO)