## Slide 1: WF on potential RRM objectives for NR-NTN deployment in above 10 GHz (NR-NTN-enh WID)
Source: Thales
3GPP TSG-RAN Meeting #101
Bangalore, India, September 11-15, 2023
Agenda Item: 9.3.2.7
RP-232693
Rev from RP-232687

## Slide 2: TDoC considered in the discussion
TDOC | Type | Title | Source | Comments
RP-232039 | discussion | On the scope of Rel-18 NR NTN enhancements | Samsung | Proposal 2 : Including the following as a sub-bullet under objective 4.1.2 “Specify necessary RRM requirements for NR-NTN UEs operating in the NTN example band (i.e. Ka band) based on associated assumptions of the UE architecture (including beam steering capabilities) .”
RP-231533 | LS in | LS on RAN4 RRM work scope for NR NTN Ka band (R4-2314484; to: RAN; cc: -; contact: Thales) | RAN4 | RAN4 discussions are still ongoing on how to define RRM requirements. However, RAN4 RRM is happy to announce that the scope of the work needed to define the RRM requirements (i.e. beam steering related) necessary for NR-NTN UEs operating in the NTN example band (i.e. Ka band) based on associated assumptions of the UE architecture has been identified

## Slide 3: Rel-18 NR-NTN-enh WID: RRM req for Ka band
Proposal 1: As part of the NR-NTN-enh WID, RAN4 shall work on the definition of RRM requirements considering the following
  cases: Case-1: Stationary UE for GSO; Case-2: Stationary UE for LEO; Case-3: Mobile UE for GSO
  UE architectures: Fully electronically-steered beam UEs (Type 1); Fully mechanically-steered beam UEs (Type 2)

## Slide 4: Rel-18 NR-NTN-enh WID: RRM req for Ka band
Proposal 2: The RRM requirements for example band (Ka band) to be defined by RAN4 are listed in the table below
RRM requirements to be defined as part of Rel-18 NR-NTN-enh WID | Electronic steering antenna | Mechanical steering antenna
 | Terminal Type 1 | Terminal Type 2
§UE uplink timing accuracy | Y | Y
§RRC IDLE and INACTIVE mobility | L | N
§(Conditional) Handover | Y | Y
§RRC Re-establishment | L | N
§RRC Connection Release with Redirection | L | N
§Radio Link Monitoring | Y | L
§Link Recovery procedure (BFD/CBD) | L | N
§Active TCI switching | Y | N
§Measurement Procedure | Y | N
§(L1/L3 measurement delay and scheduling/measurement restrictions) | Y | N
§Measurement Performance | Y | N
FFS: UL spatial relation switching | Y | N
Y | Yes (shall to be defined)
N | No (No need to define)
L | Low priority (may be defined if time allows)

## Slide 5: Rel-18 NR-NTN-enh WID: RRM req for Ka band
Proposal 3: The definition of additional RRM requirements may be discussed at RAN#102
Proposal 4: Endorse proposal 1, 2, 3 of this tdoc and reflect them in the WID