## Slide 1
Views on the RIS channel model
RISTA
Aug. 16th ,2023

## Slide 2: Overview
      RIS(Reconfigurable intelligent surface):
        It has attracted the attention of academia and industry since it can flexibly manipulate the propagation of electromagnetic characteristics and lead to a smart radio environment (SRE). It’s typically in two-dimensional implementation of metamaterials, and naturally has the characteristics of low cost, low complexity and easy deployment.
        Typically, RIS can be used to enable:
        Extensive trials and demos have been conducted as listed in the published WP and News.
Case-1: Coverage improvement in Outdoor
Case-2: Coverage improvement in O2I
Case-3: Throughput improvement (e.g., S/M RIS)

## Slide 3: Detailed views for channel model
      The following aspects are considered to be prioritized in the study for RIS channel mode：
        Scenario:
          Indoor, UMi, UMa as defined in TR 38.901
            Note: The RIS is considered as additional entity in the scenario.
            Note: The deployment of RIS may vary and lead to different location of RIS, separation distance of Tx-RIS, RIS-UE link, which may lead to the near field use case for RIS.
          Frequency range: Both FR1 and FR2 should be considered.
        RIS type:
          Passive RIS: RIS without amplifiers integrated into their elements.
          Reflective RIS
            Additionally consider the Refractive/Transmissive RIS;
        RIS layout:
          2-D rectangular planar array with M*N RIS elements

## Slide 4: Detailed views for channel model (Continued)
        Modelling methodology:
          Stochastic model, Map-based hybrid model
        Feature:
          Large scale channel model
          Small scale channel model
            Note-1: The impact mainly refers to the generation of the RIS-related cluster(es)/ray(s).
            Note-2: The additional changes on the procedure defined in TR38.901 for channel realization are expected.
          RIS element pattern
            Note: The pattern of RIS element is defined per type, which can be applicable for different RIS implementation for one type;
          Additionally, the spatial domain features are considered:
            The near field effect, e.g., in O2I case or large array.
            Spatial non-stationary

## Slide 5
Thanks