## Slide 1: NavIC L1-band AGNSS support in NR & LTE
Source: Reliance Jio, ISRO, CEWiT, Nokia, Samsung, MediaTek, Bharti Airtel, Tejas Networks, CDoT, CDAC, Lekha wireless, HFCL, IIT Kanpur, IIT Bombay, IIT Jodhpur, IIT Delhi
3GPP TSG RAN Meeting #102 RP- 232776
Edinburgh, GB, December 11-15, 2023
Document for: Discussion & Agreement
Agenda Item: 9.1.2.5

## Slide 2: Introduction: NavIC
The first generation NavIC consists of three Geostationary Earth Orbit (GEO) and four Geo Synchronous Orbit (GSO) satellites. The NavIC satellites broadcast the signal in L5 band (1164.45–1188.45 MHz) and S band (2483.5–2500 MHz) with a carrier frequency of 1176.45 MHz (F1) and 2492.08 MHz (F2) respectively. The NavIC constellation is functional in the coverage region with the satellites, i.e. 1A, 1B, 1C, 1D, 1E, 1F, 1G and 1I in the orbit. All the satellites are visible in the service region for 24 hours.
India is now introducing second generation of NavIC satellite services. As compared to the first-generation satellite series, the second-generation satellite series includes L1 navigation band and incorporates an indigenously developed rubidium atomic lock. The inclusion of L1 navigation band improves the positioning, navigation, and timing services for civilian users, and facilitates better interoperability with other GNSS services.
The NavIC Signal-in-Space ICD (ISRO-IRNSS-ICD-SPS-L1-1.0) for SPS in L1 Frequency was published in August 2023 to the public to provide the essential information on the NavIC signal-in-space, to facilitate research & development and aid the commercial use of the NavIC signals for navigation-based applications.
NavIC L1 signal was optimized to enhance overall system performance on NavIC SPS which included introduction of a new ionospheric model, update to Ephemeris representation, update to transformation of TOWC among others.
With the advent of second generation of NavIC satellite services, it is important for Indian geography to prioritize the NavIC L1 A-GNSS support in Release 19. The existing A-GNSS assistance data configuration mechanism in LPP shall be extended to enable UE-based and UE-assisted A-GNSS support using NavIC L1.

## Slide 3: Background: NavIC L5 A-GNSS Support in 3GPP
1. NavIC A-GNSS support in LTE
In September 2019 at 3GPP RAN#85 plenary a new WI LCS_NAVIC was approved for LTE
LCS_NAVIC Core impacts under Working groups RAN2, RAN3 & Performance impact under RAN4 were classified.
LCS_NAVIC feature part of 3GPP LTE Release 16 in June 2020 RAN#88 plenary
2. NavIC A-GNSS support in NR
In March 2021 3GPP RAN#91e plenary meeting NAVIC L5 A-GNSS support with its RAN2, RAN3 & RAN4 impacts was agreed to be included to NR_pos_enh WI as part of NR Release 17
NR_pos_enh feature became part of 3GPP NR Release 17 in June 2022 RAN#96 plenary
In August 2023 RAN2 & RAN4 meetings respective NavIC L5 AGNSS support correction CRs were agreed under NR_pos_enh maintenance

## Slide 4: Challenges: NavIC commercialization
The existing infrastructure and user devices are predominantly designed to receive signals in the L1 band. Many commercially available GNSS receivers are optimized for L1 frequency, and their compatibility with NavIC, which lacked L1 support, became a crucial bottleneck.
The lack of L1 band support not only limits the interoperability of NavIC with other global navigation systems but also requires significant adjustments in the design and manufacturing of GNSS receivers.
Therefore, it is imperative to prioritize NavIC L1 A-GNSS support in User Equipment (UEs) for the unique geographical context of India.

## Slide 5: Summary from RAN#101 discussions
In the RAN#101 meeting, NavIC L1 band support was introduced and discussed under the positioning enhancement topic, and it received good industry support.
Outcome of session: (RP-232626)
Reliance Jio/Bharti Airtel/QC/Nokia/Ericsson/Bosch/CeWiT/IIT Kanpur/IIT Delhi/IIT Jodhpur/DOCOMO/Lekha: Support of NavIC for L1 navigation band should be supported. Support of NavIC is important for the Indian market. Impact is mainly on RAN2 and there is no impact on RAN1. This enhancement should be considered separately from other positioning enhancements.

## Slide 6: Release-19 Proposal
Observation:
  With the advent of second generation of NavIC satellite services, it is important for Indian geography to prioritize the NavIC L1 band A-GNSS support in Release 19.
  NavIC L1 signal implies introduction of a new ionospheric model for NavIC L1, update to Ephemeris representation, update to transformation of TOWC etc which could only be addressed under a new WI.
  Major RAN2 normative updates expected to be introduced in NR & LTE correspond to the common specification TS 37.355
  The RAN3 & RAN4 updates to be introduced in respective identical specifications.
Proposal:
A-GNSS support for NavIC SPS L1 band SPS in NR should be introduced in first phase of Release 19 as anRAN2 led independent small work item. The NavIC SPS L1 A-GNSS support introduction to LTE should be considered under the same WID given major impact to common specification.

## Slide 7: TU impact: NavIC L1 band AGNSS in NR
Impacted WG, existing TS/TR & TU required |  |  |  |  | 
WG | TS/TR No. | Description of change | Target completion plenary# | Remarks | TU
RAN2 | 38.305 | General description and ICD reference about the support for NavIC L1 will be added in the stage2 specification for positioning | TSG#105 | Core part | 0.5
RAN2 | 37.355 | Necessary NavIC L1 assistance data information will be introduced in the stage 3 spec based on the existing GNSS framework. | TSG#105 | Core part (Common NR/LTE spec) | 
RAN2 | 38.331 | Inclusion of positioning SIBs for NavIC L1 to message definition IEs | TSG#105 | Core part | 
RAN3 | 38.455 | Introduction of NavIC L1 assistance data elements, Update to broadcast of assistance data mapping of respective positioning SIBs to assistance NavIC data element | TSG#105 | Core part | 0.25
RAN4 | 38.171 | Specify UE performance requirements for support of NavIC L1 for NR. | TSG#105 | Performance part | 0.5

## Slide 8: Normative work: NavIC L1 band AGNSS in LTE
Impacted WG, existing TS/TR & TU required |  |  |  |  | 
WG | TS/TR No. | Description of change | Target completion plenary# | Remarks | TU
RAN2 | 36.305 | General description and ICD reference about the support for NavIC L1 will be added in the stage2 specification for positioning | TSG#105 | Minor Core part | -
RAN2 | 37.355 | Necessary NavIC L1 assistance data information will be introduced in the stage 3 spec based on the existing GNSS framework. | TSG#105 | Major work Common NR LTE spec | 
RAN2 | 36.331 | Inclusion of positioning SIBs for NavIC L1 to message definition IEs | TSG#105 | Minor Core part | 
RAN3 | 36.455 | Introduction of NavIC L1 assistance data elements, Update to broadcast of assistance data mapping of respective positioning SIBs to assistance NavIC data element | TSG#105 | Identical spec in NR & LTE Core part | -
RAN4 | 36.171 | Specify UE performance requirements for support of NavIC L1 for NR. | TSG#105 | Identical spec in NR & LTE Performance part | -