## Slide 1: Study on AI/ML for mobility
Ericsson
3GPP TSG RAN#102
Edinburgh, UK
2023-12-11 - 2023-12-15
Agenda Item: 9.1.2.4
RP-232780

## Slide 2: AI/ML for Air Interface (Mobility) SI
References: RWS-230488, RP-231540, RP-232622
Potential objectives: possible down-scoping in RAN#102
  Type of mobility
    L3-based mobility and L1/L2-triggered mobility (LTM) are both considered
  HO optimization in Network side [/UE side], including
    Candidate/target cell prediction in L3-based mobility, or, candidate/target beam(s) and cell(s) prediction in LTM
  RRM measurement and event prediction, including
    Beam-level measurement prediction
    Cell-level measurement prediction, e.g., using intra-frequency measurement results to forecast the RRM measurement of inter-frequency/inter-RAT cells
    HO failure/RLF prediction
    Measurement events prediction
  LCM framework and others
    The conclusions in Rel-18 AI/ML study should be used as baseline
    Other impacts are further studied
  [UE RRM enhancement, RAN4]
  Note 1: no intention to change the existing framework for the mobility under connected mode
  Note 2: In the SID, target performance metrics and impacts should be clarified
  Note 3: Avoid overlap work with RAN3
From chairman’s input RP-232745

## Slide 3: Justification
Conventional handover (L3-based mobility) and L1/L2-triggered mobility (LTM) decisions are made by the gNB at least partly based on L1/L3 RRM measurements
  For example, in case of high-speed UE using FR2 or in dense deployment/urban area, there might be a quick fluctuation of cell/beam quality with a risk that the L1/L3 RRM measurement reported by the UE are not up-to-date. This might cause a RLF/HOF, possible throughput loss, ping-pong handover, etc.
Additionally, UE performs several intra- and inter-frequency measurements which contributes to power consumption and a reduction of the throughput, when measurement gaps are used (for inter-frequency measurements)
Rel-18 AI/ML study has shown that the usage of AI/ML predictions for beam management has benefits both to the network and the UE in terms of beam selection, UE processing, power savings, etc.
We expect that L3-based and LTM-based mobility might have benefits from using the AI/ML, as well
In Rel-19, it should be studied what are the benefit/gains of AI/ML aided L3/LTM-mobility

## Slide 4: Discussion on the potential objectives from chairman’s input RP-232745
On “possible down-scoping in RAN#102”
  We think a down-scoping of the activity is not needed, at least not at the SI phase. All the alternatives should be considered in order to have a clearer picture of the benefits in using AI/ML for mobility. If the outcome of the SI indicates that some alternatives do not give enough benefits, then they can be removed from the scope at the next phase (e.g. from the WI)
  However, if a down-scoping of the activity is agreed, then the SI should at least consider the usage of the temporal predictions in L3-based mobility, since this is the “basic” and more common scenario
  Note, we assume that CHO is not part of the scope, and we don’t think it should be added since the scope would be too big
On type of mobility
  We agree that both L3-based mobility and L1/L2-triggered mobility (LTM) should be considered in the SI
On “HO optimization in Network side [/UE side]”
  We think the HO optimization should be done in Network side only (i.e., NW receives the predictions from UE and based on predictions it selects the target cell). RAN WGs should consider existing mobility frameworks in this study and the study is not about specifying new mobility frameworks.

## Slide 5: Discussion on the potential objectives from chairman’s input RP-232745
On “beam level and cell level measurement prediction”
  We think that both beam level and cell level measurement prediction should be considered in the SI: beam level predictions are more relevant for LTM, while cell level predictions are more relevant for L3-based mobility. Regarding the types of predictions, we think that all three types of prediction (i.e., temporal/spatial/frequency) should be considered during the SI.
On “LCM framework and others”
  We agree to use the conclusions from Rel-18 AI/ML activity as baseline (e.g. the data collection framework, performance monitoring, functionality and model activation/deactivation/switching/fallback from Rel-18 can be reused, if applicable)

## Slide 6: Study on AI/ML for Air interface on Mobility Proposed objective
Study and evaluate potential benefits and gains of AI/ML aided mobility under connected mode, considering the following aspects:
Type of mobility:
  Network triggered L3-based mobility
  L1/L2-triggered mobility (LTM)
HO optimization in Network side including:
  Candidate/target beam(s) and cell(s) selection based on predictions received from UE, for L3-based mobility and LTM
Type of predictions:
  Temporal predictions
  Frequency predictions
  Spatial predictions
RRM measurement and event prediction, including
  Beam-level measurement prediction
  Cell-level measurement prediction
  HO failure/RLF prediction
  Measurement events prediction
The evaluation of the AI/ML aided mobility benefits should consider at least the following KPIs:
  Too early/too late/ping-pong HO
  UE Throughput
  RLF/HOF
The conclusions from Rel-18 AI/ML study should be used as baseline (e.g. data collection framework, performance monitoring, functionality and model activation/deactivation/switching/fallback from Rel-18 can be reused, if applicable)