## Slide 1: Views on Rel-19 SON/MDT scope
Qualcomm
Dec 11th to 15th, 2023
Edinburgh, Scotland
3GPP TSG RAN Meeting #102
RP-233023
Agenda Item: 9.1.3.2

## Slide 2: SON/MDT Enhancements WI
References: RWS-230488, RP-231540, RP-232624
Potential objectives:
  MRO enhancement for R18 mobility mechanisms, Lower layer triggered mobility (LTM), CHO with candidate SCGs, subsequent CPAC [RAN3, RAN2]:
    Specification of the inter-node information exchange, including possible enhancements to interfaces[RAN3];
    Identify and specify necessary UE reporting to enhance the mobility parameter tuning [RAN2]
  Only SON/MDT enhancements for intra NTN mobility, Network slicing and NW energy saving are for further consideration.
    Details of these aspects (e.g., spec changes, assessment of workload).
    No other new features are to be added
  For NW energy saving, Note: avoid duplication with AI for NG-RAN.
  R18 leftovers, FFS details, which can be decided based on further progress in RAN2/3 [RAN3, RAN2]
The 1st potential objective on “MRO enhancements for R18 mobility mechanisms” look stable and is agreeable to most companies and this can be part of Rel-19 SON/MDT WI
Other potential objectives and R18 leftovers need more clarification and that is the focus of this paper
From RAN Chair’s summary for RAN Rel-19 Package (RP-232745)

## Slide 3: SON/MDT enhancements for NTN
“SON/MDT enhancements for intra-NTN mobility” wording is not clear. whether it is to optimize failed mobility or successful mobility or both. Also, it is not clear whether it also applies to mobility in RRC_IDLE/RRC_INACTIVE (i.e., cell (re) selection) as well.
we think it is also important to optimize RACH and access issues in NTN (i.e., even scenarios without mobility) and to be able to distinguish SON/MDT reports collected over NTN and TN (so that the reports don’t get mixed leading to improper optimizations). Also, ANR might need enhancements because the neighbor relations are time and area dependent in case of NTN.
We therefore propose :
Proposal 1: Potential Rel-19 SON/MDT enhancements for NTN can include the following:
  MRO enhancements for intra-NTN mobility, including failed and successful mobility scenarios
  Optimize cell (re)selection in NTN (e.g., via logged MDT enhancements)
  Optimize access in NTN (e.g., via RA/CEF Report enhancements)
  Distinguishing SON/MDT reports collected over NTN and TN
  ANR enhancements for NTN (e.g., time dependent NCRT)

## Slide 4: SON/MDT enhancements for Network Slicing
The following features are part of Network slicing in 5G:
  Rel-15/Rel-16: Basic support for network slicing
  Rel-17: Slice-based cell reselection, Slice-based RACH configuration, Slice service continuity
  Rel-18: Partially Allowed NSSAI, Alternative NSSAI
Rel-18 SON/MDT already allows UE to indicate the used S-NSSAI and used NSAG in RA Report to optimize the slice-based RACH configuration
Proposal 2: Potential Rel-19 SON/MDT enhancements for network slicing can include:
  MRO enhancements for slice service continuity, including failed and successful mobility scenarios
  Optimize slice-based cell reselection (e.g., via logged MDT enhancements)
  Slice-specific measurements for observability purposes (e.g., via new immediate MDT enhancements or inclusion of slice related information in SON reports)

## Slide 5: SON/MDT enhancements for Network Energy Savings
The following techniques were standardized in Rel-18 Network Energy Savings (NES) WI
  Cell DTX/DRX
  NES based CHO
  Paging enhancements for RRC_INACTIVE UEs
  Inter-node beam activation
Most of the above NES techniques are quite basic and don’t have much scope for optimization. Considering NES feature was only introduced in Rel-18 and it is not yet clear which of the above techniques will be deployed, we propose to not consider SON/MDT enhancements for NES in Rel-19 (also considering other objectives would also take significant workload).
Proposal 3: There is no need to consider SON/MDT enhancements for Network Energy Savings (NES) in Rel-19

## Slide 6: Rel-18 “leftovers”
The following items were deprioritized from Rel-18 SON/MDT
  Successful HO Report (SHR) for inter-RAT HO from LTE to NR
  Optimizing redirection for voice fall back
  Optimizing SCG Failure in EN-DC, (NG)EN-DC and NE-DC
  Optimizing SDT
We think items #1-#3 are not critical to be optimized in NR as late as Rel-19 and also might have LTE impacts and therefore should be avoided.
We think item #4 (optimizing SDT) had decent interest among companies in Rel-18 but was deprioritized. We therefore propose the following:
Proposal 4: Add an objective “SON/MDT enhancements for SDT” as part of Rel-18 leftovers

## Slide 7: Summary of proposals
Proposal 1: Potential Rel-19 SON/MDT enhancements for NTN can include the following:
  MRO enhancements for intra-NTN mobility, including failed and successful mobility scenarios
  Optimize cell (re)selection in NTN (e.g., via logged MDT enhancements)
  Optimize access in NTN (e.g., via RA/CEF Report enhancements)
  Distinguishing SON/MDT reports collected over NTN and TN
  ANR enhancements for NTN (e.g., time dependent NCRT)
Proposal 2: Potential Rel-19 SON/MDT enhancements for network slicing can include:
  MRO enhancements for slice service continuity, including failed and successful mobility scenarios
  Slice-specific measurements for observability purposes (e.g., via new immediate MDT enhancements or inclusion of slice related information in SON reports)
  Optimize slice-based cell reselection (e.g., via logged MDT enhancements)
Proposal 3: There is no need to consider SON/MDT enhancements for Network Energy Savings (NES) in Rel-19
Proposal 4: Add an objective “SON/MDT enhancements for SDT” as part of Rel-18 leftovers

## Slide 8: Potential objectives for Rel-19 SON/MDT WID
MRO enhancement for R18 mobility mechanisms, Lower layer triggered mobility (LTM), CHO with candidate SCGs, subsequent CPAC [RAN3, RAN2]:
  Specification of the inter-node information exchange, including possible enhancements to interfaces[RAN3];
  Identify and specify necessary UE reporting to enhance the mobility parameter tuning [RAN2]
SON/MDT enhancements for NTN [RAN3, RAN2]:
  MRO enhancements for intra-NTN mobility, including failed and successful mobility scenarios
  Optimize cell (re)selection in NTN (e.g., via logged MDT enhancements)
  Optimize access in NTN (e.g., via RA/CEF Report enhancements)
  Distinguishing SON/MDT reports collected over NTN and TN
  ANR enhancements for NTN (e.g., time dependent NCRT)
SON/MDT enhancements for network slicing [RAN3, RAN2]:
  MRO enhancements for slice service continuity, including failed and successful mobility scenarios
  Optimize slice-based cell reselection (e.g., via logged MDT enhancements)
  Slice-specific measurements for observability purposes (e.g., via new immediate MDT enhancements or inclusion of slice related information in SON reports)
SON/MDT enhancements for SDT [RAN3, RAN2]
Only SON/MDT enhancements for intra NTN mobility, Network slicing and NW energy saving are for further consideration.
  Details of these aspects (e.g., spec changes, assessment of workload).
  No other new features are to be added
  For NW energy saving, Note: avoid duplication with AI for NG-RAN.
  R18 leftovers, FFS details, which can be decided based on further progress in RAN2/3 [RAN3, RAN2]