## Slide 1
Scope of SON/MDT Enhancements in Rel-19
Agenda: 9.1.3.2
Source: Samsung
Document for : Discussion and decision

## Slide 2
Baseline Objectives from RAN Chair
RAN chair recently shared his summary for RAN Rel-19 Package in RP-232745.
In general, we are supportive on the summary, and observe there are several discussion points, especially the yellow-highlighted parts.
  MRO enhancement for R18 mobility mechanisms, Lower layer triggered mobility (LTM), CHO with candidate SCGs, subsequent CPAC [RAN3, RAN2]:
    Specification of the inter-node information exchange, including possible enhancements to interfaces[RAN3];
    Identify and specify necessary UE reporting to enhance the mobility parameter tuning [RAN2]
  Only SON/MDT enhancements for intra NTN mobility, Network slicing and NW energy saving are for further consideration.
    Details of these aspects (e.g., spec changes, assessment of workload).
    No other new features are to be added
  For NW energy saving, Note: avoid duplication with AI for NG-RAN.
  R18 leftovers, FFS details, which can be decided based on further progress in RAN2/3 [RAN3, RAN2]

## Slide 3
Discussion Points and Proposals (1/2)
Regarding SON/MDT enhancements for intra NTN mobility, Network slicing and NW energy saving:
  NTN supports additional trigger conditions to execute CHO, e.g. timer based trigger, location based trigger. The optimization for the NTN mobility related can be considered in Rel-19 SON/MDT WI. We are fine to focus on intra NTN mobility.
  For Network energy saving, any necessary work can be done in the NES WI together with RAN1/RAN2. There is no need to have duplicated work.
  For Network slicing, the slicing configuration is left to implementation, we are not sure what’s the specification impact for SON/MDT. Since the Rel-19 WI already contains enough scope, we think network slicing can be discussed in the AI for NG-RAN SI/WI.
  Proposal 1: Include intra NTN mobility in the scope of Rel-19 SON/MDT WI.
  Proposal 2: Network energy saving can be done in the NES WI.
  Proposal 3: Network slicing can be discussed in the AI for NG-RAN SI/WI.

## Slide 4
Discussion Points and Proposals (2/2)
Regarding Rel-18 leftovers:
  On SHR, only intra-system inter-RAT HO from NR to LTE is supported in Rel-18. At RAN3#119 meeting, RAN3 agreed “RAN3 sees benefits to support inter-RAT SHR from LTE to NR for T304 trigger with no impact on LTE in Rel-18.” But the normative work cannot be finalized due to lack of time.
  On SPR, there are two leftover issues: SPR in case of HO with SN change and SPR for MR-DC.
  On MRO for SCG failure, RAN2 and RAN3 have focused on NR-DC in rel-18. MRO for MR-DC SCG failure is postponed.
  On RACH optimsation, RAN2 has done some work for RA-SDT optimization in Rel-18. But how to optimize the RA-SDT configuration parameters to avoid SDT failure or inefficient SDT transmission has not been discussed in RAN3.
  Proposal 4: Include Rel-18 leftovers including intra-system inter-RAT SHR from LTE to NR, SPR leftover scenarios and SPR for MR-DC, MRO for MR-DC SCG failure, RACH optimsation for RA-SDT in the scope of Rel-19 SON/MDT WI.

## Slide 5
Proposal
Potential objectives:
  MRO enhancement for R18 mobility mechanisms, Lower layer triggered mobility (LTM), CHO with candidate SCGs, subsequent CPAC [RAN3, RAN2]:
    Specification of the inter-node information exchange, including possible enhancements to interfaces[RAN3];
    Identify and specify necessary UE reporting to enhance the mobility parameter tuning [RAN2]
  Only SON/MDT enhancements for intra NTN mobility, Network slicing and NW energy saving are for further consideration.
    Details of these aspects (e.g., spec changes, assessment of workload).
    No other new features are to be added
  For NW energy saving, Note: avoid duplication with AI for NG-RAN.
  R18 leftovers, including:FFS details, which can be decided based on further progress in RAN2/3 [RAN3, RAN2]
      Intra-system inter-RAT SHR from LTE to NR
      SPR in case of HO with SN change, SPR for MR-DC
      MRO for MR-DC SCG failure
      RACH optimization: RA-SDT

## Slide 6
Thank you!