## Slide 1: Views on Rel-19 XR WI scope

## Slide 2: General view on potential objectives
Proposed potential objectives in Rel-19 package summary (RP-232745)
  Objective 1: Study and if justified, specify aspects related to multi-modality(intra-UE)/multi-QoS flow (intra-UE) (with coordination with SA2/SA4), and other aspects requiring coordination w/ SA initiated work as necessary (e.g., SA2/SA4 task list which may potential have RAN impact).
    Check in RAN#105
  Objective 2: Measurement Gaps / Scheduling restrictions: Specify enhancements for reducing the impact to capacity and impact to individual UEs with respect to scheduling restrictions for FR1 and FR2 inter-frequency RRM measurements with measurement gaps and FR2 intra-frequency measurements w/o measurement gaps. [RAN1, RAN2, RAN4].
  Objective 3: UTO-UCI: support multiple CG configuration.
  Objective 4: CQI/CSI link adaption enhancement.
    FFS exact scope: PDSCH reception based, Traffic related, Soft-HARQ.
    FFS CBG enh.
  Objective 5: Delay aware / Delay adaptive (remaining time) scheduling.
Although RAN2 is the leading WG for Rel-19 XR evolution, there are not enough RAN2-led topics and RAN1-led topics seems too many in the RAN chair’s summary for Rel-19 package.
  Three objectives (objective 2/3/4 ) are RAN1-led topic and one RAN2 related topic is checked in RAN#105.
Considering allocated TU for Rel-19 XR evolution, RAN1-led objectives would need to be reduced and more RAN2-led objectives should be included in Rel-19 XR WI.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Views on RAN2-led objectives
Potential scope for multi-modality/multi-flow
  Study and if justified, specify aspects related to multi-modality(intra-UE)/multi-QoS flow (intra-UE) (with coordination with SA2/SA4), and other aspects requiring coordination w/ SA initiated work as necessary (e.g., SA2/SA4 task list which may potential have RAN impact).
    Check in RAN#105
LGE is generally fine to wait till RAN#105 for this topic since if there is no clear definition/conclusion by SA2/SA4 for this topic, RAN2 discussion will be floated without conclusions.
However, nothing to do until RAN#105 is not productive and it is preferred to make RAN2 discuss other important XR traffic characteristic which is not fully considered in Rel-18 XR WI and this can be discussed in RAN2 without SA2/SA4 input during that time.
RAN2 specific objectives which can be discussed without SA2/SA4 input need to be included.

## Slide 4: Views on RAN2-led objectives
RLC AM enhancement for XR was proposed due to following reasons:
  RLC AM operation does not consider short delay budget of a packet.
  RLC AM never give up retransmission until successful transmission is confirmed or RLF is triggered.
UPIP enhancement was proposed due to following reasons:
  UE needs to perform UPIP for every packet and whole data in the packet at PDCP.
  Processing burden is too high at high data rate.
Even though this was discussed in offline discussion for Rel-19 UP enhancement at the last meeting, short delay budget and high data rate are important XR traffic characteristics and reducing packet loss and providing security protection are also important for XR services.
Power saving is critical since XR services consume more UE power than other services in order to satisfy tight QoS requirements, e.g., higher throughput and low latency.
  However, Rel-18 XR power saving enhancement is limited to handle non-integer periodicity and SFN wrap around problems in DRX operation.
Rel-18 XR power saving enhancements may not be sufficient to support multiple flows of one XR service, and it does not bring considerable power saving gain.
  Since only one XR flow is aligned with the DRX cycle which may cause the transmission delay for other XR flows. Especially it is inappropriate for multiple flows of a XR service.
It is essential to improve power saving gain for multiple flows of a XR service without transmission delay.

## Slide 5: Views on RAN2-led objectives
Potential scope for scheduling
  Delay aware / Delay adaptive (remaining time) scheduling.
For delay aware/adaptive scheduling, RAN2 discussed remaining time based enhancements in Rel-18 XR and finally delay status reporting (DSR) is introduced to report the amount of data having remaining time lower than a threshold.
However, even if the network allocates an UL grant to the UE based on the received DSR, data not reported by the DSR can be included first in the MAC PDU and all data reported by the DSR would not be transmitted in time to the network and not transmitted urgent data would be unnecessarily discarded.
Prioritized scheduling for data reported by the DSR should be considered as delay aware/adaptive scheduling to avoid unnecessary discard of urgent data.
Delay requirement is defined per QoS flow and multiple QoS flows are typical XR traffic characteristic, but this was not fully considered in Rel-18 XR and DSR would not be sufficient to satisfy delay requirement of each QoS flow among multiple QoS flows.
To enhance user experience for a XR service with multiple QoS flows, finer QoS flow handling may be needed and prioritized handling for the QoS flow with short delay budget would be important.
Prioritized scheduling for the QoS flow with short delay budget, e.g. scheduling via different LCH, should be considered as delay aware/adaptive scheduling.

## Slide 6: Views on RAN1-led objectives
Potential scope for RAN1 topic
  Objective 2: Measurement Gaps / Scheduling restrictions: Specify enhancements for reducing the impact to capacity and impact to individual UEs with respect to scheduling restrictions for FR1 and FR2 inter-frequency RRM measurements with measurement gaps and FR2 intra-frequency measurements w/o measurement gaps. [RAN1, RAN2, RAN4].
  Objective 3: UTO-UCI: support multiple CG configuration.
  Objective 4: CQI/CSI link adaption enhancement.
    FFS exact scope: PDSCH reception based, Traffic related, Soft-HARQ.
    FFS CBG enh.
Scheduling restriction due to RRM measurement may be critical in achieving required QoS of XR service, as RAN1 discussed in Rel-18 XR.
The current design of Rel-18 UTO-UCI may not be suitable to support multiple flows of one XR service and XR traffic that requires higher reliability.
  Since the current UTO-UCI is applicable only to single configuration, which causes redundant UCI multiplexing for a XR service that utilizes multiple CG configurations.
  Also, if the XR traffic requires repetitions for higher reliability, current UTO-UCI may not indicate occurrences of upcoming transport blocks since it indicates maximally 8 PUSCH occasions including repetitions.
For CQI/CSI link adaption enhancement, RAN1 has already extensively discussed in Rel-17 URLLC/IIoT
  However, RAN1 was unable to reach a consensus, since there were concerns about various obstacles to obtain the benefit and certain enhancements require specific UE implementation for the PDSCH decoding procedure.
UTO-UCI enhancement and scheduling restriction due to RRM measurement should be considered as Rel-19 XR Objectives.
  For UTO-UCI enhancement, it is necessary to consider supporting UTO-UCI bit mapping per repetition bundle.
Given allocated TU for Rel-19 XR enhancement, it may not be productive to discuss CQI/CSI link adaption enhancement again.

## Slide 7: Proposed work scope
Study and if justified, specify aspects related to multiple QoS flow (intra-UE), and other aspects requiring coordination with SA initiated work as necessary [RAN2, RAN3]
  Support multiple DRX configurations for multiple flows
Measurement Gaps / Scheduling restrictions [RAN1, RAN2, RAN4]
  Specify enhancements for reducing the impact to capacity with respect to scheduling restrictions due to RRM measurement
UTO-UCI enhancements [RAN1, RAN2]
  Support UTO-UCI applicable to multiple CG configurations
  Support UTO-UCI bit mapping per repetition bundle
Delay aware / Delay adaptive (remaining time) scheduling [RAN2]
  Support prioritized scheduling for data reported by the DSR
  Support prioritized scheduling for the QoS flow with short delay budget, e.g. scheduling via different LCH
Protocol enhancement for XR traffic with short delay budget and high data rate [RAN2]
  Specify RLC AM enhancement to support latency-sensitive data transfer
  Support partial UserPlane Integrity Protection (UPIP)