## Slide 1: Views on Ambient IoT for R19
Xiaomi
3GPP TSG RAN Meeting #102 RP-233138
Edinburgh, Scotland, December 11-15, 2023

## Slide 2: Brief conclusions from R18 RAN study
Use case | Topology
Grouping A: - Indoor - Outdoor - Indoor/outdoor | Topology 1: BS ↔ Ambient IoT device Topology 2: BS ↔ intermediate node ↔ Ambient IoT device Topology 3: BS ↔ assisting node ↔ Ambient IoT device ↔ BS Topology 4: UE ↔ Ambient IoT device
Device category | RAN design targets
- Device A: No energy storage, no independent signal generation/amplification, i.e. backscattering transmission. - Device B: Has energy storage, no independent signal generation, i.e. backscattering transmission. Use of stored energy can include amplification for reflected signals. - Device C: Has energy storage, has independent signal generation, i.e., active RF components for transmission. | - Device power consumption - Device complexity - Coverage - User experienced data rate - Maximum message size - Latency - Positioning accuracy - Connection/device density - Moving speed of device
Grouping B:
- Inventory
- Sensors
- Positioning
- Command
Observation 1: The high level study of Ambient IoT in RAN shows extensive use cases and commercial prospects.
Deployment scenarios:
1: Device indoors, BS indoors
2: Device indoors, BS outdoors
3: Device indoors, UE-based reader
4: Device outdoors, BS outdoors
5: Device outdoors, UE-based reader
Representative use cases:
- rUC1: Indoor inventory
- rUC2: Indoor sensors
- rUC3: Indoor positioning
- rUC4: Indoor command
- rUC5: Outdoor inventory
- rUC6: Outdoor sensors
- rUC7: Outdoor positioning
- rUC8: Outdoor command

## Slide 3: Deployment scenarios / Topologies
RAN SI concludes on use case grouping, representative use case and corresponding deployment scenarios, the prioritized deployment scenarios should be jointly considered with topologies
For the 4 topologies identified in RAN SI,
  Topology 4 is purely UE based which may not have an explicitly connection to the network. It may result in completely new component/designs to UE and it cannot exploit the benefit from core network which is a key differentiation feature between 3GPP and other standardization organizations.
  From ambient IoT device point of view, there may be no much difference between Topology 1 and 2. Topology 1 is a basic one and comparatively easy for specification and implementation.
  For Topology 2, the UE can be reader under network control and both RRC_CONNECTED UE and RRC_IDLE/INATIVE can be considered as reader .
  Topology 3 does not show clear benefit compared to Topology 2 but with more deployment complexity
It is preferred that Topology 1 and Topology 2(with UE as an intermediate node) are considered in Rel-19 WG study

## Slide 4: Energy source / carrier wave
As agreed in the TR 38.848,
There is only limited discussion on carrier wave for backscatter transmission as well as the energy sources for harvest in RAN discussion.
However, the assumption on carrier wave and energy source in a deployment scenario/topology largely impact the operation of ambient IoT device and the performance
The impact of carrier wave and energy sources should be studied in RAN WGs together with the assumed deployment scenarios/topologies
The following connectivity topologies for Ambient IoT networks and devices are defined for the purposes of the study. In all these topologies, the Ambient IoT device may be provided with a carrier wave from other node(s) either inside or outside the topology. The links in each topology may be bidirectional or unidirectional.

## Slide 5: Device types
3 categories of devices (i.e., Device A/B/C) are identified in RAN SI
  Device A relying on backscatter transmission without energy storage is basically targeting same market as RFID
    it is hard for Device A to be more competitive from complexity/cost aspect
    It needs further study if performance of Device A can be better than RFID assuming good control on the networking/interference
  Device B is also based on backscatter transmission, has the advantage of low complexity/cost (higher than RFID), better performance and larger coverage can be achieved.
    Device B can be a key advantage for ambient IoT over incumbent RFID
  Device C can do active transmission. It is possible to reuse more signals/procedures in NR, subject to the potential shortage of energy
Device A/B provides the larger benefit for energy saving and complexity reduction, hence should be prioritized if TU is limited

## Slide 6: Evaluations and assessment
Evaluation methodology and assumptions for both link level and system level simulations
  Link level can be prioritized if time budget is limited
Design targets evaluations, including coverage/ connection density/data rate and so on.
  Coverage assessment can be done by link level simulations.
  Some of the KPIs, e.g., connection density and user experienced data rate, can be more accurately evaluated by system level simulations, but link level simulation can also give a rough assessment.
Co-existence evaluation
  Co-existence evaluation for Ambient-IoT and NR system.
  Co-existence evaluation within Ambient-IoT system.
  Simplified system level evaluations.

## Slide 7: Physical layer related
Waveform, modulation and channel coding
  Refer to LP WUS, OOK and Manchester coding can be considered at least for network-> device link
  Other options can also be considered for device->network link.
Frame structure and numerology
  Unified design for multiple links
  Co-existing with NR channels
Physical layer signals, channels and multiple access.
  New signal/channel design to accommodate backscattering devices and the Ambient IoT use cases.
  Interference control to allow for high efficient multiple access.
Physical layer procedures
  Simplified initial access and mobility compared to NR
  More efficient scheduling compared to RFID, (H)ARQ and power control should also be studied .

## Slide 8: High layer related
Lightweight protocol stack
  Convenient data transmission procedure based on non-state transition and non-dedicated bearer
  Mobility and tracking of ambient IoT device.
  Identification and lifecycle management of ambient IoT device.
  UE reader selection and reselection in Topology 2 for RRC idle/inactive and/or and RRC connected UE.

## Slide 9: RAN3/4 related
Potential RAN-CN signaling and RAN architecture
  Based on RAN1/2 study and coordination from SA
Study on BS/UE/Device architecture and characteristics.
  Based on RAN1 study on waveform/modulation

## Slide 10: SI or WI in Rel-19 WGs
In general, two options to organize works in Rel-19 can be considered,
  Option 1: RAN WGs do limited scope SI first, followed by a WI in Rel-19
  Option 2: RAN WGs only do SI in Rel-19
Considering the emergent commercial requirement, Option 1 is preferred, with 12 month SI and then WI.

## Slide 11: Proposals for R19 SI
Proposal 1: It is preferred to have a 12 month SI for limited scope and then WI for ambient IoT in Rel-19.
Proposal 2: Based on RAN study, suggest RAN to consider the following objectives for R19 SI,
Identify evaluation methodology (including the use cases), assumptions and KPIs, including data rate/coverage/connection density/coexistence performance.
Study waveforms, modulation and channel coding for low power consumption for ambient IoT air interface.
Study L1 signals/channels design based on low power waveform.
(4) Study L1 procedures, including initial access and mobility, scheduling, (H)ARQ, power control, etc, for the following devices and topologies
Device categories: Device A, Device B.
Topologies: Topology 1, Topology 2(with UE as an intermediate node) .
Study impact of carrier wave / energy source.
(5) Study lightweight protocol stack，including convenient data transmission procedure, mobility and tracking, identification and lifecycle management, topology setting.
(6)Study Potential RAN-CN signaling and RAN architecture
(7)Study on BS/Intermediate UE/Device architecture and characteristics

## Slide 12: Thanks